# 1AC

## Plan

The United States Federal Government should obtain electricity from small modular reactors for military bases in the United States.

## adv

Contention 1 is the DoD—

#### Scenario one is power projection—

#### Domestic DoD bases are vulnerable due to connectivity to the civilian grid–only SMRs solve

Robitaille 12

(George, Department of Army Civilian, United States Army War College, “Small Modular Reactors: The Army’s Secure Source of Energy?” 21-03-2012, Strategy Research Project)

In recent years, the U.S Department of Defense (DoD) has identified a security issue at our installations related to the dependence on the civilian electrical grid. 1 The DoD depends on a steady source of electricity at military facilities to perform the functions that secure our nation. The flow of electricity into military facilities is controlled by a public grid system that is susceptible to being compromised because of the age of the infrastructure, damage from natural disasters and the potential for cyber attacks. Although most major functions at military installations employ diesel powered generators as temporary backup, the public grid may not be available to provide electricity when it is needed the most. The United States electrical infrastructure system is prone to failures and susceptible to terrorist attacks. 2 It is critical that the source of electricity for our installations is reliable and secure. In order to ensure that our military facilities possess a secure source of electricity, either the public system of electric generation and distribution is upgraded to increase its reliability as well as reducing its susceptibility to cyber attack or another source of electricity should be pursued. Although significant investments are being made to upgrade the electric grid, the current investment levels are not keeping up with the aging system. Small modular reactors (SMRs) are nuclear reactors that are about an order of magnitude smaller than traditional commercial reactor used in the United States. SMRs are capable of generating electricity and at the same time, they are not a significant contributor to global warming because of green house gas emissions. The DoD needs to look at small modular nuclear reactors (SMRs) to determine if they can provide a safe and secure source of electricity. Electrical Grid Susceptibility to Disruptions According to a recent report by the Defense Science Board, the DoD gets ninety nine percent of their electrical requirements from the civilian electric grid. 3 The electric grid, as it is currently configured and envisioned to operate for the foreseeable future, may not be reliable enough to ensure an uninterrupted flow of electricity for our critical military facilities given the influences of the aging infrastructure, its susceptibility to severe weather events, and the potential for cyber attacks. The DoD dependency on the grid is reflected in the $4.01 Billion spent on facilities energy in fiscal year 2010, the latest year which data was available. 4 The electricity used by military installations amounts to $3.76 billion. 5 As stated earlier, the DoD relies on the commercial grid to provide a secure source of energy to support the operations that ensure the security of our nation and it may not be available when we need it. The system could be taken down for extended periods of time by failure of aging components, acts of nature, or intentionally by cyber attacks. Aging Infrastructure. The U.S electric power grid is made up of independently owned power plants and transmission lines. The political and environmental resistance to building new electric generating power plants combined with the rise in consumption and aging infrastructure increases the potential for grid failure in the future. There are components in the U.S. electric grid that are over one hundred years old and some of the recent outages such as the 2006 New York blackout can be directly attributed to this out of date, aging infrastructure. 6 Many of the components of this system are at or exceeding their operational life and the general trend of the utility companies is to not replace power lines and other equipment until they fail. 7 The government led deregulation of the electric utility industry that started in the mid 1970s has contributed to a three decade long deterioration of the electric grid and an increased state of instability. Although significant investments are being made to upgrade the electric grid, the many years of prior neglect will require a considerable amount of time and funding to bring the aging infrastructure up to date. Furthermore, the current investment levels to upgrade the grid are not keeping up with the aging system. 8 In addition, upgrades to the digital infrastructure which were done to increase the systems efficiency and reliability, have actually made the system more susceptible to cyber attacks. 9 Because of the aging infrastructure and the impacts related to weather, the extent, as well as frequency of failures is expected to increase in the future. Adverse Weather. According to a 2008 grid reliability report by the Edison Electric Institute, sixty seven per cent of all power outages are related to weather. Specifically, lightning contributed six percent, while adverse weather provided thirty one percent and vegetation thirty percent (which was predominantly attributed to wind blowing vegetation into contact with utility lines) of the power outages. 10 In 1998 a falling tree limb damaged a transformer near the Bonneville Dam in Oregon, causing a cascade of related black-outs across eight western states. 11 In August of 2003 the lights went out in the biggest blackout in North America, plunging over fifty million people into darkness over eight states and two Canadian provinces. Most areas did not have power restored four or five days. In addition, drinking water had to be distributed by the National Guard when water pumping stations and/or purification processes failed. The estimated economic losses associated with this incident were about five billion dollars. Furthermore, this incident also affected the operations of twenty two nuclear plants in the United States and Canada. 12 In 2008, Hurricane Ike caused approximately seven and a half million customers to lose power in the United States from Texas to New York. 13 The electric grid suffered numerous power outages every year throughout the United States and the number of outages is expected to increase as the infrastructure ages without sufficient upgrades and weather-related impacts continue to become more frequent. Cyber Attacks. The civilian grid is made up of three unique electric networks which cover the East, West and Texas with approximately one hundred eighty seven thousand miles of power lines. There are several weaknesses in the electrical distribution infrastructure system that could compromise the flow of electricity to military facilities. The flow of energy in the network lines as well as the main distribution hubs has become totally dependent on computers and internet-based communications. Although the digital infrastructure makes the grid more efficient, it also makes it more susceptible to cyber attacks. Admiral Mr. Dennis C. Blair (ret.), the former Director of National Intelligence, testified before Congress that “the growing connectivity between information systems, the Internet, and other infrastructures creates opportunities for attackers to disrupt telecommunications, electrical power, energy pipelines, refineries, financial networks, and other critical infrastructures. 14 ” The Intelligence Community assesses that a number of nations already have the technical capability to conduct such attacks. 15 In the 2009 report, Annual Threat Assessment of the Intelligence Community for the Senate Armed Services Committee, Adm. Blair stated that “Threats to cyberspace pose one of the most serious economic and national security challenges of the 21st Century for the United States and our allies.”16 In addition, the report highlights a growing array of state and non-state actors that are targeting the U.S. critical infrastructure for the purpose of creating chaos that will subsequently produce detrimental effects on citizens, commerce, and government operations. These actors have the ability to compromise, steal, change, or completely destroy information through their detrimental activities on the internet. 17 In January 2008, US Central Intelligence Agency senior analyst Tom Donahue told a gathering of three hundred international security managers from electric, water, oil & gas, and other critical industry, that data was available from multiple regions outside the United States, which documents cyber intrusions into utilities. In at least one case (outside the U.S.), the disruption caused a power outage affecting multiple cities. Mr. Donahue did not specify who executed these attacks or why, but did state that all the intrusions were conducted via the Internet. 18 During the past twenty years, advances in computer technologies have permeated and advanced all aspects of our lives. Although the digital infrastructure is being increasingly merged with the power grid to make it more efficient and reliable, it also makes it more vulnerable to cyber attack. In October 2006, a foreign hacker invaded the Harrisburg, PA., water filtration system and planted malware. 19 In June 2008, the Hatch nuclear power plant in Georgia shut down for two days after an engineer loaded a software update for a business network that also rebooted the plant's power control system. In April 2009, The Wall Street Journal reported that cyber spies had infiltrated the U.S. electric grid and left behind software that could be used to disrupt the system. The hackers came from China, Russia and other nations and were on a “fishing expedition” to map out the system. 20 According to the secretary of Homeland Security, Janet Napolitano at an event on 28 October 2011, cyber–attacks have come close to compromising the country’s critical infrastructure on multiple occasions. 21 Furthermore, during FY11, the United States Computer Emergency Readiness Team took action on more than one hundred thousand incident reports by releasing more than five thousand actionable cyber security alerts and information products. 22 The interdependence of modern infrastructures and digital based systems makes any cyber attacks on the U.S. electric grid potentially significant. The December 2008 report by the Commission on Cyber Security for the forty fourth Presidency states the challenge plainly: “America’s failure to protect cyberspace is one of the most urgent national security problems facing the new administration”. 23 The susceptibility of the grid to being compromised has resulted in a significant amount of resources being allocated to ensuring the systems security. Although a substantial amount of resources are dedicated to protecting the nation’s infrastructure, it may not be enough to ensure the continuous flow of electricity to our critical military facilities. SMRs as they are currently envisioned may be able to provide a secure and independent alternative source of electricity in the event that the public grid is compromised. SMRs may also provide additional DoD benefit by supporting the recent government initiatives related to energy consumption and by circumventing the adverse ramifications associated with building coal or natural gas fired power plants on the environment.

#### Those communication breakdowns go nuclear and decimate military operations

Andres 11

Richard Andres, Professor of National Security Strategy at the National War College and a Senior Fellow and Energy and Environmental Security and Policy Chair in the Center for Strategic Research, Institute for National Strategic Studies, at the National Defense University, and Hanna Breetz, doctoral candidate in the Department of Political Science at The Massachusetts Institute of Technology, Small Nuclear Reactorsfor Military Installations:Capabilities, Costs, andTechnological Implications, www.ndu.edu/press/lib/pdf/StrForum/SF-262.pdf

The DOD interest in small reactors derives largely from problems with base and logistics vulnerability. Over the last few years, the Services have begun to reexamine virtually every aspect of how they generate and use energy with an eye toward cutting costs, decreasing carbon emissions, and reducing energy-related vulnerabilities. These actions have resulted in programs that have significantly reduced DOD energy consumption and greenhouse gas emissions at domestic bases. Despite strong efforts, however, two critical security issues have thus far proven resistant to existing solutions: bases’ vulnerability to civilian power outages, and the need to transport large quantities of fuel via convoys through hostile territory to forward locations. Each of these is explored below. Grid Vulnerability. DOD is unable to provide its bases with electricity when the civilian electrical grid is offline for an extended period of time. Currently, domestic military installations receive 99 percent of their electricity from the civilian power grid. As explained in a recent study from the Defense Science Board: DOD’s key problem with electricity is that critical missions, such as national strategic awareness and national command authorities, are almost entirely dependent on the national transmission grid . . . [which] is fragile, vulnerable, near its capacity limit, and outside of DOD control. In most cases, neither the grid nor on-base backup power provides sufficient reliability to ensure continuity of critical national priority functions and oversight of strategic missions in the face of a long term (several months) outage.7 The grid’s fragility was demonstrated during the 2003 Northeast blackout in which 50 million people in the United States and Canada lost power, some for up to a week, when one Ohio utility failed to properly trim trees. The blackout created cascading disruptions in sewage systems, gas station pumping, cellular communications, border check systems, and so forth, and demonstrated the interdependence of modern infrastructural systems.8 More recently, awareness has been growing that the grid is also vulnerable to purposive attacks. A report sponsored by the Department of Homeland Security suggests that a coordinated cyberattack on the grid could result in a third of the country losing power for a period of weeks or months.9 Cyberattacks on critical infrastructure are not well understood. It is not clear, for instance, whether existing terrorist groups might be able to develop the capability to conduct this type of attack. It is likely, however, that some nation-states either have or are working on developing the ability to take down the U.S. grid. In the event of a war with one of these states, it is possible, if not likely, that parts of the civilian grid would cease to function, taking with them military bases located in affected regions. Government and private organizations are currently working to secure the grid against attacks; however, it is not clear that they will be successful. Most military bases currently have backup power that allows them to function for a period of hours or, at most, a few days on their own. If power were not restored after this amount of time, the results could be disastrous. First, military assets taken offline by the crisis would not be available to help with disaster relief. Second, during an extended blackout, global military operations could be seriously compromised; this disruption would be particularly serious if the blackout was induced during major combat operations. During the Cold War, this type of event was far less likely because the United States and Soviet Union shared the common understanding that blinding an opponent with a grid blackout could escalate to nuclear war. America’s current opponents, however, may not share this fear or be deterred by this possibility. In 2008, the Defense Science Board stressed that DOD should mitigate the electrical grid’s vulnerabilities by turning military installations into “islands” of energy self-sufficiency. The department has made efforts to do so by promoting efficiency programs that lower power consumption on bases and by constructing renewable power generation facilities on selected bases. Unfortunately, these programs will not come close to reaching the goal of islanding the vast majority of bases. Even with massive investment in efficiency and renewables, most bases would not be able to function for more than a few days after the civilian grid went offline Unlike other alternative sources of energy, small reactors have the potential to solve DOD’s vulnerability to grid outages. Most bases have relatively light power demands when compared to civilian towns or cities. Small reactors could easily support bases’ power demands separate from the civilian grid during crises. In some cases, the reactors could be designed to produce enough power not only to supply the base, but also to provide critical services in surrounding towns during long-term outages. Strategically, islanding bases with small reactors has another benefit. One of the main reasons an enemy might be willing to risk reprisals by taking down the U.S. grid during a period of military hostilities would be to affect ongoing military operations. Without the lifeline of intelligence, communication, and logistics provided by U.S. domestic bases, American military operations would be compromised in almost any conceivable contingency. Making bases more resilient to civilian power outages would reduce the incentive for an opponent to attack the grid. An opponent might still attempt to take down the grid for the sake of disrupting civilian systems, but the powerful incentive to do so in order to win an ongoing battle or war would be greatly reduced.

#### And it makes the military ineffective–collapses hegemony.

CNA 9

Center for Naval Analyses Military Adviser Board, Chaired by General Charles Wald, USAF (Ret.) Former Deputy Commander, Headquarters U.S. European Command (USEUCOM), May 2009, Powering America’s Defense: Energy and the Risks to National Security, https://www.cna.org/sites/default/files/Powering%20Americas%20Defense.pdf

Our vulnerabilities from energy use are not limited to battlefields and forward operating bases; they also exist at home. The biggest impacts may be local, but can extend to locations and operations around the world. In August 2003, 50 million people living in the Northeast, Midwest, and Ontario were suddenly left in the dark when their electric power failed. More than 500 generating units at 265 power plants shut down—a quiet collapse cascading across the landscape. Most homes and businesses regained power within a day (though some plants took two weeks to regain full capacity), a quick restoration that was possible primarily because no significant equipment was damaged. Still, critical national security systems failed. U.S. border check systems were not fully operational, causing a severe backup of truck traffic on our northern boundary. There were related effects from the outage as well. Water and sewage plants shut down. Gas stations stopped working, and rail service was curtailed. Many cellular phone providers, radio stations, and television stations lost service—their backup power systems were insufficient. The blackout is estimated to have caused economic losses of $7 to $10 billion [55]. The trigger for this massive blackout was tragically simple: An Ohio utility had failed to properly trim trees near a power line. American utilities have experience responding to interruptions caused by extreme weather. Even after severe ice storms and hurricanes, power is most often restored within a few days. But the effects of a long-term power outage are unknown. Our ability to recover from a dedicated attack is also not known—except to say that a deliberate attack would require a different response. There have been numerous attacks on the operating systems of major critical infrastructure facilities, including power grids, around the world in recent years: • In one instance outside the U.S., a power outage was triggered that affected multiple cities; in other instances, hackers have extorted hundreds of millions of dollars out of their victims [57, 58]. • Foreign cyber spies are also a serious concern: U.S. Homeland Security and Intelligence officials revealed that Chinese and Russian spies have “penetrated the U.S. electrical grid” and left behind dormant but malicious software [59]. • In 2007, the discovery of what is now known as the “Aurora threat” revealed the possibility that sophisticated hackers could seriously dam age the grid by destroying mechanisms downstream from the initial point of attack. Aurora involves opening and quickly closing a high voltage circuit breaker, which can result in an out-of-synchronism condition that can physically damage rotating equipment connected to the power grid [60-63]. At military installations across the country, a myriad of critical systems must be operational 24 hours a day, 365 days a year. They receive and analyze data to keep us safe from threats, they provide direction and support to combat troops, and stay ready to provide relief and recovery services when natural disasters strike or when someone attempts to attack our homeland. These installations are almost completely dependent on commercial electrical power delivered through the national electrical grid. When the DSB studied the 2003 blackout and the condition of the grid, they concluded it is “fragile and vulnerable... placing critical military and homeland defense missions at unacceptable risk of extended outage”. As the resiliency of the grid continues to decline, it increases the potential for an expanded and/ or longer duration outage from natural events as well as deliberate attack. The DSB noted that the military’s backup power is inadequately sized for its missions and military bases cannot easily store sufficient fuel supplies to cope with a lengthy or widespread outage. An extended outage could jeopardize ongoing missions in far-flung battle spaces for a variety of reasons: • The American military’s logistics chains operate a just-in-time delivery system familiar to many global businesses. If an aircraft breaks down in Iraq, parts may be immediately shipped from a supply depot in the U.S. If the depot loses power, personnel there may not fill the order for days, increasing the risk to the troops in harm’s way. • Data collected in combat zones are often analyzed at data centers in the U.S. In many cases, the information helps battlefield commanders plan their next moves. If the data centers lose power, the next military move can be delayed, or taken without essential information. • The loss of electrical power affects refineries, ports, repair depots, and other commercial or military centers that help assure the readiness of American armed forces. When power is lost for lengthy periods, vulnerability to attack increases. President Obama, Congress, and major utilities, among others, are discussing an upgrade of the national electrical grid for a variety of reasons. We add our voice to this discussion with a singular perspective: we see that our national security is directly linked to the security and reliability of our system of energy production and delivery.

#### Hegemony solves nuclear war and de-escalates all conflict.

Barnett ‘11

(Thomas, Naval War College Warfare Analysis & Research professor, “The New Rules: Leadership Fatigue Puts U.S., and Globalization, at Crossroads,” http://www.worldpoliticsreview.com/articles/8099/the-new-rules-leadership-fatigue-puts-u-s-and-globalization-at-crossroads)

Let me be more blunt: As the guardian of globalization, the U.S. military has been the greatest force for peace the world has ever known. Had America been removed from the global dynamics that governed the 20th century, the mass murder never would have ended. Indeed, it's entirely conceivable there would now be no identifiable human civilization left, once nuclear weapons entered the killing equation. But the world did not keep sliding down that path of perpetual war. Instead, America stepped up and changed everything by ushering in our now-perpetual great-power peace. We introduced the international liberal trade order known as globalization and played loyal Leviathan over its spread. What resulted was the collapse of empires, an explosion of democracy, the persistent spread of human rights, the liberation of women, the doubling of life expectancy, a roughly 10-fold increase in adjusted global GDP and a profound and persistent reduction in battle deaths from state-based conflicts. That is what American "hubris" actually delivered. Please remember that the next time some TV pundit sells you the image of "unbridled" American military power as the cause of global disorder instead of its cure. With self-deprecation bordering on self-loathing, we now imagine a post-American world that is anything but. Just watch who scatters and who steps up as the Facebook revolutions erupt across the Arab world. While we might imagine ourselves the status quo power, we remain the world's most vigorously revisionist force. As for the sheer "evil" that is our military-industrial complex, again, let's examine what the world looked like before that establishment reared its ugly head. The last great period of global structural change was the first half of the 20th century, a period that saw a death toll of about 100 million across two world wars. That comes to an average of 2 million deaths a year in a world of approximately 2 billion souls. Today, with far more comprehensive worldwide reporting, researchers report an average of less than 100,000 battle deaths annually in a world fast approaching 7 billion people. Though admittedly crude, these calculations suggest a 90 percent absolute drop and a 99 percent relative drop in deaths due to war. We are clearly headed for a world order characterized by multipolarity, something the American-birthed system was designed to both encourage and accommodate. But given how things turned out the last time we collectively faced such a fluid structure, we would do well to keep U.S. power, in all of its forms, deeply embedded in the geometry to come.

#### Regardless of relative power, military operations solve all conflict.

Kagan and O’Hanlon 7

Frederick Kagan and Michael O’Hanlon, Fred’s a resident scholar at AEI, Michael is a senior fellow in foreign policy at Brookings, “The Case for Larger Ground Forces”, April 24, 2007, http://www.aei.org/files/2007/04/24/20070424_Kagan20070424.pdf

We live at a time when wars not only rage in nearly every region but threaten to erupt in many places where the current relative calm is tenuous. To view this as a strategic military challenge for the United States is not to espouse a specific theory of America’s role in the world or a certain political philosophy. Such an assessment flows directly from the basic bipartisan view of American foreign policy makers since World War II that overseas threats must be countered before they can directly threaten this country’s shores, that the basic stability of the international system is essential to American peace and prosperity, and that no country besides the United States is in a position to lead the way in countering major challenges to the global order. Let us highlight the threats and their consequences with a few concrete examples, emphasizing those that involve key strategic regions of the world such as the Persian Gulf and East Asia, or key potential threats to American security, such as the spread of nuclear weapons and the strengthening of the global Al Qaeda/jihadist movement. The Iranian government has rejected a series of international demands to halt its efforts at enriching uranium and submit to international inspections. What will happen if the US—or Israeli—government becomes convinced that Tehran is on the verge of fielding a nuclear weapon? North Korea, of course, has already done so, and the ripple effects are beginning to spread. Japan’s recent election to supreme power of a leader who has promised to rewrite that country’s constitution to support increased armed forces—and, possibly, even nuclear weapons— may well alter the delicate balance of fear in Northeast Asia fundamentally and rapidly. Also, in the background, at least for now, SinoTaiwanese tensions continue to flare, as do tensions between India and Pakistan, Pakistan and Afghanistan, Venezuela and the United States, and so on. Meanwhile, the world’s nonintervention in Darfur troubles consciences from Europe to America’s Bible Belt to its bastions of liberalism, yet with no serious international forces on offer, the bloodletting will probably, tragically, continue unabated. And as bad as things are in Iraq today, they could get worse. What would happen if the key Shiite figure, Ali al Sistani, were to die? If another major attack on the scale of the Golden Mosque bombing hit either side (or, perhaps, both sides at the same time)? Such deterioration might convince many Americans that the war there truly was lost—but the costs of reaching such a conclusion would be enormous. Afghanistan is somewhat more stable for the moment, although a major Taliban offensive appears to be in the offing. Sound US grand strategy must proceed from the recognition that, over the next few years and decades, the world is going to be a very unsettled and quite dangerous place, with Al Qaeda and its associated groups as a subset of a much larger set of worries. The only serious response to this international environment is to develop armed forces capable of protecting America’s vital interests throughout this dangerous time. Doing so requires a military capable of a wide range of missions—including not only deterrence of great power conflict in dealing with potential hotspots in Korea, the Taiwan Strait, and the Persian Gulf but also associated with a variety of Special Forces activities and stabilization operations. For today’s US military, which already excels at high technology and is increasingly focused on re-learning the lost art of counterinsurgency, this is first and foremost a question of finding the resources to field a large-enough standing Army and Marine Corps to handle personnel intensive missions such as the ones now under way in Iraq and Afghanistan.

#### Scenario two is Alaska—

#### DOD facilities in Alaska vulnerable to grid disruptions—climate and geography makes it inevitable

Warwick , 10

(Engineer & Researcher- Pacific Northwest National Laboratory, Renewable Resource Development on Department of Defense Bases in Alaska:  Challenges and Opportunities, September,  http://www.pnl.gov/main/publications/external/technical_reports/PNNL-19742.pdf)

Alaska Military Facilities There are seven major DOD facilities in Alaska, as follows (see Figure 1 for a map). Fort Richardson (FRA) is the major Army facility in the southern part of the state. It is in Anchorage adjacent to Elmendorf Air Force Base (AFB). There is another cluster of facilities in the north central part of the state near Fairbanks. This includes Fort Wainwright (FWA) on the eastern edge of Fairbanks and Eielson AFB (EAFB) approximately 26 miles southeast of Fairbanks. Roughly 100 miles further southeast of Fairbanks is Fort Greely (FGA) and the training ranges for Fort Wainwright. Facilities of the Ground Missile Defense (GMD) are located on the range as well. While support to Ground Missile Defense is provided by the Army, it is a facility of the Missile Defense Agency. Approximately mid-way between Fairbanks and Anchorage is the Clear Air Force Station (CAFS). The Base Realignment and Closure (BRAC) process resulted in Fort Wainwright having greater control over the lands at Fort Greely and joint-basing of Fort Richardson and Elmendorf AFB under the control of the Air Force as Joint Base Elmendorf-Richardson (JBER). As a result of this consolidation the focus of Army operations is now primarily Fort Wainwright, while the Air Force operates three major facilities. The Air Force facilities are under the Air Force Pacific and Space Commands. Each of the services, including the Navy, operates smaller facilities in remote areas that are either not interconnected to the Alaska power grid or are too small to be of concern for this study. Alaska Utility Infrastructure The electrical system in Alaska is primitive in comparison to that in the lower 48 states and the rest of the developed world because of the harsh climate, large land mass and sparse population. There are two major population centers in the state, Anchorage and Fairbanks, and a cluster of smaller towns scattered across the Kenai Peninsula (see Figure 2). All three areas are linked by a single transmission circuit that is about 600 miles long. It follows the major railroad and highway linking these areas and is therefore called the Railbelt transmission system. Power exchanges along the system are limited primarily as a consequence of the nature of electricity requirements in the state and the associated history of each utility. The climate in Alaska is so harsh that a power outage of any duration can be devastating. As a result, each utility has planned to be able to operate independently of all others. They also plan to have sufficient reserve generating capacity to be able to provide power even if multiple generators are inoperable. The end result is sufficient generating capability to offset the need for integrated operations, and therefore, the need for an extensive transmission system (see Figure 3, from Doyon Utilities). The major interconnected utilities are Golden Valley Electric Association (GVEA),  which serves the north central part of the state centered on Fairbanks. The Anchorage  area has two primary utilities, Anchorage Municipal Light and Power (ML&P) and  Chugach Electric Association (CEA). Matanuska Electric Association (MEA) provides  power to the northern suburbs of Anchorage.   The GVEA system in the north is connected to the three Anchorage area utilities by a  170-mile transmission line, the Alaska Intertie, owned by the Alaska Energy Authority,  which is a “public,” meaning state-owned, corporation of the Department of Commerce  (Alaska Energy Authority 1991). Access to the intertie is through an “intertie  agreement.” This is standard practice among utilities in regions where there is no  independent system operator (ISO) to collectively manage transmission access on behalf  of multiple utility owners. The California ISO (CAISO) is an example of an ISO. In this  case, Alaska Energy Authority (AEA) contracts with ML&P and GVEA to manage the  intertie. As noted previously, to complete the circuit between GVEA and the two  Anchorage utilities, transmission has to pass through the MEA system. AEA recently  constructed an extension to the intertie to bypass the MEA system and tie in to the CEA  system directly.   The intertie was initially envisioned as means to distribute power from a large  hydropower development project on the Susitna River. This development is north of the  Anchorage area and would require connections to both the south and the north to be  feasible. The generating capability from the Susitna project could equal the combined  generation of Alaska’s major utilities if fully developed. Like all large hydropower  projects, this one is controversial and expensive, and consequently has had an on-again,  off-again history. Interest in the project remains high, however, given the current  dependence on fossil fuel for generation and shrinking supplies of oil from the North  Slope and natural gas from the Cook Inlet near Anchorage (see Figure 4).   GVEA serves Forts Wainwright and Greely and Eielson AFB. Elmendorf AFB and Fort Richardson (JBER) are served by ML&P. Power flowing between GVEA and ML&P passes through the systems of MEA and CEA because Anchorage is located on the southern edge of Cook Inlet and MEA and CEA are on the northern and eastern edges, respectively. Clear AFS is not connected to any utility power grid. It is in the GVEA territory and could be interconnected by constructing a transmission line approximately 3-miles long. Clear AFS, Eielson AFB, Fort Wainwright, and Fort Greely have their own central plants that provide both heat and power. Therefore, they are self-sufficient and typically operate without grid power. The plants at Clear, Eielson, and Wainwright are coal-fired using low Btu content coal mined near Clear, roughly 100 miles southeast of Fort Wainwright. Coal is delivered by rail. Fort Greely and GMD have diesel-fired generation in place, however because of the cost, Fort Greely uses excess power generated at Fort Wainwright whenever it is available. Power from Wainwright is wheeled by GVEA under a standard service tariff. The wheeling service is somewhat expensive but doesn’t require GVEA customers on either end of the transaction to provide reliability reserves or ancillary services, which are typically required in wholesale wheeling transactions.

#### No defense applies—federal laws exclude Alaska from traditional grid-protection

Magnuson, 12

(September, Columnist-National Defense Magazine, Feds Fear Coordinated Physical, Cyber-Attacks on Electrical Grids,

http://www.nationaldefensemagazine.org/archive/2012/september/Pages/FedsFearCoordinatedPhysical,Cyber-AttacksonElectricalGrids.aspx)

Electrical grids in the United States are vulnerable to both cyber-attacks and space weather, federal officials have said. But an assault that combines the skills of a hacker with a physical attack on key parts of a grid’s infrastructure may result in hundreds of millions of U.S. homes and businesses losing electricity. “I am most concerned about coordinated physical and cyber-attacks intended to disable elements of the power grid or deny electricity to specific targets, such as government or business centers, military installations, or other infrastructures,” Gerry Cauley, president and CEO of the North American Electric Reliability Corp., said at a recent Senate hearing.  Scott Pugh, of the Department of Homeland Security’s interagency program office, said at an energy conference in April that there are maps — not available for public viewing — that “show you a handful of substations — six or so —  [where] you could take out those six substations and black out most of the U.S. east of the Mississippi, if you knew which six [they] were. And in many cases you could do it with a hunting rifle from a couple hundred yards away.” There are some 1,500 companies that generate electricity in the United States, and the hodgepodge of federal agencies that oversee them have limited statutory authorities to force them to protect themselves against attacks, the Senate Energy and Natural Resources Committee hearing revealed.  “Limitations in federal authority do not fully protect the grid against physical and cyberthreats,” Joseph McClelland, director of the office of reliability at the Federal Energy Regulatory Commission, said.   Legislation passed in 2005 gave the agency the authority to impose reliability standards on “bulk,” or large-scale, power systems. That law excludes local distribution facilities, federal installations located inside grids, and major cities such as New York. Hawaii and Alaska also don’t fall under the commission’s jurisdiction. Officials are concerned about two threats: electromagnetic pulses, which come from solar storms or weapons, and cyber-attacks, particularly on “smartgrids,” which it turns out, are not very “smart” when it comes to protecting against hackers. “No single security asset, technique, procedure or standard — even if strictly followed — will protect an entity from all potential cyberthreats,” said Gregory Wilshusen, director of information security issues at the Government Accountability Office. “The cybersecurity threat environment is constantly changing and our defenses must keep up.” However, in the case of smartgrids, utilities continue to employ them without the necessary safeguards, the GAO has found. There is a lack of security features consistently being integrated into smartgrids and the current regulatory environment makes it difficult to ensure that power companies are properly protecting them. Physical attacks against the grid can cause equal or greater destruction than cyber-attacks, McClelland said. An electromagnetic pulse, or EMP event, could seriously degrade or shut down large swaths of the nation. Depending on the attack, a significant part of the infrastructure could be “out of service for periods measured in months to a year or more,” he said. “The self-reporting requirements, the enforcement provisions under the existing standards are important,” he said. “But at the end of the day, if there’s no enforcement provisions, there’s no teeth behind the provisions.” The National Institute of Standards and Technology has guidelines for utilities to gird themselves from physical and cyber-attacks, but they do not address coordinated attacks, said Wilshusen. NIST “guidelines did not address an important element essential to securing smartgrid systems — the risk of attacks using both cyber and physical means.”

#### Alaskan bases vital to prevent Arctic conflict escalation

Schanz, 8

(Associate Editor-Airforce Magazine, “Strategic Alaska,” http://www.airforce-magazine.com/MagazineArchive/Pages/2008/November%202008/1108alaska.aspx)

Billy Mitchell saw its great potential in 1935, and now the rest of the world has finally caught on.

More than ever before, the Air Force is paying close attention to its force structure in Alaska. Indeed, a major rush of events in the High North has propelled the 49th state up to the top ranks of service thinking. A resurgent Russia has ramped up its long-range bomber flights nearby. A changing Arctic climate has uncorked a flurry of activity in the region as once inaccessible resources now seem ready for exploitation. Alaska’s strategic Arctic location is viewed as useful for missile defense, air defense, and force deployments to locations ranging from Europe to East Asia and beyond. And the military training space available to USAF there is huge and varied. For these and other reasons, the Air Force has started beefing up its forces in the state. A visitor there sees that the service has been sending its newest and most advanced equipment for Alaskan service, including brand-new F-22 fighters and C-17 transports. "From an airman’s perspective, [it’s] probably the most strategic location," said Lt. Gen. Dana T. Atkins, commander of Alaskan Command and Alaskan NORAD region. The state’s geographic location "makes it hugely of strategic import to the United States and really important in a global context." From Alaskan bases, the Air Force can gain quick access both to the Pacific and European Theaters. Transiting across the Arctic, forces could arrive in Europe faster than if flying from the East Coast of the US, Atkins pointed out. This responsive location has helped to push Alaska to the forefront of USAF’s investment queue. The reinvigoration of Russian bomber patrols over Arctic waters in August 2007 was an opening push of that country’s increasingly assertive power projection efforts. NORAD’s US and Canadian fighters have repeatedly intercepted Russian flights skirting Alaskan airspace. New F-22s at Elmendorf Air Force Base took center stage last fall when Raptors stepped in to fill the role of the temporarily grounded F-15 fleet to intercept Russian Tu-95 Bear bombers. The Air Sovereignty Mission Many of the Raptor pilots leveraged their F-15 backgrounds, and the scrambles led to the development of a new training plan for the air sovereignty mission, said Lt. Col. Orlando Sanchez, director of operations for the 525th Fighter Squadron at Elmendorf. While F-22s are no longer on alert, they may perform intercepts in the future. The commander of Russia’s Air Force, Col. Gen. Alexander Zelin, said in April the country will increase its strategic patrols to as many as 30 a month. "It’s been interesting in the last few years," said Gen. Carrol H. Chandler, chief of Pacific Air Forces, in September. "When I was ... Alaskan Command commander, we had one intercept in the time that I was there. The Russians have continued to put emphasis on long-range aviation; they’ve continued to put emphasis on presence in the Arctic. ... Those numbers have picked up considerably over the last three to four years." Chandler suspects that a "competition for resources" will continue, and perhaps intensify, in the Arctic. Last year, Russia publicized a submarine trip to the bottom of the seabed at the North Pole—where the crew deposited a titanium Russian flag, symbolically marking territory. The Canadians derided the expedition as a "stunt," with Prime Minister Stephen Harper making a trip to Canada’s Arctic region to unveil several major military investments, and following with a new defense strategy, outlining new capabilities in the North. Russia’s focus on Arctic operations is a part of the country’s push to assert its own interests over Siberia’s extended continental shelf—the largest and least explored so far of the world’s continental shelves, according to senior Russian military officials. Geologists believe major oil and gas deposits could potentially become available as the polar ice cap slowly recedes with warming temperatures—a fact that is the focus of increasing attention to the nations claiming Arctic waters. "I don’t see that abating anytime in the near future, and the Russians certainly have the resources at this point" to continue to push into the region, said Chandler. A Resurgent Russia While Russia’s Arctic bellicosity has been on the rise, commanders in the region say the moves have to be kept in perspective. "Is it Cold War games all over again? I don’t think so," said Brig. Gen. Thomas L. Tinsley, who led the 3rd Wing at Elmendorf until his death in July. The moves are not hollow, however, and represent Russia’s "desire to bring their Air Forces back up to the speed they were." Tinsley noted that Russia has doubled the fuel it allots to its strategic aviation forces in order to bring back lost training capability. "But you know we’re constantly testing each others’ intel ability, we’re constantly testing each others’ reaction ability, and that’s just part of it." A big issue in the mix is the filing of standard international flight plans by the Russians, Atkins said. If an aircraft approaches a nation’s sovereign boundary with a flight plan, things would be a lot less complicated, he said. The problem with the Russian long-range bomber missions is that "what we’ve witnessed ... is these flights occur without these flight plans." This is one of the goals of improved mil-to-mil relations with the Russian Far East Military District commanders, Atkins added. "It seems too simple to say that, but if they would just adhere to the protocols that we have all accepted, then I think a lot of the perceived tension will evaporate." The US Coast Guard cooperates closely with the Russians just across the Bering Strait on issues ranging from fishing to limiting piracy, Atkins said. This month a survival search and rescue exercise was to be conducted, and this past summer US forces participated in a homeland defense exercise where a simulated hijacking took place—with command and control elements in both Alaska and Russia simulating the tracking and handing off of the aircraft. Both Atkins and Gen. Victor E. Renuart Jr. at NORAD have been working to invite some of the Russian Far East Military District commanders to visit Alaska to continue building between the two militaries professional relationships—which haven’t always been as close as the Coast Guard’s. "I’m the new guy. I’m going to try to keep building that professional rapport," Atkins quipped. "It would be great to get a rapport like the [Coast Guard’s]. ... I’d like to achieve the same kind of professional tie." In addition to renewed tensions with Russia, increased air and maritime traffic is a growing concern at Alaskan Command. Climate conditions have revealed a host of new Arctic transnational issues.

#### Strengthening Alaskan bases the key internal link to stopping all-out Arctic war

Dowd, 11

(MA-Indiana University, Senior Fellow of the Fraser Institute, “The Big Chill: Energy Needs Fueling Tensions in the Arctic,” https://www.fraserinstitute.org/research-news/news/display.aspx?id=2147483979)

One reason a military presence will be necessary is the possibility of accidents caused by drilling and shipping. In addition, competition for Arctic resources could lead to confrontation. Adm. James Stavridis, who serves as NATO’s military commander, concedes that the Arctic could become “a zone of conflict” (UPI). To brace for that possibility and thwart Russia’s Arctic fait accompli, the United States, Canada, Denmark and Norway—all NATO members and Arctic nations—should follow the Cold War playbook: build up the assets needed to defend their interests, use those assets to deter aggression, and deal with Moscow from a posture of strength and unity. The challenge is to remain open to cooperation while bracing for worst-case scenarios. After all, Russia is not the Soviet Union. Even as Putin and his puppets make mischief, Moscow is open to making deals. Russia and Norway, for instance, recently resolved a long-running boundary dispute, paving the way for development in 67,000 square-miles of the Arctic. Moreover, the U.S., Russia, Canada, Denmark and Norway have agreed on Arctic search-and-rescue responsibilities (Cummins). In a world of increasingly integrated markets, we know there is much to gain from Arctic cooperation and much to lose from protracted military standoff. But we also know that dealing naively with Moscow carries a heavy cost—and that integration is a two-way street. “Russian leaders today yearn not for integration,” the Brookings Institution’s Robert Kagan concludes, “but for a return to a special Russian greatness.” In short, Russia is more interested in recreating the autarky of some bygone era than in the shared benefits of globalization. Framework for Partnership Dealing with Russia is about power. As Churchill once said of his Russian counterparts, “There is nothing they admire so much as strength, and there is nothing for which they have less respect than for weakness.” When the message is clear—or “hard and consistent,” to use Putin’s language—Russia will take a cooperative posture. When the message is unclear, Russia will take what it can get. Just consider Russia’s contrasting treatment of its neighbors: Moscow blusters about Poland and the Baltic states but keeps its hands off, largely because they are protected by the U.S.-NATO umbrella. Conversely, Russia bullies Ukraine, garrisons its troops—uninvited—in Moldova, and occupies Georgian territory. The common denominator of these unfortunate countries: They have no U.S. security guarantee. Russia should be given an opportunity to participate as a responsible partner in Arctic development. But if Russia continues to take Putin’s hard line, the U.S. and its allies are left with few other options than standing together or allowing Russia to divide and conquer. To avoid that, the allies may need to agree among themselves on lines of demarcation, transit routes and exploration rights—and then pool their resources to protect their shared interests. This will require investment in Arctic capabilities. For instance, the U.S. has only three polar icebreakers, two of which have exceeded their projected 30-year lifespan (O’Rourke). Russia can deploy 20 icebreakers.  “We have extremely limited Arctic response capabilities,” explains Adm. Robert Papp, USCG commandant. Noting that the Coast Guard has “the lead role in ensuring Arctic maritime safety, security and stewardship,” Papp urges Congress “to start building infrastructure up there” (Joling and Papp). Washington’s defense cuts will only exacerbate these gaps, especially as Russia’s oil-aided boom enables it to retool its armed forces. Investing just 1.1 percent of its GDP on defense, Canada faces even greater challenges in defending its Arctic interests. But if the allies can combine their Arctic capabilities—each filling a niche role—and agree on a common approach to Arctic security, the framework to put those capabilities into practice is arguably already in place. Jointly operated by the U.S. and Canada, NORAD could serve as the model for an Arctic security partnership. Just as NORAD defends North American airspace, an allied maritime arrangement under the NORAD rubric could provide for security in Arctic waters. It’s worth noting that maritime surveillance was added to NORAD’s responsibilities in 2006. And in 2011, the Pentagon shifted responsibility for most Arctic operations to Northern Command (NORTHCOM), headed up by the same person who commands NORAD (Elliot). Preparing Bracing for military eventualities in the Arctic is not armchair alarmism. In fact, Gen. Gene Renuart, former NORTHCOM commander, reported in 2008 that U.S. officials were beginning to explore ways to “posture NORAD…to provide the right kind of search and rescue, military response, if need be, and certainly security for whatever activities occur in the Arctic.” “In order to ensure a peaceful opening of the Arctic,” adds Adm. James Winnefeld, current NORTHCOM commander, “DOD must anticipate today the Arctic operations that will be expected of it tomorrow.” In other words, the goal in preparing for worst-case scenarios and shoring up allied resolve in the Arctic is not to trigger a military confrontation, but to prevent one.

#### Only US leadership can stop war

Borgerson, 8

(International Affairs Fellow at the Council on Foreign Relations and a former Lieutenant Commander in the U.S. Coast Guard, Foreign Affairs, March/April, Arctic Meltdown Subtitle: The Economic and Security Implications of Global Warming, Lexis)

Washington cannot afford to stand idly by. The Arctic region is not currently governed by any comprehensive multilateral norms and regulations because it was never expected to become a navigable waterway or a site for large-scale commercial development. Decisions made by Arctic powers in the coming years will therefore profoundly shape the future of the region for decades. Without U.S. leadership to help develop diplomatic solutions to competing claims and potential conflicts, the region could erupt in an armed mad dash for its resources.

#### Risk of conflict high—most recent evidence

Tassinari, 9/7

(Non-resident Senior Fellow at the German Marshall Fund and the Head of Foreign Policy and EU Studies at the Danish Institute for International Studies, “Avoiding a Scramble for the High North”, http://blog.gmfus.org/2012/09/07/avoiding-a-scramble-for-the-high-north/http://blog.gmfus.org/2012/09/07/avoiding-a-scramble-for-the-high-north/)

BERLIN - The geopolitics of the Arctic are stuck in a paradox: The more regional players restate the importance of international cooperation, the more some pundits and policymakers seem to conclude that the Arctic risks descending into competition and even conflict. The world is awakening to the growing strategic importance of the High North. As the Arctic ice melts due to global warming, it opens up new opportunities, from shorter shipping lanes to newly accessible oil and gas reserves; respectively, about 13 percent and 30 percent of the world’s undiscovered resources are in the Arctic, according to the U.S. Geological Survey. These discoveries are usually followed by declarations of the littoral nations to the effect that any potential disagreements over them will be resolved peacefully. However, beneath expressions of goodwill, the Arctic debate is often characterized by a sense of urgency, and even forms of alarmism. In recent years, instances of growing securitization of the Arctic have abounded. Back in 2008, a paper by Javier Solana, then the EU’s foreign policy’s chief, and the European Commission warned about “potential conflict over resources in Polar regions” as they become exploitable due to melting ice. In 2010, NATO’s supreme allied commander in Europe, Adm. James Stavridis, argued that “for now, the disputes in the North have been dealt with peacefully, but climate change could alter the equilibrium.” Then there are actions that speak louder than prepared speeches — from the famous August 2007 expedition that planted a Russian flag on the North Pole’s seabed to the annual summer military exercises carried out by Canada to assert its sovereignty in the North. Although the Russian stunt was most likely aimed at nationalist domestic audiences, some observers view these exercises as the expressions of competing national interests. As the scholar Scott Borgerson ominously put it: “The Arctic powers are fast approaching diplomatic gridlock, and that could eventually lead to the sort of armed brinkmanship that plagues other territories.” The geopolitical constellation in and around the region provides a ready justification for such an assessment.  While no-one really imagines the United States, Canada, Norway, and Denmark fighting over the Arctic, some of their politicians have occasionally framed rhetoric in more peppered terms than one might expect. Russia, the fifth Arctic littoral nation, typically treads a fine line between declarations of cooperation and an innate instinct for great-power competition. Add to that the EU, which is seeking to carve its own role, and Asia’s giants, above all China, for which the opening of the Northeast passage may reduce sailing distance with Europe by some 40 percent, and it is not hard to conjure up the prospect of an Arctic race building up.

#### Best scholarship proves our impact

Murray 12

(Professor of Political Science @ Alberta, “Arctic politics in the emerging multipolar system: challenges and consequences,” The Polar Journal, 2.1)

It is no overstatement to say that the end of the Cold War was one of the most important events in recent world history. Scholars from many areas of study have used the fall of the Soviet Union as a starting point to explain shifts in security, globalization, humanitarianism and institutional integration, all of which played important roles in world affairs in the immediate post-Cold War era. Since 1991, explanatory models for international and global politics have broadened their scope to include variables such as individual preferences, capitalist oppression, ideational construction, environmentalism, gender and sexual politics, and discursive power to levels previously unforeseen throughout the Cold War years. As such, we now see the world as a far more complex and nefarious arena in which power and dominance are exercised each day. At the systemic level, the fall of the Soviet Union equated to nothing short of a monumental shift in the way states would make foreign and defence strategy. For 50 years, the bipolar system was dominated by two superpowers constantly competing and building arms in an effort to balance one another. The end of the Cold War signalled a major shift in systemic arrangement, as the system went from being bipolar to the world entering what was often referred to as the “unipolar moment.”1 The era of unipolarity and American hegemony in the international system has been marked by stability in an interstate sense, and the realignment of various spheres of influence in the wake of the Soviet Union’s demise. Far from being just a theoretical notion, the unipolar moment has also provided states with an environment in which to pursue their national self-interest where the likelihood of conflict is decreased and great power security competition has been minimized.2 As such, new areas of foreign affairs and defence strategy have become far more important than they could have been throughout the bipolar constrained Cold War years. One of the most notable examples in this regard has been the increased desire for territorial protection and extension in the Arctic region. In an era of state preoccupation with humanitarianism, terrorism and economic recession, it is being suggested by some observers that the Arctic has become the primary stage through which states, both great and minor in power, can pursue their self-interest in a way that combines soft power cooperation through bodies of governance with hard power and military build-up. As things presently stand, there are a variety of nations and institutions all seek- ing to claim governing authority over different parts of the circumpolar region. Nations making claims to parts of the Arctic Ocean or other northern waters include Canada, Russia, the United States, Norway, Iceland and Denmark/Greenland. On the institutional side, Arctic governance has been debated and defined by bodies such as the United Nations, the European Union, the United Nations Convention on the Law of the Sea (UNCLOS) and the Arctic Council.3 To date, no clear resolution to competing claims is in sight, and in some cases the situation is on the verge of becoming far more competitive as nations such as Russia have resorted to asserting possible military solutions to contested Arctic issues to bolster their declarations. It is important to note the increased levels of interest over Arctic relations between states, but, on this point, little attention has been given to the influence of the international system over this situation. If the unipolar moment has been defined as an era of relative stability and diplomatic coexistence, and tensions in the Arctic are already on the rise, what is to happen when the multipolar system finally emerges in the near future? Since 2005, the status of the United States as systemic hegemon has been in decline due to economic, military and political strains placed on American power capabilities throughout the Bush era and beyond. This decrease in relative power preponderance has been even further exacerbated by the economic recession starting in 2008 and the nation’s inability to stabilize its markets. As such, the predictions of those like Christopher Layne and John Mearsheimer are on the verge of coming to fruition, in that the unipolar moment is about to end.4 New great powers are rising, the United States is no longer able to prevent these nations from balancing their power, and the once obvious prevalence of American power is far murkier than it was a decade ago. As the multipolar era becomes increasingly likely, one must ponder the effects this shift might have on state foreign and defence strategy- making, especially towards the Arctic region. To date, though its relative power position has declined significantly in recent years, the United States remains the hegemon of the international system, but it is contended here that such status is soon to evaporate. In this context, this article argues that the emergence of a multipolar systemic arrangement is very likely to increase security competition in the system as a whole, and the Arctic will be at the epicentre of such conflict. To lend support to this hypothesis, an examination of the impending shift from unipolarity to multipolarity will be made, as will an account of current security dynamics in the circumpolar region. The article concludes with a stark warning that without some kind of real action towards settling competing Arctic claims, it will be left to states to secure their own territorial assertions through hard power and forceful means. The system is unipolar ... for now In order to evaluate the polarity of the international system in a given historical period, one must identify the hierarchy of power in terms of the number of super or great powers dominating international outcomes. Counting great or super powers can be somewhat difficult in contemporary international relations, as scholars have begun to expand the notions of power and capabilities, but the clearest guideline for being able to identify great powers is through determining capabilities. The reason it is essential to understand the great powers in international relations is that they, above all other states, institutions, non-state actors and ideational forces, are responsible for the daily conduct of behaviour in the international system, and they have been historically accountable for substantial alterations to power distribution since the 1648 Peace of Westphalia. Measuring capabilities allows observers to explain which states are most likely to affect the behaviour of other states, to use force or violence; also, the number of great powers in a given era determines how stable or unstable the international system will be. Identifying great powers is literally done by evaluating each state’s capabilities in essential areas of political life that can maximize security or extend one’s power. When discussing the distribution of power across states, there is a clear hierarchy of capabilities among states that leads observers to classify these utility maximizing, rational actors as super, great, major, middle or minor powers in the international system. In terms of actual measurement, Kenneth Waltz argues: “Their rank depends on how they score on all of the following items: size of population and territory, resource endowment, economic capability, military strength, political stability and competence.”5 Once these various factors are taken into account, one can clearly determine the given polarity of the system at a given moment in history. Why is polarity important? According to structural realist theory, the number of great powers in the system determines how conflictual, violent or stable international politics will be. While the overall structure of the system remains anarchic, meaning a clear absence of a governing authority above states that can control their actions, there can be consequential variations within the anarchic structure that can impact how states will evaluate their foreign and defence policy strategies and affect their overall behaviour. Waltz claims that “ ‘consequential’ variations in number are changes of number that lead to different expectations about the effect of structure on units.”6 There are three types of structure within the system that have been determined throughout the history of the modern state system – unipolarity, bipolarity and multipolarity. The consequential variations described by Waltz take place when great powers either rise or fall, and induce shifts from one type of polarity to another. The rise and fall of great powers is perhaps the most important explanatory aspect of international politics because it is these states that “inherently possess some offensive military capability, which gives them the wherewithal to hurt and possibly destroy each other.”7 Though the primary motivation for all states is security maximization, great powers become the most important actors because while they are capable of defending themselves, they also have the ability to extend their sphere of influence in offensive posturing. It is in this context that the polarity of the system becomes even more vital, in that the more great powers there are, the greater likelihood of violence and conflict there is. In each systemic arrangement, the abilities of great powers to pursue their ultimate goal, which is hegemony, dictates whether foreign and defence policy strategies will be overtly defensive or potentially offensive. All states are like-units, in that they all strive for survival by making rational calculations about how to best pursue their interests in an anarchic system. Of course, strategies of states will differ greatly based on the distribution of power, meaning that great powers are able to pursue their goals more freely than minor powers because they can operate without allies or institutions in achieving their goals. Lesser powers, however, typically try to increase their power position in world affairs through various alliance blocs and institutional binding. In doing so, it is hoped that middle and minor powers are able to guarantee their survival by aligning themselves with powers larger than themselves. Given the arrangement of the system, the number of alliances or blocs of power will differ, which also contributes to just how stable or violent the system will be. Conflict, or the possibility of it, is a constant problem in international relations due to the anarchic structure of the international system. Anarchy, by its definition, denotes a lack of overarching authority and thus states, especially the most powerful states, are able to behave as they would like, without any external body capable of controlling their actions. Robert Art and Robert Jervis aptly define anarchy by arguing: “States can make commitments and treaties, but no sovereign power ensures compliance and punished deviation. This – the absence of a supreme power – is what is meant by the anarchic environment of international politics.”8 In anarchy, just as in the state of nature or war prior to the establishment of civilized human society, there is no harmony and actors are left to their own inclinations to pursue their self-interest. The key elements of anarchy that precipitate conflict are the constant distrust of others’ motives, the assumption that other actors may not be as rational as oneself, and, as Waltz notes, “a state will use force to attain its goals if, after assessing the prospects for success, it values those goals more than it values the pleasures of peace.”9 The constant tensions between states, and the ability of great powers to more freely pursue their national interests, contributes to a system where security and survival are at a premium, and the polarity of the system matters to all states. By definition, bipolar systems are the most stable. According to Mearsheimer, this assumption is made based on three criteria: First, the number of conflict dyads is fewer, leaving fewer possibilities for war. Second, deterrence is easier, because imbalances of power are fewer and more easily averted. Third, the prospects for deterrence are greater because miscalculations of relative power and opponents’ resolve are fewer and less likely.10 By contrast, multipolar systems have a far greater probability of conflict, tension and distrust among states. War is far more likely in multipolar systems because major power dyads are more numerous, each posing the potential for conflict. Conflict could also erupt across dyads involving major and minor powers. Dyads between minor powers could also lead to war [...]. Wars in a multipolar world involving just minor powers or only one major power are not likely to be as devastating as a conflict between two major powers. However, local wars tend to widen and escalate. Hence there is always a chance that a small war will trigger a general conflict.11 While bipolarity is considered to be the most stable arrangement, and multipolarity the least stable, there is also the rare time when the system is unipolar in character. Put simply, unipolarity occurs when there is such a preponderance of power by one state that others are incapable of balancing against it. According to William Wohlforth, unipolarity is also a stable and peaceful arrangement: unipolarity favors the absence of war among the great powers and comparatively low levels of competition for prestige or security for two reasons: the leading state’s power advantage removes the problem of hegemonic rivalry from world politics, and it reduces the salience and stakes of balance-of-power politics among the major states.12 The status of the hegemonic power in a unipolar system allows for the expansion of its normative agenda, but also allows it to pacify international affairs because it lacks both a hegemonic rival and the effects of balance of power politics.13 As such, unipolar systems can be stable, depending on whom the hegemon is and what its vision for dominance might be. Since the end of World War II, only two types of polarity have been seen. Between 1945 and 1991, the system was bipolar, in that there were only two super- powers dominating the affairs of international politics. This bipolar arrangement was surprisingly stable and though smaller proxy wars erupted throughout the years of the Cold War, the relations between the two dominant powers, namely the United States and the Soviet Union, never came to a head. There are various explanations for why this was the case, but John Mearsheimer provides perhaps the most concise and accurate explanations as he contends that the absence of war in Europe and beyond throughout the Cold War can be attributed to three specific factors: the bipolar distribution of military power on the [European] Continent; the rough military equality between the two states comprising the two poles in Europe, the United States and the Soviet Union; and the fact that each superpower was armed with a large nuclear arsenal.14 At the conclusion of the Cold War, there was a clear and major shift in the distribution of power in the system, which translated into the unipolar moment. With the fall of the Soviet Union, the United States retained its superpower status and held a preponderance of power in virtually all areas of capabilities measurement. Christopher Layne contends that American hegemony is contingent upon two factors: First, the United States enjoys a commanding preeminence in both military and economic power. Second, since the Soviet Union’s disappearance, no other great power has emerged to challenge US preponderance. In this sense, US hegemony is the result of objective material conditions.15 Throughout the Clinton and early years of the Bush administrations, the role of the United States as systemic hegemon was virtually unquestioned, and it seemed as if American hegemony could last for a very long time. It was not until the latter years of the Bush administration that the waning of American hegemony began to become apparent. One of the key reasons the system remains unipolar is that there has yet to be a state that can balance against US power in either the hard or soft power senses. That said, the main reason for the decline in American hegemony has been a costly set of irrational and ill-advised foreign policy decisions, combined with years of economic overvaluation that eroded the hegemonic position of the world’s lone superpower.16 Both the intervention into Iraq, starting in 2003, and the fallout of the 2008 recession have served to substantially weaken the United States in both the hard and soft power contexts, and thus it is clear that a multipolar system is on the horizon. As Layne notes, “although a new geopolitical balance has yet to emerge, there is considerable evidence that other states have been engaging in balancing against the United States – including hard balancing.”17 The emerging great powers, especially China and Russia, will have a profound impact on the conduct of international relations in the years to come. Perhaps the most important area of security competition that has gone under- scrutinized from a systemic standpoint is the increased level of interest in the Arctic. Currently, the competing claims for the circumpolar region are mostly peaceful and focusing on diplomatic and legal battles, but recent trends suggest that non-violent strategy may not continue. As the era of American hegemony comes to an end, and a multipolar system begins to emerge, the impact on the Arctic region is likely to be profound due to the militaristic nature of state security strategies, unpredictability and a potential retreat from cooperation normally seen in multipolar structures. The Arctic in the unipolar moment One of the cornerstones of America’s unipolar moment has been the remarkable decline in interstate conflict. Since the fall of the Soviet Union in 1991, the international system has not been on the verge of any major war, nor have great powers aggressively pursued policies that would balance against American power in a way that would be taken seriously. According to many scholarly studies, the world since the end of the Cold War has become far more secure in the interstate sense, and security and defence policies of states are now preoccupied more with human- centric and intrastate variables than anything else. Though it is difficult to deny that the world has become more stable at the systemic level, the role of hard power and military capabilities did not disappear with the Soviet Union; instead, the use of militarism to achieve national goals in the unipolar moment greatly decreased as a direct result of the values and grand strategy of the United States. The impact of a unipolar systemic arrangement on state behaviour is best explained by the hegemonic stability theory.18 According to this theory, a unipolar structure is able to pacify the relations of states because there is recognition of the hegemon’s ability to control or intervene in conflicts that may threaten its power, or the order of the system. Wohlforth summarizes the basic precept of hegemonic stability theory by contending: The theory stipulates that especially powerful states (“hegemons”) foster international orders that are stable until differential growth in power produces a dissatisfied state with the capability to challenge the dominant state for leadership. The clearer and larger the concentration of power in the leading state, the more peaceful the international order associated with it will be [...] If the system is unipolar, the great power hierarchy should be much more stable than any hierarchy lodged within a system of more than one pole. Because unipolarity is based on a historically unprecedented concentration of power in the United States, a potentially important source of great power conflict – hegemonic rivalry – will be missing.19 It is essential to note two things about the status of the United States as systemic hegemon throughout the immediate post-Cold War era – first, that its preponderance of power in every area of capability measurement created a stable and less tense system in which states were able to interact; and second, that the United States’ time as hegemon has fostered the growth of multilateral institutions and agreements rather than a bullying type of unipolarity.20 From a systemic standpoint, it would seem that there is little reason to be concerned about military aggression, arms racing and distrustful competition in the modern system, but one vital concern to note is that much of the unipolar and hegeomic stability literature completely ignores the role of the Arctic in state security calculations. Throughout an era of institutional binding, regional integration, humanitarianism and soft power growth, the competition for the Arctic was following much of the same pattern, with states preferring to make their claims in institutional or legal settings. Yet, as the unipolar moment has started to decline, and multipolarity is on the horizon, the competition in the circumpolar region has taken on a very different tone. Competing claims over Arctic territories, such as the Northwest Passage, Beaufort Sea and other maritime boundaries, and the use of the region as a space for military exercises are by no means new and they have not come to the forefront of the strategic security agendas of states since the post-9/11 era. Rather, throughout the Cold War, the Arctic was a realm of constant supervision, not because either superpower wanted to develop the region, but more because of the mutual fear each side had of offensive attacks being launched over the pole. Even throughout the unipolar moment, the Arctic has been a space for sovereignty competition, but the nature of the competition had been mostly legal, institutional or soft power focused.21 Worth noting as well is the very complex nature of reasons for state interests in the Arctic. Mark Nuttall effectively summarizes the complexities of the high north as he claims: In the post-Cold War world [the Arctic] is seen as a natural scientific laboratory, under- stood as a homeland for indigenous peoples, a place of sovereignty conflicts, an emerging hydrocarbon province with which the world is coming to think of as one of the last major frontiers for oil and gas, and a region of dramatic environmental change.22 Though the intricacies of Arctic competition are intriguing to note, it is how states are strategically asserting their claims that is of particular importance. The start of America’s hegemonic decline has allowed states to revisit their approaches to the Arctic as nations jockey for position by balancing or rivalling American preferences. As a result, the nature of Arctic competition has incorporated both soft power and hard power elements. Further, the nature of militarism and hard power tension has increased due to the recent spending and strategic shifts by many Arctic states in recent years, including Canada, Norway, Sweden and Russia.23 The reasons for America’s decline are relatively unsurprising – military overextension in Afghanistan and Iraq; the lack of international support for American foreign policy objectives throughout the Bush era; the 2008 economic recession; and the utter dis- trust by most states, including close American allies, of the United States’ political objectives.24 The system remains unipolar, of course, but as stated above, the preponderance of power capabilities has substantially diminished, opening the door for others to balance and rival American power in the coming years. Coincidentally, it has also been the revelations of science in recent years that have also promoted a faster pace for those states making Arctic claims. The role of climate change and its impact over the Arctic has allowed for states to more freely move into the region and pursue strategies previously unavailable.25 According to Lotta Numminen, climate change has recently affected states’ perceptions of the possible economic opportunities in the Arctic in four ways: first, that the subsurface of the Arctic Ocean floor is assumed to contain substantial oil and gas reserves, to which there will be increased access; second, that melting waters will provide new waters for international fisheries; third, the increase in research strategies; and fourth, is the greater access to sea passages.26 One of the main reasons states see the Arctic region as such a lucrative area is the potential for increasing their respective economic and natural resource capabilities. Previously, the northern ice caps prevented states from entering most of the Arctic Ocean and surrounding areas, but as these environmental situations change, states have readily identified the high north as a priority in both their security and economic strategies. Among the main reasons the Arctic has not been more readily seen as a potential area for security competition and conflict is the interpretation that the United States has little or no interest in the circumpolar region at all. According to Stephen Brooks and William Wohlforth, American hegemony throughout the post-Cold War era was seen as passive, stable and enduring because of the lack of counter power being demonstrated in the system: Bounded by oceans to the east and west and weak, friendly powers to the north and south, the United States is both less vulnerable than previous aspiring hegemons and also less threatening to others. The main potential challengers to its unipolarity, meanwhile – China, Russia, Japan, and Germany – are in the opposite position. They can- not augment their military capabilities so as to balance the United States without simultaneously becoming an immediate threat to their neighbors. Politics, even international politics, is local. Although American power attracts a lot of attention globally, states are usually more concerned with their own neighborhoods than with the global equilibrium. Were any of the potential challengers to make a serious run at the United States, regional balancing efforts would almost certainly help contain them, as would the massive latent power capabilities of the United States, which could be mobilized as necessary to head off an emerging threat.27 Almost completely omitted from such interpretations, however, are America’s north- ern borders over Alaska and into the Arctic. Latitudinal thinking would seem to indicate that Brooks and Wohlforth are correct in terms of America’s interests in many areas of the globe, but this ignores what has been happening at the top of the world in the high north. It is not as if the United States has been ignorant of its own decline in power, especially regarding the Arctic. In 2009, the United States issued National Security Presidential Directive 66 and Homeland Security Presidential Directive 25 that deal exclusively with American Arctic policy. According to these directives, the alterations to national policies of other states regarding the Arctic compelled the United States to clearly outline the security and development strategies they would use to protect its Arctic interests. Among the first, and most clear, elements of the directives is the clear intention of the United States to defend their national security interests. According to Article III, subsection B 1 of the directives: The United States has broad and fundamental national security interests in the Arctic region and is prepared to operate either independently or in conjunction with other states to safeguard these interests. These interests include such matters as missile defense and early warning; deployment of sea and air systems for strategic sealift, strategic deterrence, maritime presence, and maritime security operations; and ensuring freedom of navigation and overflight.28 The contemporary changes to the international system as the era of American hegemony has begun to wane, the effects of climate change and greater access, and the increasingly militaristic strategies of most every Arctic state have led to a situation where tensions are at an all time high, and that legal or institutional processes are unlikely to resolve anything amicably. As the system continues its transition away from unipolarity, observers are left to ponder what might come next after an era of relative interstate stability. Multipolarity and the circumpolar In their 2002 article on the nature of United States primacy and the enduring aspects of American hegemony, Brooks and Wohlforth argue that the United States would have to act as a benevolent hegemon in order to prevent counterbalancing and to be able to build effective regimes worldwide. They argue: Magnanimity and restraint in the face of temptation are tenets of successful statecraft that have proved their worth from classical Greece onward. Standing taller than leading states of the past, the United States has unprecedented freedom to do as it pleases. It can play the game for itself alone or for the system as a whole; it can focus on small returns today or larger ones tomorrow. If the administration truly wants to be loved as well as feared, the policy answers are not hard to find.29 The problem with such analyses of American hegemony is that the Bush administration chose to ignore utterly such warnings and, rather than acting magnanimously, post-9/11 American foreign policy did precisely what it should not have. Pre-emption, coercion and irrational interventions, combined with a major economic recession, all serve to explain why American hegemony began to decline by 2005 in terms of both actual power levels and perceptions of legitimate hegemonic status.30 The clearest sign that American exceptionalism has been decreasing is the aggressive and regional balancing dynamics taking place between states in the Arctic region. Security strategy in the circumpolar region has altered dramatically since 2005, with more states showing interest, hard power spending increasing, and legal processes being coupled by at times overtly offensive strategy.31 Russia, Canada and a number of European states, especially Norway and Sweden, exemplify this line of argument about how sovereignty claims have become focused on traditional inter- state arms racing and militarism while soft power components, like governance structures and legal processes, continually evolve.32 As mentioned previously, even the United States has woken up to see that, as their hegemony declines, other states have begun to balance against them in the Arctic, thus provoking the 2009 Presidential Directives. Even so, Arctic interested nations have not yielded to American claims, nor has there been any evidence of America’s closest allies backing down in the face of its Arctic assertions, most clearly evidenced by Canada’s continued claims over the Northwest Passage.33 In the international relations canon, most observers point to either India or China as emerging great powers that are the most likely to counterbalance American power. The 2004 American National Intelligence Council report highlights this theory by stating: The likely emergence of China and India as new major global players – similar to the rise of Germany in the 19th century and the United States in the early 20th century – will transform the geopolitical landscape, with impacts potentially as dramatic as those of the previous two centuries. In the same way that commentators refer to the 1900s as the American Century, the early 21st century may be seen as the time when some in the developing world led by China and India came into their own.34 Both China and India have recently expressed their interest in Arctic affairs, but no power is as close to rivalling or challenging American power in hard power terms than Russia. This is especially true in the Arctic, as Russia’s Arctic policies have made its intentions towards asserting its control over territory it deems to be sovereign very clear. The role of the Arctic in Russian foreign policy cannot be understated. According to Russia’s 2008 Arctic policy document, the region is seen as the epicentre of Russia’s military and socio-economic development. The top two priorities for Russian Arctic interests are defined as follows: (a) In the sphere of socio-economic development – the expansion of the resource base of the Arctic Zone of the Russian Federation, in order to substantially satisfy Russia’s needs in hydrocarbon resources, hydro-biological resources, and other types of strategic raw materials; (b) In the sphere of military security, defense, and safekeeping of the state borders of the Russian Federation located in the Arctic Zone of the Russian Federation – the upkeep of a favorable operational regime in the Arctic Zone of the Russian Federation, including the maintenance of the required combat potential of military groupings under the Armed Forces of the Russian Federation, other troops, military formations and agencies in this region [...]35 In order to achieve these goals, the Russians have created a unique military brigade to be permanently posted in the Arctic, have placed a Russian Federation flag on the Arctic Ocean seabed, have conducted various missile tests, have sailed their nuclear submarines through contested waters and have openly challenged the abilities of other states to enforce their own claims. In response to Russian offensive posturing and the inability of the United States to dissuade security competition in the area, middle and minor powers have begun to use hard power as a means of trying to enforce their sovereignty. Perhaps the best example here is Canada, whose military capabilities are extremely weak, but strong rhetoric and a drastically increased level of high-north military spending since 2006 seems to indicate that the Canadian government cannot rely on its American alliances to protect its interests, and that posturing by states like Russia or even Denmark clearly threaten Canada’s national interests. As Norway, Sweden and Denmark have begun to put an emphasis on hard power capabilities to extend or defend northern claims, Canada has done the same. Worth noting as well in the Canadian context is that, while great powers like Russia and the United States can easily defeat any middle or minor power, Canada’s capabilities are being either rivalled or surpassed by European states like Norway.36 Canada’s realization of the evolving security and environmental climate in the Arctic has compelled changes to its domestic and foreign security policies, each seeking to assert Canadian sovereignty over areas of the Arctic, especially the Northwest Passage. One of the main components of now Prime Minister Harper’s 2005–06 campaign was to bolster Arctic security resources, as many Canadians have identified the region as an essential part of Canada’s national security and identity.37 Rob Huebert argues: The Harper government has increasingly recognized the significance of maintaining a strong presence in the Arctic and has vigorously begun to improve Canada’s northern abilities [...] The Harper government has also made a series of promises to consider- ably expand Canada’s northern capability [...] If these promises are implemented, Canada will have significantly improved its ability to control activity in its Arctic.38 In virtually any other area of the world, Canadian national security cannot be divorced from the United States, which is a partial explanation for why Canada has traditionally been considered a middle power since the end of World War II.39 Yet, since the start of American decline, the Canadian government has recognized that its fate in the Arctic will be its own, and not intrinsically tied to the protection of the United States, as the Americans have their own interests in the region and have shown a complete disregard for Canadian claims over the Northwest Passage and the Beaufort Sea. As the world moves towards multipolarity, it has become increasingly obvious that the Arctic region represents an area of increased security competition and a potentially conflictual region in the future. Multipolar systems are the most unstable, and history has shown these to produce military conflict due to the natural effects brought by a larger number of self-interested powers vying for power and security. Further, as new great powers begin to emerge, American strategic considerations will be spread so thin that they will be unable to prevent against their eventual loss of hegemony. The largest mistake being made at this time by international security scholars and policymakers is their normal obsession with China, India and latitudinal thinking. The next area of major war is not likely to be the Middle East, the Indian Ocean or the South China Sea, due to traditional security balancing, deterrence and economic interests in each of these areas. Multipolarity naturally brings the possibility of war. Mearsheimer contends that war is far more likely in multipolar systems for three reasons: First, there are more opportunities for war, because there are more potential conflict dyads in a multipolar system. Second, imbalances of power are more commonplace in a multipolar world, and thus great powers are more likely to have the capability to win a war, making deterrence more difficult and war more likely. Third, the potential for miscalculation is greater in multipolarity: states might think they have the capability to coerce or conquer another state when, in fact, they do not.40 Presently, there is little reason to believe that tension and strategic posturing will lead to the outbreak of war in the near future. That said, as America’s influence continues to wane, other states have shown their desire to take full advantage of the United States’ inability to control northern affairs. If the United States does lose its hegemony, which many commentators believe is inevitable, there will be at least four dyads in security calculations, with Russia, China and India entering the fray, and two of those states have Arctic borders and a historical legacy of conflict. Power imbalance in the Arctic is already apparent, with only Russia and the United States as great powers, while the other Arctic states are middle or minor powers with no hope of preventing a great power from doing as it pleases. Lastly, miscalculation is evident in the present context, as Sweden and Norway are both arming for possible Russian aggression, though Russia has shown little or no overtly aggressive tendencies towards Nordic nations. Unipolarity was not going to last forever, but as it fades the probability of northern conflict is ever increasing. The shift to hard power strategies, the effects of cli- mate change, and the decline of the United States all speak to the fact that multipolarity can increase levels of tension and mistrust, thus altering the currently stable nature of Arctic affairs. Efforts at Arctic governance through institutional binding or legal claims, as seen in the Arctic Council and UNCLOS, are able at present to mitigate the ongoing and ever increasing security competition in the high north, but as the system changes from unipolarity to multipolarity, constraining state behaviour becomes increasingly difficult. As such, observers must be mindful of the systemic variables at play when explaining and forecasting Arctic politics, as changes to the structure are very likely to translate into changes to state security strategies.

#### Goes nuclear

Wallace, 10

(Professor Emeritus at the University of British Columbia, March, “Ridding the Arctic of Nuclear Weapons A Task Long Overdue”, http://www.arcticsecurity.org/docs/arctic-nuclear-report-web.pdf)

The fact is, the Arctic is becoming a zone of increased military competition. Russian President Medvedev has announced the creation of a special military force to defend Arctic claims. Last year Russian General Vladimir Shamanov declared that Russian troops would step up training for Arctic combat, and that Russia’s submarine fleet would increase its “operational radius.” Recently, two Russian attack submarines were spotted off the U.S. east coast for the first time in 15 years. In January 2009, on the eve of Obama’s inauguration, President Bush issued a National Security Presidential Directive on Arctic Regional Policy. It affirmed as a priority the preservation of U.S. military vessel and aircraft mobility and transit throughout the Arctic, including the Northwest Passage, and foresaw greater capabilities to protect U.S. borders in the Arctic. The Bush administration’s disastrous eight years in office, particularly its decision to withdraw from the ABM treaty and deploy missile defence interceptors and a radar station in Eastern Europe, have greatly contributed to the instability we are seeing today, even though the Obama administration has scaled back the planned deployments. The Arctic has figured in this renewed interest in Cold War weapons systems, particularly the upgrading of the Thule Ballistic Missile Early Warning System radar in Northern Greenland for ballistic missile defence. The Canadian government, as well, has put forward new military capabilities to protect Canadian sovereignty claims in the Arctic, including proposed ice-capable ships, a northern military training base and a deep-water port. Earlier this year Denmark released an all-party defence position paper that suggests the country should create a dedicated Arctic military contingent that draws on army, navy and air force assets with shipbased helicopters able to drop troops anywhere. Danish fighter planes would be tasked to patrol Greenlandic airspace. Last year Norway chose to buy 48 Lockheed Martin F-35 fighter jets, partly because of their suitability for Arctic patrols. In March, that country held a major Arctic military practice involving 7,000 soldiers from 13 countries in which a fictional country called Northland seized offshore oil rigs. The manoeuvres prompted a protest from Russia – which objected again in June after Sweden held its largest northern military exercise since the end of the Second World War. About 12,000 troops, 50 aircraft and several warships were involved. Jayantha Dhanapala, President of Pugwash and former UN under-secretary for disarmament affairs, summarized the situation bluntly: “From those in the international peace and security sector, deep concerns are being expressed over the fact that two nuclear weapon states – the United States and the Russian Federation, which together own 95 per cent of the nuclear weapons in the world – converge on the Arctic and have competing claims. These claims, together with those of other allied NATO countries – Canada, Denmark, Iceland, and Norway – could, if unresolved, lead to conflict escalating into the threat or use of nuclear weapons.” Many will no doubt argue that this is excessively alarmist, but no circumstance in which nuclear powers find themselves in military confrontation can be taken lightly. The current geo-political threat level is nebulous and low – for now, according to Rob Huebert of the University of Calgary, “[the] issue is the uncertainty as Arctic states and non-Arctic states begin to recognize the geo-political/economic significance of the Arctic because of climate change.”

#### Extinction

Corcoran 9

(PhD, Senior Fellow @ Global Security, Frmr. Strategic Analyst at the US Army War College where he chaired studies for the Office of the Deputy Chief of Operations and member of the National Advisory Board for the Alsos Digital Library for Nuclear Issues, we win the qualification game, 4/21, http://sitrep.globalsecurity.org/articles/090421301-strategic-nuclear-targets.htm)

That brings us to Russia, our former main adversary, now a competitive partner and still a potential future adversary, particularly as relations have gradually soured in recent years. Russia is the only other nation with a formidable arsenal of some three thousand strategic weapons. Our opposing arsenals were built up in the period when Mutually Assured Destruction (MAD) was the underlying strategic concept -- each side deterred from striking the other by the prospect of assured retaliatory destruction. The situation became even madder as both sides worked to develop a capability to destroy the other's strike force with a crippling first strike. This resulted in further large increases in the sizes of the arsenals, as well as early warning systems and hair-trigger launch-on-warning alert procedures. The final result was an overall system in which each side could destroy the other in a matter of minutes. And it also raised another chilling specter, Nuclear Winter, in which the atmospheric dust raised from a major nuclear exchange would block sunlight for an extended period and essentially destroy human civilization globally. The collapse of the Soviet Union collapsed this threat, but did not eliminate it. US and Russian nuclear forces remained frozen in adversarial positions. The May 2002 Moscow Treaty began to address this legacy and is leading to a reduction in strategic nuclear forces down to levels of about two thousand on each side by 2012. These levels are still sufficient to destroy not only both nations but also human civilization. It is hard to even construct scenarios where the use of even a few strategic nuclear weapons does not risk a total escalation. Strikes on Russian warning facilities or strike forces would almost certainly bring a wave of retaliatory strikes. Strikes on hardened command centers would be of questionable effectiveness and also risk total escalation. In addition, successful elimination of Russian leaders could greatly complicate any efforts to stop escalation short of a total nuclear exchange.

#### SMRs on Alaskan bases solve

Holdmann, 11

(Director of Alaska Center for Energy and Power-University of Alaska Fairbanks, “Small Scale Modular Nuclear Power: an option for Alaska,” http://www.uaf.edu/files/acep/Executive-Summary-3-2-11.pdf)

Executive Summary Alaska is home to some of the most abundant supplies of fossil fuels and renewable energy resources on the planet. While the Alaska treasury benefits financially from development of these resources for export, the supply of reliable, affordable energy to small and often isolated Alaska markets remains a challenge. These conditions result in energy prices for space heating and electricity that are volatile and expensive in many areas of the state. These high energy prices are a significant burden for Alaska residents and businesses and stifle economic development. Ways to address high energy prices are being deliberated, including the possible construction of one of several proposed natural gas pipeline projects, funding of individual projects in rural communities with access to developable resources, and consideration of a large-scale hydroelectric project to serve the Railbelt. Another possible source of energy is nuclear power. Why discuss the nuclear option? With Alaska’s abundant energy resources, this form of energy might not seem needed. However, Alaska’s resources are not equitably distributed geographically, with some areas located near energy sources (for example, the gas fields of Cook Inlet that supply energy for Anchorage), and many other areas less fortunate. In particular, communities in rural Alaska face very high energy prices due to reliance on imported diesel fuel, and many do not have access to developable local resources that can appreciably reduce this dependence. To a lesser degree, the Fairbanks area also lacks low-cost, locally abundant energy resources. It is possible that the new small-scale modular nuclear power plants could lower the cost of energy in some of these locations. Alaska was not part of the first wave of nuclear power development in the U.S., as the nation’s existing commercial nuclear industry is comprised of 1000 MW reactors that are too large for any Alaska applications. However, as part of a new generation of nuclear power plants worldwide, small modular reactors (SMRs) are being developed that range in size from 10 MWe to 300 MWe. These SMRs would be manufactured in factories, allowing standardized design and fabrication, high quality control, shorter power facility construction times, and reduced finance charges during construction. In larger markets in the Lower 48, multiple SMR modules could be combined to form a single gigawatt-scale power plant, which would have several advantages over a single large reactor, including reduced downtime for maintenance and improved safety. These SMRs would also be appropriately sized for use in Alaska, making nuclear energy a viable option to consider. In addition to providing energy (heat and power) for rural communities and/or the Railbelt, other potential applications include providing energy to military bases, remote mining operations, and other industrial users

#### DoD procurement of SMR’s solves security and islands military bases.

Loudermilk 11

Micah J. Loudermilk, Research Associate for the Energy & Environmental Security Policy program with the Institute for National Strategic Studies at National Defense University, 5/31/11, Small Nuclear Reactors and US Energy Security: Concepts, Capabilities, and Costs, www.ensec.org/index.php?option=com_content&view=article&id=314:small-nuclear-reactors-and-us-energy-security-concepts-capabilities-and-costs&catid=116:content0411&Itemid=375

Path forward: Department of Defense as first-mover Problematically, despite the immense energy security benefits that would accompany the wide-scale adoption of small modular reactors in the US, with a difficult regulatory environment, anti-nuclear lobbying groups, skeptical public opinion, and of course the recent Fukushima accident, the nuclear industry faces a tough road in the battle for new reactors. While President Obama and Energy Secretary Chu have demonstrated support for nuclear advancement on the SMR front, progress will prove difficult. However, a potential route exists by which small reactors may more easily become a reality: the US military. The US Navy has successfully managed, without accident, over 500 small reactors on-board its ships and submarines throughout 50 years of nuclear operations. At the same time, serious concern exists, highlighted by the Defense Science Board Task Force in 2008, that US military bases are tied to, and almost entirely dependent upon, the fragile civilian electrical grid for 99% of its electricity consumption. To protect military bases’ power supplies and the nation’s military assets housed on these domestic installations, the Board recommended a strategy of “islanding” the energy supplies for military installations, thus ensuring their security and availability in a crisis or conflict that disrupts the nation’s grid or energy supplies. DOD has sought to achieve this through decreased energy consumption and renewable technologies placed on bases, but these endeavors will not go nearly far enough in achieving the department’s objectives. However, by placing small reactors on domestic US military bases, DOD could solve its own energy security quandary—providing assured supplies of secure and constant energy both to bases and possibly the surrounding civilian areas as well. Concerns over reactor safety and security are alleviated by the security already present on installations and the military’s long history of successfully operating nuclear reactors without incident. Unlike reactors on-board ships, small reactors housed on domestic bases would undoubtedly be subject to Nuclear Regulatory Commission (NRC) regulation and certification, however, with strong military backing, adoption of the reactors may prove significantly easier than would otherwise be possible. Additionally, as the reactors become integrated on military facilities, general fears over the use and expansion of nuclear power will ease, creating inroads for widespread adoption of the technology at the private utility level. Finally, and perhaps most importantly, action by DOD as a “first mover” on small reactor technology will preserve America’s badly struggling and nearly extinct nuclear energy industry. The US possesses a wealth of knowledge and technological expertise on SMRs and has an opportunity to take a leading role in its adoption worldwide. With the domestic nuclear industry largely dormant for three decades, the US is at risk of losing its position as the global leader in the international nuclear energy market. If the current trend continues, the US will reach a point in the future where it is forced to import nuclear technologies from other countries—a point echoed by Secretary Chu in his push for nuclear power expansion. Action by the military to install reactors on domestic bases will guarantee the short-term survival of the US nuclear industry and will work to solidify long-term support for nuclear energy. Conclusions In the end, small modular reactors present a viable path forward for both the expansion of nuclear power in the US and also for enhanced US energy security. Offering highly safe, secure, and proliferation-resistant designs, SMRs have the potential to bring carbon-free baseload distributed power across the United States. Small reactors measure up with, and even exceed, large nuclear reactors on questions of safety and possibly on the financial (cost) front as well. SMRs carry many of the benefits of both large-scale nuclear energy generation and renewable energy technologies. At the same time, they can reduce US dependence on fossil fuels for electricity production—moving the US ahead on carbon dioxide and GHG reduction goals and setting a global example. While domestic hurdles within the nuclear regulatory environment domestically have proven nearly impossible to overcome since Three Mile Island, military adoption of small reactors on its bases would provide energy security for the nation’s military forces and may create the inroads necessary to advance the technology broadly and eventually lead to their wide-scale adoption.

## adv

Contention 2 is warming—

#### Warming is real and anthropogenic, but reversible with cuts in carbon emissions

Correll et al 11/5/12

Dr. Bob Corell is a senior policy fellow for the American Meteorological Society and former Chair of the United States Global Change Research Program. Dr. Jeff Masters is the founder and Director of Meteorology for Weather Underground and a former NOAA Hurricane Hunter. Dr. Kevin Trenberth is a Distinguished Senior Scientist in the Climate Analysis Section at the National Center for Atmospheric Research. “Did climate change contribute to Sandy? Yes”, http://www.politico.com/news/stories/1112/83335.html, AM

As Hurricane Sandy battered the East Coast last week, meteorologists and climate scientists were repeatedly asked to explain what role climate change played in amplifying the storm. We did our best to answer: We know that a warming climate puts more energy into storms, including hurricanes, loading them with more rainfall and the stronger winds pushing more of a storm surge. That makes flooding more likely. We also know that storm surge now rides higher on sea levels that have risen over the last century due to global warming, amplifying losses where the surge strikes. On the stretch of the Atlantic Coast that spans from Norfolk to Boston, sea levels have been rising four times faster than the global average. Overall, we know that climate change has stacked the deck so that this kind of event happens more frequently. That answer, however, prompts a deeper, more unsettling question that many want to know: is climate change worsening some recent extreme weather events like super storm Sandy? The short answer is yes. Climate scientists broadly agree that the extreme weather we’ve seen over the past few years is exactly what we’d expect to see in a changing climate. And it’s not just Sandy; we’re on track to have the hottest year in more than a century of record-keeping in the continental United States, the country has suffered one of the most crippling droughts in history, as well as one of the worst wildfire years in history. Last year, when Hurricane Irene hit the United States, meteorologists called it “unprecedented,” yet Sandy has already outpaced the damage from Irene. We’ll probably never know the exact point when the weather stopped being entirely natural. But we should consider Sandy—and other recent extreme weather events – an early taste of a climate-changed world, and a grim preview of the even worse to come, particularly if we continue to pump more carbon pollution from smokestacks and tailpipes up into the atmosphere. Last weekend, millions of Americans prepared for the storm by turning to meteorologists to tell them where the storm would hit. The meteorologists relied on detailed computer models to form an accurate prediction of where it would hit and how strong it would be. We climate scientists use models too, and our results are remarkably consistent and remarkably dire. For example, our models predicted an increase in extreme precipitation with global warming, and that’s exactly what we have witnessed. In the northeast U.S. extreme precipitation has gone up 67 percent in recent years, due to the same rain-loading action that pumped up both Sandy and Hurricane Irene. Our models also predicted more heat waves, and again that’s exactly what we have gotten as the most extreme summers are now much more frequent around the world, setting the stage for intense heat waves. This new world is expensive – damage from Sandy will be in the billions of dollars, with estimates as high as $50 billion. In 2011, the United States broke a record for the most billion dollar weather disasters in one year, fourteen, totaling $47 billion dollars. It’s time to stop asking when climate change will arrive. It’s here, and we need to move aggressively to curb carbon emissions while also preparing for a changed world. We are at nothing less than a critical juncture. In addition to more extreme weather, failing to change our ways will mean extreme costs. Not acting on climate change could cost our nation more than 1 percent of GDP by 2025, or $218 billion a year, according to an analysis by Frank Ackerman, an economist at Tufts University. And it skyrockets from there, possibly to an estimated $1.8 trillion by 2100. Fortunately, scientists have outlined what is needed to meet this challenge. We need to cut industrial carbon pollution. There are several ways to achieve that goal, many of them also money-savers, and as scientists we stand ready to help policymakers figure out the best, most cost-effective ways to do so.

#### It’s not too late

Nuccitelli 8/31/12

(Dana, environmental scientist at a private environmental consulting firm, Bachelor's Degree in astrophysics from the University of California at Berkeley, and a Master's Degree in physics from the University of California at Davis, “Realistically What Might the Future Climate Look Like?,” http://www.skepticalscience.com/realistically-what-might-future-climate-look-like.html, AM)

We're not yet committed to surpassing 2°C global warming, but as Watson noted, we are quickly running out of time to realistically give ourselves a chance to stay below that 'danger limit'. However, 2°C is not a do-or-die threshold. Every bit of CO2 emissions we can reduce means that much avoided future warming, which means that much avoided climate change impacts. As Lonnie Thompson noted, the more global warming we manage to mitigate, the less adaption and suffering we will be forced to cope with in the future. Realistically, based on the current political climate (which we will explore in another post next week), limiting global warming to 2°C is probably the best we can do. However, there is a big difference between 2°C and 3°C, between 3°C and 4°C, and anything greater than 4°C can probably accurately be described as catastrophic, since various tipping points are expected to be triggered at this level. Right now, we are on track for the catastrophic consequences (widespread coral mortality, mass extinctions, hundreds of millions of people adversely impacted by droughts, floods, heat waves, etc.). But we're not stuck on that track just yet, and we need to move ourselves as far off of it as possible by reducing our greenhouse gas emissions as soon and as much as possible.

#### Prefer scientific consensus

Trenberth et al. 12 (Kevin Trenberth, Sc.D, Distinguished Senior Scientist, Climate Analysis Section, National Center for Atmospheric Research Richard Somerville, Ph.D., Distinguished Professor, Scripps Institution of Oceanography, University of California, San Diego Katharine Hayhoe, Ph.D., Director, Climate Science Center, Texas Tech University Rasmus Benestad, Ph.D., Senior Scientist, The Norwegian Meteorological Institute Gerald Meehl, Ph.D., Senior Scientist, Climate and Global Dynamics Division, National Center for Atmospheric Research Michael Oppenheimer, Ph.D., Professor of Geosciences; Director, Program in Science, Technology and Environmental Policy, Princeton University Peter Gleick, Ph.D., co-founder and president, Pacific Institute for Studies in Development, Environment, and Security Michael C. MacCracken, Ph.D., Chief Scientist, Climate Institute, Washington Michael Mann, Ph.D., Director, Earth System Science Center, Pennsylvania State University Steven Running, Ph.D., Professor, Director, Numerical Terradynamic Simulation Group, University of Montana Robert Corell, Ph.D., Chair, Arctic Climate Impact Assessment; Principal, Global Environment Technology Foundation Dennis Ojima, Ph.D., Professor, Senior Research Scientist, and Head of the Dept. of Interior's Climate Science Center at Colorado State University Josh Willis, Ph.D., Climate Scientist, NASA's Jet Propulsion Laboratory Matthew England, Ph.D., Professor, Joint Director of the Climate Change Research Centre, University of New South Wales, Australia Ken Caldeira, Ph.D., Atmospheric Scientist, Dept. of Global Ecology, Carnegie Institution Warren Washington, Ph.D., Senior Scientist, National Center for Atmospheric Research Terry L. Root, Ph.D., Senior Fellow, Woods Institute for the Environment, Stanford University David Karoly, Ph.D., ARC Federation Fellow and Professor, University of Melbourne, Australia Jeffrey Kiehl, Ph.D., Senior Scientist, Climate and Global Dynamics Division, National Center for Atmospheric Research Donald Wuebbles, Ph.D., Professor of Atmospheric Sciences, University of Illinois Camille Parmesan, Ph.D., Professor of Biology, University of Texas; Professor of Global Change Biology, Marine Institute, University of Plymouth, UK Simon Donner, Ph.D., Assistant Professor, Department of Geography, University of British Columbia, Canada Barrett N. Rock, Ph.D., Professor, Complex Systems Research Center and Department of Natural Resources, University of New Hampshire David Griggs, Ph.D., Professor and Director, Monash Sustainability Institute, Monash University, Australia Roger N. Jones, Ph.D., Professor, Professorial Research Fellow, Centre for Strategic Economic Studies, Victoria University, Australia William L. Chameides, Ph.D., Dean and Professor, School of the Environment, Duke University Gary Yohe, Ph.D., Professor, Economics and Environmental Studies, Wesleyan University, CT Robert Watson, Ph.D., Chief Scientific Advisor to the UK Department of Environment, Food and Rural Affairs; Chair of Environmental Sciences, University of East Anglia Steven Sherwood, Ph.D., Director, Climate Change Research Centre, University of New South Wales, Sydney, Australia Chris Rapley, Ph.D., Professor of Climate Science, University College London, UK Joan Kleypas, Ph.D., Scientist, Climate and Global Dynamics Division, National Center for Atmospheric Research James J. McCarthy, Ph.D., Professor of Biological Oceanography, Harvard University Stefan Rahmstorf, Ph.D., Professor of Physics of the Oceans, Potsdam University, Germany Julia Cole, Ph.D., Professor, Geosciences and Atmospheric Sciences, University of Arizona William H. Schlesinger, Ph.D., President, Cary Institute of Ecosystem Studies Jonathan Overpeck, Ph.D., Professor of Geosciences and Atmospheric Sciences, University of Arizona Eric Rignot, Ph.D., Senior Research Scientist, NASA's Jet Propulsion Laboratory; Professor of Earth System Science, University of California, Irvine Wolfgang Cramer, Professor of Global Ecology, Mediterranean Institute for Biodiversity and Ecology, CNRS, Aix-en-Provence, France, 2/1/2012, “Check With Climate Scientists for Views on Climate”, http://online.wsj.com/article/SB10001424052970204740904577193270727472662.html)

Do you consult your dentist about your heart condition? In science, as in any area, reputations are based on knowledge and expertise in a field and on published, peer-reviewed work. If you need surgery, you want a highly experienced expert in the field who has done a large number of the proposed operations. You published "No Need to Panic About Global Warming" (op-ed, Jan. 27) on climate change by the climate-science equivalent of dentists practicing cardiology. While accomplished in their own fields, most of these authors have no expertise in climate science. The few authors who have such expertise are known to have extreme views that are out of step with nearly every other climate expert. This happens in nearly every field of science. For example, there is a retrovirus expert who does not accept that HIV causes AIDS. And it is instructive to recall that a few scientists continued to state that smoking did not cause cancer, long after that was settled science. Climate experts know that the long-term warming trend has not abated in the past decade. In fact, it was the warmest decade on record. Observations show unequivocally that our planet is getting hotter. And computer models have recently shown that during periods when there is a smaller increase of surface temperatures, warming is occurring elsewhere in the climate system, typically in the deep ocean. Such periods are a relatively common climate phenomenon, are consistent with our physical understanding of how the climate system works, and certainly do not invalidate our understanding of human-induced warming or the models used to simulate that warming. Thus, climate experts also know what one of us, Kevin Trenberth, actually meant by the out-of-context, misrepresented quote used in the op-ed. Mr. Trenberth was lamenting the inadequacy of observing systems to fully monitor warming trends in the deep ocean and other aspects of the short-term variations that always occur, together with the long-term human-induced warming trend. The National Academy of Sciences of the U.S. (set up by President Abraham Lincoln to advise on scientific issues), as well as major national academies of science around the world and every other authoritative body of scientists active in climate research have stated that the science is clear: The world is heating up and humans are primarily responsible. Impacts are already apparent and will increase. Reducing future impacts will require significant reductions in emissions of heat-trapping gases. Research shows that more than 97% of scientists actively publishing in the field agree that climate change is real and human caused. It would be an act of recklessness for any political leader to disregard the weight of evidence and ignore the enormous risks that climate change clearly poses. In addition, there is very clear evidence that investing in the transition to a low-carbon economy will not only allow the world to avoid the worst risks of climate change, but could also drive decades of economic growth. Just what the doctor ordered.

#### The impact is extinction

Brandenberg 99

(John & Monica Paxson, Visiting Prof. Researcher @ Florida Space Institute, Physicist Ph.D., Science Writer, Dead Mars Dying Earth, Pg 232-233)

The ozone hole expands, driven by a monstrous synergy with global warming that puts more catalytic ice crystals into the stratosphere, but this affects the far north and south and not the major nations’ heartlands. The seas rise, the tropics roast but the media networks no longer cover it. The Amazon rainforest becomes the Amazon desert. Oxygen levels fall, but profits rise for those who can provide it in bottles. An equatorial high-pressure zone forms, forcing drought in central Africa and Brazil, the Nile dries up and the monsoons fail.  Then inevitably, at some unlucky point in time, a major unexpected event occurs—a major volcanic eruption, a sudden and dramatic shift in ocean circulation or a large asteroid impact (those who think freakish accidents do not occur have paid little attention to life or Mars), or a nuclear war that starts between Pakistan and India and escalates to involve China and Russia . . . Suddenly the gradual climb in global temperatures goes on a mad excursion as the oceans warm and release large amounts of dissolved carbon dioxide from their lower depths into the atmosphere. Oxygen levels go down precipitously as oxygen replaces lost oceanic carbon dioxide. Asthma cases double and then double again. Now a third of the world fears breathing. As the oceans dump carbon dioxide, the greenhouse effect increases, which further warms the oceans, causing them to dump even more carbon. Because of the heat, plants die and burn in enormous fires, which release more carbon dioxide, and the oceans evaporate, adding more water vapor to the greenhouse. Soon, we are in what is termed a runaway greenhouse effect, as happened to Venus eons ago. The last two surviving scientists inevitably argue, one telling the other, “See! I told you the missing sink was in the ocean!” Earth, as we know it, dies. After this Venusian excursion in temperatures, the oxygen disappears into the soil, the oceans evaporate and are lost and the dead Earth loses its ozone layer completely. Earth is too far from the Sun for it to be the second Venus for long. Its atmosphere is slowly lost—as is its water—because of ultraviolet bombardment breaking up all the molecules apart from carbon dioxide. As the atmosphere becomes thin, the Earth becomes colder. For a short while temperatures are nearly normal, but the ultraviolet sears any life that tries to make a comeback. The carbon dioxide thins out to form a thin veneer with a few wispy clouds and dust devils. Earth becomes the second Mars—red, desolate, with perhaps a few hardy microbes surviving.

#### Warming specifically causes hydrogen sulfide expansion—that causes extinction.

Ward 10

(Peter, PhD, professor of Biology and Earth and Space Sciences at the University of Washington, paleontologist and NASA astrobiologist, Fellow at the California Academy of Sciences, The Flooded Earth: Our Future in a World Without Ice Caps, June 29, 2010)

In the rest of this chapter I will support a contention that within several millennia (or less) the planet will see a changeover of the oceans from their current “mixed” states to something much different and dire. Oceans will become stratified by their oxygen content and temperature, with warm, oxygen-free water lining the ocean basins. Stratified oceans like this in the past (and they were present for most of Earth’s history) have always been preludes to biotic catastrophe. Because the continents were in such different positions at that time, models we use today to understand ocean current systems are still crude when it comes to analyzing the ancient oceans, such as those of the Devonian or Permian Periods. Both times witnessed major mass extinctions, and these extinctions were somehow tied to events in the sea. Yet catastrophic as it was, the event that turned the Canning Coral Reef of Devonian age into the Canning Microbial Reef featured at the start of this chapter was tame compared to that ending the 300 million- to 251 million-year-old Permian Period, and for this reason alone the Permian ocean and its fate have been far more studied than the Devonian. But there is another reason to concentrate on the Permian mass extinction: it took place on a world with a climate more similar to that of today than anytime in the Devonian. Even more important, it was a world with ice sheets at the poles, something the more tropical Devonian Period may never have witnessed. For much of the Permian Period, the Earth, as it does today, had abundant ice caps at both poles, and there were large-scale continental glaciations up until at least 270 million years ago, and perhaps even later.4 But from then until the end of the Permian, the planet rapidly warmed, the ice caps disappeared, and the deep ocean bottoms filled with great volumes of warm, virtually oxygen-free seawater. The trigger for disaster was a short-term but massive infusion of carbon dioxide and other greenhouse gases into the atmosphere at the end of the Permian from the spectacular lava outpourings over an appreciable portion of what would become northern Asia. The lava, now ancient but still in place, is called the “Siberian Traps,” the latter term coming from the Scandinavian for lava flows. The great volcanic event was but the start of things, and led to changes in oceanography. The ultimate kill mechanism seems to have been a lethal combination of rising temperature, diminishing oxygen, and influx into water and air of the highly poisonous compound hydrogen sulfide. The cruel irony is that this latter poison was itself produced by life, not by the volcanoes. The bottom line is that life produced the ultimate killer in this and surely other ancient mass extinctions. This finding was one that spurred me to propose the Medea Hypothesis, and a book of the same name.5 Hydrogen sulfide poisoning might indeed be the worst biological effect of global warming. There is no reason that such an event cannot happen again, given short-term global warming. And because of the way the sun ages, it may be that such events will be ever easier to start than during the deep past. How does the sun get involved in such nasty business as mass extinction? Unlike a campfire that burns down to embers, any star gets ever hotter when it is on the “main sequence,” which is simply a term used to described the normal aging of a star—something like the progression we all go through as we age. But new work by Jeff Kiehl of the University of Colorado shows that because the sun keeps getting brighter, amounts of CO2 that in the past would not have triggered the process result in stagnant oceans filled with H2S-producing microbes. His novel approach was to estimate the global temperature rise to be expected from carbon dioxide levels added to the energy hitting the earth from the sun. Too often we refer to the greenhouse effect as simply a product of the gases. But it is sunlight that actually produces the heat, and that amount of energy hitting the earth keeps increasing. He then compared those to past times of mass extinctions. The surprise is that a CO2 level of 1,000 ppm would—with our current solar radiation—make our world the second hottest in Earth history—when the five hottest were each associated with mass extinction. In the deep history of our planet, there have been at least five short intervals in which the majority of living species suddenly went extinct. Biologists are used to thinking about how environmental pressures slowly choose the organisms most fit for survival through natural selection, shaping life on Earth like an artist sculpting clay. However, mass extinctions are drastic examples of natural selection at its most ruthless, killing vast numbers of species at one time in a way hardly typical of evolution. In the 1980s, Nobel Prize-winning physicist Luis Alvarez, and his son Walter Alvarez, first hypothesized that the impact of comets or asteroids caused the mass extinctions of the past.6 Most scientists slowly come to accept this theory of extinction, further supported by the discovery of a great scar in the earth—an impact crater—off the coast of Mexico that dates to around the time the dinosaurs went extinct. An asteroid probably did kill off the dinosaurs, but the causes of the remaining four mass extinctions are still obscured beneath the accumulated effects of hundreds of millions of years, and no one has found any credible evidence of impact craters. Rather than comets and asteroids, it now appears that short-term global warming was the culprit for the four other mass extinctions. I detailed the workings of these extinctions first in a 1996 Discover magazine article,7 then in an October 2006 Scientific American article, and finally in my 2007 book, Under a Green Sky.8 In each I considered whether such events could happen again. In my mind, such extinctions constitute the worst that could happen to life and the earth as a result of short-term global warming. But before we get to that, let us look at the workings of these past events. The evidence at hand links the mass extinctions with a changeover in the ocean from oxygenated to anoxic bottom waters. The source of this was a change in where bottom waters are formed. It appears that in such events, the source of our earth’s deep water shifted from the high latitudes to lower latitudes, and the kind of water making it to the ocean bottoms was different as well: it changed from cold, oxygenated water to warm water containing less oxygen. The result was the extinction of deep-water organisms. Thus a greenhouse extinction is a product of a changeover of the conveyor-belt current systems found on Earth any time there is a marked difference in temperatures between the tropics and the polar regions. Let us summarize the steps that make greenhouse extinction happen. First, the world warms over short intervals due to a sudden increase in carbon dioxide and methane, caused initially by the formation of vast volcanic provinces called flood basalts. The warmer world affects the ocean circulation systems and disrupts the position of the conveyor currents. Bottom waters begin to have warm, low-oxygen water dumped into them. The warming continues, and the decrease of equator-to-pole temperature differences brings ocean winds and surface currents to a near standstill. The mixing of oxygenated surface waters with the deeper and volumetrically increasing low-oxygen bottom waters lessens, causing ever-shallower water to change from oxygenated to anoxic. Finally, the bottom water exists in depths where light can penetrate, and the combination of low oxygen and light allows green sulfur bacteria to expand in numbers, filling the low-oxygen shallows. The bacteria produce toxic amounts of H2S, with the flux of this gas into the atmosphere occurring at as much as 2,000 times today’s rates. The gas rises into the high atmosphere, where it breaks down the ozone layer. The subsequent increase in ultraviolet radiation from the sun kills much of the photosynthetic green plant phytoplankton. On its way up into the sky, the hydrogen sulfide also kills some plant and animal life, and the combination of high heat and hydrogen sulfide creates a mass extinction on land.9 Could this happen again? No, says one of the experts who write the RealClimate.org Web site, Gavin Schmidt, who, it turns out, works under Jim Hansen at the NASA Goddard Space Flight Center near Washington, DC. I disagreed and challenged him to an online debate. He refused, saying that the environmental situation is going to be bad enough without resorting to creating a scenario for mass extinction. But special pleading has no place in science. Could it be that global warming could lead to the extinction of humanity? That prospect cannot be discounted. To pursue this question, let us look at what might be the most crucial of all systems maintaining habitability on Planet Earth: the thermohaline current systems, sometimes called the conveyor currents.

#### It also acidifies the oceans—the impact is extinction

Romm ‘9

(Joe, a Fellow at American Progress and is the editor of Climate Progress, which New York Times columnist Tom Friedman called "the indispensable blog" and Time magazine named one of the 25 “Best Blogs of 2010.″ In 2009, Rolling Stone put Romm #88 on its list of 100 “people who are reinventing America.” Time named him a “Hero of the Environment″ and “The Web’s most influential climate-change blogger.” Romm was acting assistant secretary of energy for energy efficiency and renewable energy in 1997, where he oversaw $1 billion in R&D, demonstration, and deployment of low-carbon technology. He is a Senior Fellow at American Progress and holds a Ph.D. in physics from MIT, “Imagine a World without Fish: Deadly ocean acidification — hard to deny, harder to geo-engineer, but not hard to stop — is subject of documentary ,” http://thinkprogress.org/romm/2009/09/02/204589/a-sea-change-imagine-a-world-without-fish-ocean-acidification-film/, AM)

Global warming is “capable of wrecking the marine ecosystem and depriving future generations of the harvest of the seas” (see Ocean dead zones to expand, “remain for thousands of years”). A post on ocean acidification from the new Conservation Law Foundation blog has brought to my attention that the first documentary on the subject, A Sea Change: Imagine a World without Fish, is coming out. Ocean acidification must be a core climate message, since it is hard to deny and impervious to the delusion that geoengineering is the silver bullet. Indeed, a major 2009 study GRL study, “Sensitivity of ocean acidification to geoengineered climate stabilization” (subs. req’d), concluded: The results of this paper support the view that climate engineering will not resolve the problem of ocean acidification, and that therefore deep and rapid cuts in CO2 emissions are likely to be the most effective strategy to avoid environmental damage from future ocean acidification. If you want to understand ocean acidification better, see this BBC story, which explains: Man-made pollution is raising ocean acidity at least 10 times faster than previously thought, a study says. Or see this Science magazine study, “Evidence for Upwelling of Corrosive “Acidified” Water onto the Continental Shelf” (subs. req’), which found Our results show for the first time that a large section of the North American continental shelf is impacted by ocean acidification. Other continental shelf regions may also be impacted where anthropogenic CO2-enriched water is being upwelled onto the shelf. Or listen to the Australia’s ARC Centre of Excellence for Coral Reef Studies, which warns: The world’s oceans are becoming more acid, with potentially devastating consequences for corals and the marine organisms that build reefs and provide much of the Earth’s breathable oxygen. The acidity is caused by the gradual buildup of carbon dioxide (CO2) in the atmosphere, dissolving into the oceans. Scientists fear it could be lethal for animals with chalky skeletons which make up more than a third of the planet’s marine life”¦. Corals and plankton with chalky skeletons are at the base of the marine food web. They rely on sea water saturated with calcium carbonate to form their skeletons. However, as acidity intensifies, the saturation declines, making it harder for the animals to form their skeletal structures (calcify). “Analysis of coral cores shows a steady drop in calcification over the last 20 years,” says Professor Ove Hoegh-Guldberg of CoECRS and the University of Queensland. “There’s not much debate about how it happens: put more CO2 into the air above and it dissolves into the oceans. “When CO2 levels in the atmosphere reach about 500 parts per million, you put calcification out of business in the oceans.” (Atmospheric CO2 levels are presently 385 ppm, up from 305 in 1960.) I’d like to see an analysis of what happens when you get to 850 to 1000+ ppm because that is where we’re headed (see U.S. media largely ignores latest warning from climate scientists: “Recent observations confirm “¦ the worst-case IPCC scenario trajectories (or even worse) are being realised” “” 1000 ppm). The CLF post notes: Dr. Jane Lubchenco, Administrator of the National Oceanic and Atmospheric Administration (NOAA) warns that an acidic ocean is the “equally evil twin” of climate change. Scott Doney, a senior scientist at the Woods Hole Oceanographic Institution noted in a public presentation that “New England is the most vulnerable region in the country to ocean acidification.” In June, dozens of Academies of Science, including ours and China’s, issued a joint statement on ocean acidification, warned “Marine food supplies are likely to be reduced with significant implications for food production and security in regions dependent on fish protein, and human health and wellbeing” and “Ocean acidification is irreversible on timescales of at least tens of thousands of years.” They conclude: Ocean acidification is a direct consequence of increasing atmospheric CO2 concentrations. To avoid substantial damage to ocean ecosystems, deep and rapid reductions of global CO2 emissions by at least 50% by 2050, and much more thereafter are needed. We, the academies of science working through the InterAcademy Panel on International Issues (IAP), call on world leaders to: “¢ Acknowledge that ocean acidification is a direct and real consequence of increasing atmospheric CO2 concentrations, is already having an effect at current concentrations, and is likely to cause grave harm to important marine ecosystems as CO2 concentrations reach 450 ppm and above; “¢ Recognise that reducing the build up of CO2 in the atmosphere is the only practicable solution to mitigating ocean acidification; “¢ Within the context of the UNFCCC negotiations in the run up to Copenhagen 2009, recognise the direct threats posed by increasing atmospheric CO2 emissions to the oceans and therefore society, and take action to mitigate this threat; “¢ Implement action to reduce global CO2 emissions by at least 50% of 1990 levels by 2050 and continue to reduce them thereafter. If we want to save life in the oceans “” and save ourselves, since we depend on that life “” the time to start slashing carbon dioxide emissions is now.

#### SMRs are key–it’s the only source that can scale

Palley 11

Reese Palley, The London School of Economics,  2011, The Answer: Why Only Inherently Safe, Mini Nuclear Power Plans Can Save Our World, p. 186-90

The central investigation of this book has been directed at the scale of the nuclear industry. The book has argued that all anthropogenic challenges that put in question continued human existence on Earth are a matter of scale. It was nature’s unanticipated success with her human experiment, the evolutionary choice of brains over brawn, setting in motion the underlying scale problems that opened our Pandora’s box of calamities. The history of man on Earth can best be viewed as a race between population and resources in which, for some millennia, population expansion leads and the Earth’s resources have been straining to catch up. When population bloomed from 100 million brainy humans to a billion, the problems of scale emerged as the price we had to pay for success as a species. The conversion of forests to agriculture, responding to the need to feed a burgeoning population, initiated the emerging problem of scale. The elimination of oxygen-emitting forests was mitigated to a large measure in the beginning of our population growth by the slow rate of change of the deforestation, which allowed an absorbable increase of CO2 in the atmosphere. Natural processes, such as the ability of the oceans to take up CO2, tamped down global warming. But as the scale of the release of warming gases exploded a few hundred years ago, our remaining forests and our seas, our first line of defense against CO2 imbalance, could not cope and the level of CO2 has risen alarmingly each year since 1800. When human population climbed from a billion to six billion and these six billion reveled in the enormous energy content of coal, the scenario for disaster on a global scale came into play. The impact of the loss of forest paled in comparison to the havoc that the use of fossil fuels represented. In a world that was hungry for energy and, not incidentally, living on a Malthusian edge of food supply, coal burst upon us as manna from heaven. Coal was everywhere, easy to mine, and in enormous, almost unending supply It generated the cheap heat needed to run the engines of early industrialization. An unintended Faustian bargain was struck. The immediate cost of coal in the cities, dirt and pollution, were not out of sync with what urban man had lived with for centuries. It was beyond the science and the understanding of the time that burning vast millennial coal deposits would do little more than discommode the proximate few and benefit many. Again it was not the burning, it was the scale of the burning that dumped billions of tons of CO2 into the atmosphere. We are now presented with a horrendous invoice that must be paid if we are to survive in anywhere near the comfort to which we have become accustomed. It has been the intent of this book to argue that the scale of the warming catastrophe must be viewed primarily in terms of the continuing flow of CO2 into the atmosphere. Every possible source of CO2, no matter how small, must be identified and interdicted, since every fourth molecule of the gas will remain with us as a climate moderator for thousands of years. What we find is that all of the sources of energy including so-called green energy are CO2-culpable and that each, in spite of claims to the contrary, adds its tiny mite or enormous mass to the climate changes looming in man’s future. The book argues that the scale of the consumption of fossil fuels is clearly unsustainable and, more to the point, that the feeble attempts to restrict CO2 production are little more than a glossing over of the problem. Capping but not ending production of greenhouse gases only magnifies the unthinkable future costs of bringing the level of CO2 and other greenhouse gases back into balance. Logic dictates that merely limiting greenhouse gases pushes possible solutions farther and farther into the future and does little to mitigate the difficulties that will arise in the near future. Logic dictates that our reasonably comfortable survival depends on the immediate and total cessation of increases to parts per million of CO2 in the air. Logic dictates that if we are to continue to enjoy the level of comfort, wealth, and ease afforded us since the beginning of the twentieth century we must not only halt the increase but commence the actual decrease of warming gases at work in the atmosphere. That conclusion brings the book to the problems and the solutions inherent in nuclear power, the only energy source that can guarantee us a reasonable future that might be resistant to CO2 warming. Here the argument returns once again to the problem of scale of nuclear reactors, especially as the size of these reactors is related to the brief time left to us to get a grip on calamitous climate changes. The beginnings of nuclear energy lay in the demands of war. The battle between good and evil characterized by the Second World War gave hurried birth to a discovery that had the inherent power to both destroy and salvage. The power to destroy required plutonium on an enormous scale, which was projected forward into the postwar development of civilian reactors. The demand for scarce plutonium for the bombs of the cold war defined the type of reactors that were being developed. These were the breeder reactors, which spewed out plutonium measured in tons that had previously been available only in ounces, and would continue to do so when the wartime need was far behind us. What was once precious, rare, and desirable has become dangerous nuclear waste, and the imperfectly perceived scale of the waste problem has seriously inhibited the logical growth and development of nuclear power. By some unthinkable universal coincidence, nuclear power became available to man for war at the same time that it could prove to be the solution to man’s greatest peacetime challenge. But the gigawatt nuclear power plants that emerged from the war had within them the seeds of their own severe limitation. The scale of the risks, real and imagined, grew exponentially as the scale of energy output grew only linearly. These risks, some merely perceived, some dangerously real and some financial, have conspired to restrict the enormous expansion of nuclear power that is needed to quickly replace our present consumption of energy from fossil fuels. The present rate of replacement of fossil with nuclear sources is at a pace that will have little impact on ultimately dealing with the CO2 imbalance. This slow rate of change is compounded of public fears, bureaucratic regulatory mechanisms resistant to novel solutions, and a private capital market that is unable to conjure with the imagined and real risks of the huge gigawatt reactors that dominate the industry. It is a Gordian knot that cannot be unraveled but which can only be cut by a political sword that, alas, still lacks the edge to do the job. By another rare act of cosmic fortuity, there is a parallel existing nuclear technology that, barring political interference, is capable of addressing the scale problems inherent in gigawatt reactors. From the beginning of the nuclear era, researchers such as Weinberg and Wigner and Teller developed small, inherently safe nuclear reactors that did not breed plutonium. This was reason enough for the military, balancing urgent demands on research and development budgets, to consign the concept of “smaller and safer is better” to dusty shelves in our national science attic. This book has argued that small reactors, that produce a tenth of the energy of the giants also generate inordinately less of the risk that inhibits growth of the industry. Construction of small reactors is a fraction of the cost of construction of gigawatt reactors. Thus the number of years that scarce capital is tied up and at risk is substantially reduced. The book argues that a 100 MWe reactor88 is a much bigger hardware bargain than a gigawatt reactor, which, from start to output, can cost $15 billion. It is not only the hardware costs that contribute to the devilish details of risk. The problem is the inability of the market to accurately or even approximately estimate the real cost of the capital that would be tied up for over a decade in a project that, through technological advancements, could be obsolete before it ever joins the grid.

#### SMR-based nuclear power is safe and solves warming

Shellenberger 12

(Michael, founder of the Breakthrough Institute, graduate of Earlham College and holds a masters degree in cultural anthropology from the University of California, Santa Cruz, "New Nukes: Why We Need Radical Innovation to Make New Nuclear Energy Cheap", September 11, http://thebreakthrough.org/index.php/programs/energy-and-climate/new-nukes/)

Arguably, the biggest impact of Fukushima on the nuclear debate, ironically, has been to force a growing number of pro-nuclear environmentalists out of the closet, including us. The reaction to the accident by anti-nuclear campaigners and many Western publics put a fine point on the gross misperception of risk that informs so much anti-nuclear fear. Nuclear remains the only proven technology capable of reliably generating zero-carbon energy at a scale that can have any impact on global warming. Climate change -- and, for that matter, the enormous present-day health risks associated with burning coal, oil, and gas -- simply dwarf any legitimate risk associated with the operation of nuclear power plants. About 100,000 people die every year due to exposure to air pollutants from the burning of coal. By contrast, about 4,000 people have died from nuclear energy -- ever -- almost entirely due to Chernobyl. But rather than simply lecturing our fellow environmentalists about their misplaced priorities, and how profoundly inadequate present-day renewables are as substitutes for fossil energy, we would do better to take seriously the real obstacles standing in the way of a serious nuclear renaissance. Many of these obstacles have nothing to do with the fear-mongering of the anti-nuclear movement or, for that matter, the regulatory hurdles imposed by the U.S. Nuclear Regulatory Commission and similar agencies around the world. As long as nuclear technology is characterized by enormous upfront capital costs, it is likely to remain just a hedge against overdependence on lower-cost coal and gas, not the wholesale replacement it needs to be to make a serious dent in climate change. Developing countries need large plants capable of bringing large amounts of new power to their fast-growing economies. But they also need power to be cheap. So long as coal remains the cheapest source of electricity in the developing world, it is likely to remain king. The most worrying threat to the future of nuclear isn't the political fallout from Fukushima -- it's economic reality. Even as new nuclear plants are built in the developing world, old plants are being retired in the developed world. For example, Germany's plan to phase-out nuclear simply relies on allowing existing plants to be shut down when they reach the ends of their lifetime. Given the size and cost of new conventional plants today, those plants are unlikely to be replaced with new ones. As such, the combined political and economic constraints associated with current nuclear energy technologies mean that nuclear energy's share of global energy generation is unlikely to grow in the coming decades, as global energy demand is likely to increase faster than new plants can be deployed. To move the needle on nuclear energy to the point that it might actually be capable of displacing fossil fuels, we'll need new nuclear technologies that are cheaper and smaller. Today, there are a range of nascent, smaller nuclear power plant designs, some of them modifications of the current light-water reactor technologies used on submarines, and others, like thorium fuel and fast breeder reactors, which are based on entirely different nuclear fission technologies. Smaller, modular reactors can be built much faster and cheaper than traditional large-scale nuclear power plants. Next-generation nuclear reactors are designed to be incapable of melting down, produce drastically less radioactive waste, make it very difficult or impossible to produce weapons grade material, use less water, and require less maintenance. Most of these designs still face substantial technical hurdles before they will be ready for commercial demonstration. That means a great deal of research and innovation will be necessary to make these next generation plants viable and capable of displacing coal and gas. The United States could be a leader on developing these technologies, but unfortunately U.S. nuclear policy remains mostly stuck in the past. Rather than creating new solutions, efforts to restart the U.S. nuclear industry have mostly focused on encouraging utilities to build the next generation of large, light-water reactors with loan guarantees and various other subsidies and regulatory fixes. With a few exceptions, this is largely true elsewhere around the world as well. Nuclear has enjoyed bipartisan support in Congress for more than 60 years, but the enthusiasm is running out. The Obama administration deserves credit for authorizing funding for two small modular reactors, which will be built at the Savannah River site in South Carolina. But a much more sweeping reform of U.S. nuclear energy policy is required. At present, the Nuclear Regulatory Commission has little institutional knowledge of anything other than light-water reactors and virtually no capability to review or regulate alternative designs. This affects nuclear innovation in other countries as well, since the NRC remains, despite its many critics, the global gold standard for thorough regulation of nuclear energy. Most other countries follow the NRC's lead when it comes to establishing new technical and operational standards for the design, construction, and operation of nuclear plants. What's needed now is a new national commitment to the development, testing, demonstration, and early stage commercialization of a broad range of new nuclear technologies -- from much smaller light-water reactors to next generation ones -- in search of a few designs that can be mass produced and deployed at a significantly lower cost than current designs. This will require both greater public support for nuclear innovation and an entirely different regulatory framework to review and approve new commercial designs. In the meantime, developing countries will continue to build traditional, large nuclear power plants. But time is of the essence. With the lion's share of future carbon emissions coming from those emerging economic powerhouses, the need to develop smaller and cheaper designs that can scale faster is all the more important. A true nuclear renaissance can't happen overnight. And it won't happen so long as large and expensive light-water reactors remain our only option. But in the end, there is no credible path to mitigating climate change without a massive global expansion of nuclear energy. If you care about climate change, nothing is more important than developing the nuclear technologies we will need to get that job done.

#### Plan results in global SMR exports–massively reduces emissions.

Rosner 11

Robert Rosner, Stephen Goldberg, Energy Policy Institute at Chicago, The Harris School of Public Policy Studies, November 2011, SMALL MODULAR REACTORS –KEY TO FUTURE NUCLEAR POWER GENERATION IN THE U.S., https://epic.sites.uchicago.edu/sites/epic.uchicago.edu/files/uploads/EPICSMRWhitePaperFinalcopy.pdf

As stated earlier, SMRs have the potential to achieve significant greenhouse gas emission reductions. They could provide alternative baseload power generation to facilitate the retirement of older, smaller, and less efficient coal generation plants that would, otherwise, not be good candidates for retrofitting carbon capture and storage technology. They could be deployed in regions of the U.S. and the world that have less potential for other forms of carbon-free electricity, such as solar or wind energy. There may be technical or market constraints, such as projected electricity demand growth and transmission capacity, which would support SMR deployment but not GW-scale LWRs. From the on-shore manufacturing perspective, a key point is that the manufacturing base needed for SMRs can be developed domestically. Thus, while the large commercial LWR industry is seeking to transplant portions of its supply chain from current foreign sources to the U.S., the SMR industry offers the potential to establish a large domestic manufacturing base building upon already existing U.S. manufacturing infrastructure and capability, including the Naval shipbuilding and underutilized domestic nuclear component and equipment plants. The study team learned that a number of sustainable domestic jobs could be created – that is, the full panoply of design, manufacturing, supplier, and construction activities – if the U.S. can establish itself as a credible and substantial designer and manufacturer of SMRs. While many SMR technologies are being studied around the world, a strong U.S. commercialization program can enable U.S. industry to be first to market SMRs, thereby serving as a fulcrum for export growth as well as a lever in influencing international decisions on deploying both nuclear reactor and nuclear fuel cycle technology. A viable U.S.-centric SMR industry would enable the U.S. to recapture technological leadership in commercial nuclear technology, which has been lost to suppliers in France, Japan, Korea, Russia, and, now rapidly emerging, China.

## Solvency

Contention 3 is solvency—

#### DoD acquisition of SMR’s ensures rapid military adoption, commercialization, and U.S. leadership

Andres 11

Richard Andres, Professor of National Security Strategy at the National War College and a Senior Fellow and Energy and Environmental Security and Policy Chair in the Center for Strategic Research, Institute for National Strategic Studies, at the National Defense University, and Hanna Breetz, doctoral candidate in the Department of Political Science at The Massachusetts Institute of Technology, Small Nuclear Reactorsfor Military Installations:Capabilities, Costs, andTechnological Implications, www.ndu.edu/press/lib/pdf/StrForum/SF-262.pdf

Thus far, this paper has reviewed two of DOD’s most pressing energy vulnerabilities—grid insecurity and fuel convoys—and explored how they could be addressed by small reactors. We acknowledge that there are many uncertainties and risks associated with these reactors. On the other hand, failing to pursue these technologies raises its own set of risks for DOD, which we review in this section: first, small reactors may fail to be commercialized in the United States; second, the designs that get locked in by the private market may not be optimal for DOD’s needs; and third, expertise on small reactors may become concentrated in foreign countries. By taking an early “first mover” role in the small reactor market, DOD could mitigate these risks and secure the long-term availability and appropriateness of these technologies for U.S. military applications. The “Valley of Death.” Given the promise that small reactors hold for military installations and mobility, DOD has a compelling interest in ensuring that they make the leap from paper to production. However, if DOD does not provide an initial demonstration and market, there is a chance that the U.S. small reactor industry may never get off the ground. The leap from the laboratory to the marketplace is so difficult to bridge that it is widely referred to as the “Valley of Death.” Many promising technologies are never commercialized due to a variety of market failures— including technical and financial uncertainties, information asymmetries, capital market imperfections, transaction costs, and environmental and security externalities— that impede financing and early adoption and can lock innovative technologies out of the marketplace. 28 In such cases, the Government can help a worthy technology to bridge the Valley of Death by accepting the first mover costs and demonstrating the technology’s scientific and economic viability.29 [FOOTNOTE 29: There are numerous actions that the Federal Government could take, such as conducting or funding research and development, stimulating private investment, demonstrating technology, mandating adoption, and guaranteeing markets. Military procurement is thus only one option, but it has often played a decisive role in technology development and is likely to be the catalyst for the U.S. small reactor industry. See Vernon W. Ruttan, Is War Necessary for Economic Growth? (New York: Oxford University Press, 2006); Kira R. Fabrizio and David C. Mowery, “The Federal Role in Financing Major Inventions: Information Technology during the Postwar Period,” in Financing Innovation in the United States, 1870 to the Present, ed. Naomi R. Lamoreaux and Kenneth L. Sokoloff (Cambridge, MA: The MIT Press, 2007), 283–316.] Historically, nuclear power has been “the most clear-cut example . . . of an important general-purpose technology that in the absence of military and defense related procurement would not have been developed at all.”30 Government involvement is likely to be crucial for innovative, next-generation nuclear technology as well. Despite the widespread revival of interest in nuclear energy, Daniel Ingersoll has argued that radically innovative designs face an uphill battle, as “the high capital cost of nuclear plants and the painful lessons learned during the first nuclear era have created a prevailing fear of first-of-a-kind designs.”31 In addition, Massachusetts Institute of Technology reports on the Future of Nuclear Power called for the Government to provide modest “first mover” assistance to the private sector due to several barriers that have hindered the nuclear renaissance, such as securing high up-front costs of site-banking, gaining NRC certification for new technologies, and demonstrating technical viability.32 It is possible, of course, that small reactors will achieve commercialization without DOD assistance. As discussed above, they have garnered increasing attention in the energy community. Several analysts have even argued that small reactors could play a key role in the second nuclear era, given that they may be the only reactors within the means of many U.S. utilities and developing countries.33 However, given the tremendous regulatory hurdles and technical and financial uncertainties, it appears far from certain that the U.S. small reactor industry will take off. If DOD wants to ensure that small reactors are available in the future, then it should pursue a leadership role now. Technological Lock-in. A second risk is that if small reactors do reach the market without DOD assistance, the designs that succeed may not be optimal for DOD’s applications. Due to a variety of positive feedback and increasing returns to adoption (including demonstration effects, technological interdependence, network and learning effects, and economies of scale), the designs that are initially developed can become “locked in.”34 Competing designs—even if they are superior in some respects or better for certain market segments— can face barriers to entry that lock them out of the market. If DOD wants to ensure that its preferred designs are not locked out, then it should take a first mover role on small reactors. It is far too early to gauge whether the private market and DOD have aligned interests in reactor designs. On one hand, Matthew Bunn and Martin Malin argue that what the world needs is cheaper, safer, more secure, and more proliferation-resistant nuclear reactors; presumably, many of the same broad qualities would be favored by DOD.35 There are many varied market niches that could be filled by small reactors, because there are many different applications and settings in which they can be used, and it is quite possible that some of those niches will be compatible with DOD’s interests.36 On the other hand, DOD may have specific needs (transportability, for instance) that would not be a high priority for any other market segment. Moreover, while DOD has unique technical and organizational capabilities that could enable it to pursue more radically innovative reactor lines, DOE has indicated that it will focus its initial small reactor deployment efforts on LWR designs.37 If DOD wants to ensure that its preferred reactors are developed and available in the future, it should take a leadership role now. Taking a first mover role does not necessarily mean that DOD would be “picking a winner” among small reactors, as the market will probably pursue multiple types of small reactors. Nevertheless, DOD leadership would likely have a profound effect on the industry’s timeline and trajectory. Domestic Nuclear Expertise. From the perspective of larger national security issues, if DOD does not catalyze the small reactor industry, there is a risk that expertise in small reactors could become dominated by foreign companies. A 2008 Defense Intelligence Agency report warned that the United States will become totally dependent on foreign governments for future commercial nuclear power unless the military acts as the prime mover to reinvigorate this critical energy technology with small, distributed power reactors.38 Several of the most prominent small reactor concepts rely on technologies perfected at Federally funded laboratories and research programs, including the Hyperion Power Module (Los Alamos National Laboratory), NuScale (DOE-sponsored research at Oregon State University), IRIS (initiated as a DOE-sponsored project), Small and Transportable Reactor (Lawrence Livermore National Laboratory), and Small, Sealed, Transportable, Autonomous Reactor (developed by a team including the Argonne, Lawrence Livermore, and Los Alamos National Laboratories). However, there are scores of competing designs under development from over a dozen countries. If DOD does not act early to support the U.S. small reactor industry, there is a chance that the industry could be dominated by foreign companies. Along with other negative consequences, the decline of the U.S. nuclear industry decreases the NRC’s influence on the technology that supplies the world’s rapidly expanding demand for nuclear energy. Unless U.S. companies begin to retake global market share, in coming decades France, China, South Korea, and Russia will dictate standards on nuclear reactor reliability, performance, and proliferation resistance.

#### SMR’s are cost-effective and safe

Ringle 10

(John C. Ringle of Corvallis is professor emeritus of nuclear engineering at Oregon State University, “Reintroduction of reactors in US a major win” November 13, 2010, http://robertmayer.wordpress.com/2010/11/21/reintroduction-of-reactors-in-us-a-major-win/)

Small nuclear reactors will probably be the mechanism that ushers in nuclear power’s renaissance in the U.S. Nuclear plants currently supply about 20 percent of the nation’s electricity and more than 70 percent of our carbon-free energy. But large nuclear plants c ost $8 billion to $10 billion and utilities are having second thoughts about how to finance these plants. A small modular reactor (SMR) has several advantages over the conventional 1,000-megawatt plant: 1. It ranges in size from 25 to 140 megawatts, hence only costs about a tenth as much as a large plant. 2. It uses a cookie-cutter standardized design to reduce construction costs and can be built in a factory and shipped to the site by truck, railroad or barge. 3. The major parts can be built in U.S. factories, unlike some parts for the larger reactors that must be fabricated overseas. 4. Because of the factory-line production, the SMR could be built in three years with one-third of the workforce of a large plant. 5. More than one SMR could be clustered together to form a larger power plant complex. This provides versatility in operation, particularly in connection with large wind farms. With the variability of wind, one or more SMRs could be run or shut down to provide a constant base load supply of electricity. 6. A cluster of SMRs should be very reliable. One unit could be taken out of service for maintenance or repair without affecting the operation of the other units. And since they are all of a common design, replacement parts could satisfy all units. France has already proved the reliability of standardized plants. At least half a dozen companies are developing SMRs, including NuScale in Oregon. NuScale is American-owned and its 45-megawatt design has some unique features. It is inherently safe. It could be located partially or totally below ground, and with its natural convection cooling system, it does not rely on an elaborate system of pumps and valves to provide safety. There is no scenario in which a loss-of-coolant accident could occur. Tests conducted on a one-third model of the NuScale reactor at Oregon State University have confirmed the effectiveness of this cooling system. Small reactors haven’t been built for commercial use since the very early days of nuclear power development, when the very first power reactors were of this size. For more than 50 years, however, small reactors have been built and operated successfully and safely by the Navy in submarines and aircraft carriers. The Nuclear Regulatory Commission anticipates getting applications from two to three companies within the next two years for approval of SMR designs. Energy Secretary

#### DoD needs to lead

Glen Butler, Lt. Col., 2011, Not Green Enough, www.mca-marines.org/gazette/not-green-enough

SMRs have relatively low plant cost, can replace aging fossil plants, and do not emit greenhouse gasses. Some are as small as a “hot tub” and can be stored underground, dramatically increasing safety and security from terrorist threats.25 Encouragingly, in fiscal year 2010 (FY10) the DoE allocated $0 to the U.S. SMR Program; in FY11, they’ve requested $38.9 million. This funding is to support two main activities—public/private partnerships to advance SMR designs and research and development and demonstrations. According to the DoE’s website, one of the planned program accomplishments for FY11 is to “collaborate with the Department of Defense (DoD) . . . to assess the feasibility of SMR designs for energy resources at DoD installations.”26 The Marine Corps should vigorously seek the opportunity to be a DoD entity providing one platform for this feasibility assessment.27 Fourth, SMR technology offers the Marine Corps another unique means to lead from the front—not just of the other Services but also of the Nation, and even the world.28 This potential Pete Ellis moment should be seized. There are simple steps we could take, and others stand ready to lead if we are not.30 But the temptation to “wait and see” and “let the others do it; then we’ll adopt it” mentality is not always best. Energy security demands boldness, not timidity. To be fair, nuclear technology comes with challenges, of course, and with questions that have been kicked around for decades. An April 1990 Popular Science article asked, “Next Generation Nuclear Reactors—Dare we build them?” and included some of the same verbiage heard in similar discussions today.31 Compliance with National Environment Policy Act requirements necessitates lengthy and detailed preaction analyses, critical community support must be earned, and disposal challenges remain. Still, none of these hurdles are insurmountable. Yet despite the advances in safety, security, and efficiency in recent years, nuclear in the energy equation remains the new “n-word” for most military circles. And despite the fact that the FY10 National Defense Authorization Act called on the DoD to “conduct a study [of] the feasibility of nuclear plants on military installations,” the Office of the Secretary of Defense has yet to fund the study. Fifth, the cumbersome, bureaucratic certification process of the Nuclear Regulatory Commission (NRC), often enough to scare away potential entrepreneurs and investors, is not necessarily a roadblock to success. The NRC is “responsible for licensing and regulating the operation of commercial nuclear power plants in the United States.” Military installations offer unique platforms that could likely bypass an extended certification process. With established expertise and a long safety record in nuclear reactor certification, operations, training, and maintenance, the Naval Nuclear Propulsion Program comprises the civilian and military personnel who: . . . design, build, operate, maintain, and manage the nuclear-powered ships and the many facilities that support the U.S. nuclear-powered naval fleet.”34 Bypassing the NRC and initiating SMR experimentation under ADM Hyman Rickover’s legacy umbrella of naval reactors could shorten the process to a reasonable level for Marine and naval installations.35

#### No link uniqueness—DOE just massively increased payments for SMRs, but it fails.

DoD Energy Blog, 2/16/11, Good Things in Small Packages:Small Reactors for Military Power Good Things in Small Packages:Small Reactors for Military Power, dodenergy.blogspot.com/2011/02/good-things-in-small-packagessmall.html

They conclude that DOD should lead the charge for small reactors to meet their own needs as well as to make sure that the US leads that industry’s development. When first written the paper mentioned that most of the technology was stymied somewhere between the drawing board and production. But there is good news in the President’s 2011 Budget for nukes. The New York Times reported that the budget contains $500 million over five years for DOE to complete two designs and secure National Regulatory Commission (NRC) approval. The reactors will be built entirely in a factory and trucked to the site, like “modular homes”. Sounds just like what Dr. Andres ordered. Only problem is that $500 million is only about half of the cost to get to NRC approval. Actual production is in the $2 billion neighborhood, and that is a pricey neighborhood. Enter Amory Lovins. Amory has often derided the cost for nuclear power as an unnecessary expenditure. His argument is that micropower is the way of the future, not big honking gigawatt nuclear power plants. Although there has been a resurgence in the interest in nuclear power, it is still difficult to find private investments willing to underwrite the expense. Maybe the development of small nukes for national security reasons will lead to cost effective small nukes for distributed micropower nationwide. Small reactors for FOBs are more problematic. Even Bagram only needs about 25 MW with other FOBS being smaller. Security will be the first concern. If someone tries a smash and grab at Fort Hood they have to go through a couple of armored divisions and have a long way to got to get away. Kabul to Peshawar is only 128 miles. Cost shouldn’t be an overriding factor in considering secure power, but even at a 75% cost reduction in production, half a billion for 25MW is a bit much. Of course if you could produce a 300MW system, Bagram could air condition Kabul! The real soft power. My buddy, T.C. the fighter pilot, would tell you that DOD's mission is to fight and win the Nation's wars, not spark business recovery. DOD needs to focus on conserving energy. “Reducing the consumption at Miramar by 50% might save a lot of fuel and money, but I'd rather reduce consumption by 50% at PB Jugroom eve./in though the savings in gallons and dollars are tiny.” Reducing demand reduces risk. All that being said, it may well be worth DOE and DOD efforts to explore the potential. It is something that may be beyond the means of commercial entities, but not government (See China). If there is going to be a market here, let us not be left behind as we have been with other alternative energy production means.

#### DOD is key to commercialization.

Marqusee 12

(Jeffrey, Executive Director of the Strategic Environmental Research and Development Program (SERDP) and the Environmental Security Technology Certification Program (ESTCP) at the Department of Defense, “Military Installations and Energy Technology Innovation”, March, http://bipartisanpolicy.org/sites/default/files/Energy%20Innovation%20at%20DoD.pdf)

The key reason that DoD cannot passively rely on the private sector to provide a suite of new, cost-effective energy technologies is the difficulty of the transition from research and development to full deployment. Many have noted this challenge; it is often described as the “Valley of Death,” a term widely used in the early and mid-1990s to describe the obstacles to commercialization and deployment of environmental technologies. DoD’s environmental technology demonstration program, the Environmental Security Technology Certification Program (ESTCP), was created to overcome that hurdle. Why can’t DoD rely on the Department of Energy (DOE) to solve the commercialization and deployment problem? DOE has a mixed record in this area. Reasons for past failures at DOE are: 1) the lack of a market within DOE for the technologies; 2) overly optimistic engineering estimates; 3) lack of attention to potential economic or market failures; 4) a disconnect between business practices at DOE and commercial practices, which leads to demonstration results that are not credible in the private sector; and 5) programs completely driven by a technology “push,” rather than a mix of technology push and market-driven pull.81 Many of these issues can be viewed as arising from the first: the lack of a market within DOE. Since DOE is neither the ultimate supplier nor buyer of these technologies at the deployment scale, it is not surprising that there are challenges in creating a system that can bring technologies across the Valley of Death. DoD’s market size allows it to play a critical role in overcoming this challenge for the energy technologies the department’s installations require, as it has for environmental technologies. In addressing the barriers energy technologies face, and understanding the role DoD installations can play, it is important to understand the type and character of technologies that DoD installations need. Energy technologies span a wide spectrum in costs, complexities, size, and market forces. Installation energy technologies are just a subset of the field, but one that is critical in meeting the nation’s and DoD’s energy challenges. DOE, in its recent strategic plans and quadrennial technology review, has laid out the following taxonomy (figure 3.5): It is useful to divide these energy technologies into two rough classes based on the nature of the market and the characteristics of deployment decisions. There are technologies whose capital costs at full scale are very high, for which a modest number of players will play a key role in implementation decisions. Examples include utility-scale energy generation, large-scale carbon sequestration, commercial production of alternative fuels, nextgeneration utility-grid-level technologies, and manufacturing of new transportation platforms. Some of these technologies produce products (e.g., fuel and power from the local utility) that DoD installations buy as commodities, but DoD does not expect to buy the underlying technology. A second but no less important class of energy technologies are those that will be widely distributed upon implementation, and the decisions to deploy them at scale will be made by thousands, if not millions, of decision makers. These include: 1) Technologies to support improved energy efficiency and conservation in buildings; 2) Local renewable or distributed energy generation; and 3) Local energy control and management technologies. Decisions on implementing these technologies will be made in a distributed sense and involve tens of thousands of individual decision makers if they are ever to reach large-scale deployment. These are the energy technologies that DoD installations will be buying, either directly through appropriated funds or in partnership with third-party financing through mechanisms such as Energy Saving Performance Contracts (ESPCs) or Power Purchase Agreements (PPAs). In the DOE taxonomy shown above, these distributed installation energy technologies cover the demand space on building and industrial efficiency, portions of the supply space for clean electricity when restricted to distributed generation scale, and a critical portion in the middle where microgrids and their relationship to energy storage and electric vehicles reside.

# 2AC

## DOD

#### Pursuit of hegemony’s locked-in

Zach Dorfman 12, assistant editor of Ethics and International Affairs, the journal of the Carnegie Council, and co-editor of the Montreal Review, “What We Talk About When We Talk About Isolationism”, May 18, http://dissentmagazine.org/online.php?id=605

The rise of China notwithstanding, the United States remains the world’s sole superpower. Its military (and, to a considerable extent, political) hegemony extends not just over North America or even the Western hemisphere, but also Europe, large swaths of Asia, and Africa. Its interests are global; nothing is outside its potential sphere of influence. There are an estimated 660 to 900 American military bases in roughly forty countries worldwide, although figures on the matter are notoriously difficult to ascertain, largely because of subterfuge on the part of the military. According to official data there are active-duty U.S. military personnel in 148 countries, or over 75 percent of the world’s states. The United States checks Russian power in Europe and Chinese power in South Korea and Japan and Iranian power in Iraq, Afghanistan, and Turkey. In order to maintain a frigid peace between Israel and Egypt, the American government hands the former $2.7 billion in military aid every year, and the latter $1.3 billion. It also gives Pakistan more than $400 million dollars in military aid annually (not including counterinsurgency operations, which would drive the total far higher), Jordan roughly $200 million, and Colombia over $55 million. U.S. long-term military commitments are also manifold. It is one of the five permanent members of the UN Security Council, the only institution legally permitted to sanction the use of force to combat “threats to international peace and security.” In 1949 the United States helped found NATO, the first peacetime military alliance extending beyond North and South America in U.S. history, which now has twenty-eight member states. The United States also has a trilateral defense treaty with Australia and New Zealand, and bilateral mutual defense treaties with Japan, Taiwan, the Philippines, and South Korea. It is this sort of reach that led Madeleine Albright to call the United States the sole “indispensible power” on the world stage. The idea that global military dominance and political hegemony is in the U.S. national interest—and the world’s interest—is generally taken for granted domestically. Opposition to it is limited to the libertarian Right and anti-imperialist Left, both groups on the margins of mainstream political discourse. Today, American supremacy is assumed rather than argued for: in an age of tremendous political division, it is a bipartisan first principle of foreign policy, a presupposition. In this area at least, one wishes for a little less agreement. In Promise and Peril: America at the Dawn of a Global Age, Christopher McKnight Nichols provides an erudite account of a period before such a consensus existed, when ideas about America’s role on the world stage were fundamentally contested. As this year’s presidential election approaches, each side will portray the difference between the candidates’ positions on foreign policy as immense. Revisiting Promise and Peril shows us just how narrow the American worldview has become, and how our public discourse has become narrower still. Nichols focuses on the years between 1890 and 1940, during America’s initial ascent as a global power. He gives special attention to the formative debates surrounding the Spanish-American War, U.S. entry into the First World War, and potential U.S. membership in the League of Nations—debates that were constitutive of larger battles over the nature of American society and its fragile political institutions and freedoms. During this period, foreign and domestic policy were often linked as part of a cohesive political vision for the country. Nichols illustrates this through intellectual profiles of some of the period’s most influential figures, including senators Henry Cabot Lodge and William Borah, socialist leader Eugene Debs, philosopher and psychologist William James, journalist Randolph Bourne, and the peace activist Emily Balch. Each of them interpreted isolationism and internationalism in distinct ways, sometimes deploying the concepts more for rhetorical purposes than as cornerstones of a particular worldview. Today, isolationism is often portrayed as intellectually bankrupt, a redoubt for idealists, nationalists, xenophobes, and fools. Yet the term now used as a political epithet has deep roots in American political culture. Isolationist principles can be traced back to George Washington’s farewell address, during which he urged his countrymen to steer clear of “foreign entanglements” while actively seeking nonbinding commercial ties. (Whether economic commitments do in fact entail political commitments is another matter.) Thomas Jefferson echoed this sentiment when he urged for “commerce with all nations, [and] alliance with none.” Even the Monroe Doctrine, in which the United States declared itself the regional hegemon and demanded noninterference from European states in the Western hemisphere, was often viewed as a means of isolating the United States from Europe and its messy alliance system. In Nichols’s telling, however, modern isolationism was born from the debates surrounding the Spanish-American War and the U.S. annexation of the Philippines. Here isolationism began to take on a much more explicitly anti-imperialist bent. Progressive isolationists such as William James found U.S. policy in the Philippines—which it had “liberated” from Spanish rule just to fight a bloody counterinsurgency against Philippine nationalists—anathema to American democratic traditions and ideas about national self-determination. As Promise and Peril shows, however, “cosmopolitan isolationists” like James never called for “cultural, economic, or complete political separation from the rest of the world.” Rather, they wanted the United States to engage with other nations peacefully and without pretensions of domination. They saw the United States as a potential force for good in the world, but they also placed great value on neutrality and non-entanglement, and wanted America to focus on creating a more just domestic order. James’s anti-imperialism was directly related to his fear of the effects of “bigness.” He argued forcefully against all concentrations of power, especially those between business, political, and military interests. He knew that such vested interests would grow larger and more difficult to control if America became an overseas empire. Others, such as “isolationist imperialist” Henry Cabot Lodge, the powerful senator from Massachusetts, argued that fighting the Spanish-American War and annexing the Philippines were isolationist actions to their core. First, banishing the Spanish from the Caribbean comported with the Monroe Doctrine; second, adding colonies such as the Philippines would lead to greater economic growth without exposing the United States to the vicissitudes of outside trade. Prior to the Spanish-American War, many feared that the American economy’s rapid growth would lead to a surplus of domestic goods and cause an economic disaster. New markets needed to be opened, and the best way to do so was to dominate a given market—that is, a country—politically. Lodge’s defense of this “large policy” was public and, by today’s standards, quite bald. Other proponents of this policy included Teddy Roosevelt (who also believed that war was good for the national character) and a significant portion of the business class. For Lodge and Roosevelt, “isolationism” meant what is commonly referred to today as “unilateralism”: the ability for the United States to do what it wants, when it wants. Other “isolationists” espoused principles that we would today call internationalist. Randolph Bourne, a precocious journalist working for the New Republic, passionately opposed American entry into the First World War, much to the detriment of his writing career. He argued that hypernationalism would cause lasting damage to the American social fabric. He was especially repulsed by wartime campaigns to Americanize immigrants. Bourne instead envisioned a “transnational America”: a place that, because of its distinct cultural and political traditions and ethnic diversity, could become an example to the rest of the world. Its respect for plurality at home could influence other countries by example, but also by allowing it to mediate international disputes without becoming a party to them. Bourne wanted an America fully engaged with the world, but not embroiled in military conflicts or alliances. This was also the case for William Borah, the progressive Republican senator from Idaho. Borah was an agrarian populist and something of a Jeffersonian: he believed axiomatically in local democracy and rejected many forms of federal encroachment. He was opposed to extensive immigration, but not “anti-immigrant.” Borah thought that America was strengthened by its complex ethnic makeup and that an imbalance tilted toward one group or another would have deleterious effects. But it is his famously isolationist foreign policy views for which Borah is best known. As Nichols writes: He was consistent in an anti-imperialist stance against U.S. domination abroad; yet he was ambivalent in cases involving what he saw as involving obvious national interest….He also without fail argued that any open-ended military alliances were to be avoided at all costs, while arguing that to minimize war abroad as well as conflict at home should always be a top priority for American politicians. Borah thus cautiously supported entry into the First World War on national interest grounds, but also led a group of senators known as “the irreconcilables” in their successful effort to prevent U.S. entry into the League of Nations. His paramount concern was the collective security agreement in the organization’s charter: he would not assent to a treaty that stipulated that the United States would be obligated to intervene in wars between distant powers where the country had no serious interest at stake. Borah possessed an alternative vision for a more just and pacific international order. Less than a decade after he helped scuttle American accession to the League, he helped pass the Kellogg-Briand Pact (1928) in a nearly unanimous Senate vote. More than sixty states eventually became party to the pact, which outlawed war between its signatories and required them to settle their disputes through peaceful means. Today, realists sneer at the idealism of Kellogg-Briand, but the Senate was aware of the pact’s limitations and carved out clear exceptions for cases of national defense. Some supporters believed that, if nothing else, the law would help strengthen an emerging international norm against war. (Given what followed, this seems like a sad exercise in wish-fulfillment.) Unlike the League of Nations charter, the treaty faced almost no opposition from the isolationist bloc in the Senate, since it did not require the United States to enter into a collective security agreement or abrogate its sovereignty. This was a kind of internationalism Borah and his irreconcilables could proudly support. The United States today looks very different from the country in which Borah, let alone William James, lived, both domestically (where political and civil freedoms have been extended to women, African Americans, and gays and lesbians) and internationally (with its leading role in many global institutions). But different strains of isolationism persist. Newt Gingrich has argued for a policy of total “energy independence” (in other words, domestic drilling) while fulminating against President Obama for “bowing” to the Saudi king. While recently driving through an agricultural region of rural Colorado, I saw a giant roadside billboard calling for American withdrawal from the UN. Yet in the last decade, the Republican Party, with the partial exception of its Ron Paul/libertarian faction, has veered into such a belligerent unilateralism that its graybeards—one of whom, Senator Richard Lugar of Indiana, just lost a primary to a far-right challenger partly because of his reasonableness on foreign affairs—were barely able to ensure Senate ratification of a key nuclear arms reduction treaty with Russia. Many of these same people desire a unilateral war with Iran. And it isn’t just Republicans. Drone attacks have intensified in Yemen, Pakistan, and elsewhere under the Obama administration. Massive troop deployments continue unabated. We spend over $600 billion dollars a year on our military budget; the next largest is China’s, at “only” around $100 billion. Administrations come and go, but the national security state appears here to stay.

## TO DA

#### No risk of Asia war – Peaceful China and multilateral institutions

Bitzinger and Desker, 9

[Richard, Senior Fellow at the S. Rajaratnam School of International Studies, Barry, Dean of the S. Rajaratnam School of International Studies and Director of the Institute of Defense and Strategic Studies, Nanyang Technological University, Singapore, “ Why East Asian War is Unlikely,” Survival | vol. 50 no. 6 | December 2008–January 2009

The Asia-Pacific region can be regarded as a zone of both relative insecurity and strategic stability. It contains some of the world’s most significant flashpoints – the Korean peninsula, the Taiwan Strait, the Siachen Glacier – where tensions between nations could escalate to the point of major war. It is replete with unresolved border issues; is a breeding ground for transnational terrorism and the site of many terrorist activities (the Bali bombings, the Manila superferry bombing); and contains overlapping claims for maritime territories (the Spratly Islands, the Senkaku/Diaoyu Islands) with considerable actual or potential wealth in resources such as oil, gas and fisheries. Finally, the Asia-Pacific is an area of strategic significance with many key sea lines of communication and important chokepoints. Yet despite all these potential crucibles of conflict, the Asia-Pacific, if not an area of serenity and calm, is certainly more stable than one might expect. To be sure, there are separatist movements and internal struggles, particularly with insurgencies, as in Thailand, the Philippines and Tibet. Since the resolution of the East Timor crisis, however, the region has been relatively free of open armed warfare. Separatism remains a challenge, but the break-up of states is unlikely. Terrorism is a nuisance, but its impact is contained. The North Korean nuclear issue, while not fully resolved, is at least moving toward a conclusion with the likely denuclearisation of the peninsula. Tensions between China and Taiwan, while always just beneath the surface, seem unlikely to erupt in open conflict any time soon, especially given recent Kuomintang Party victories in Taiwan and efforts by Taiwan and China to re-open informal channels of consultation as well as institutional relationships between organisations responsible for cross-strait relations. And while in Asia there is no strong supranational political entity like the European Union, there are many multilateral organisations and international initiatives dedicated to enhancing peace and stability, including the Asia-Pacific Economic Cooperation (APEC) forum, the Proliferation Security Initiative and the Shanghai Co-operation Organisation. In Southeast Asia, countries are united in a common geopolitical and economic organisation – the Association of Southeast Asian Nations (ASEAN) – which is dedicated to peaceful economic, social and cultural development, and to the promotion of regional peace and stability. ASEAN has played a key role in conceiving and establishing broader regional institutions such as the East Asian Summit, ASEAN+3 (China, Japan and South Korea) and the ASEAN Regional Forum. All this suggests that war in Asia – while not inconceivable – is unlikely. This is not to say that the region will not undergo significant changes. The rise of China constitutes perhaps the most significant challenge to regional security and stability – and, from Washington’s vantage point, to American hegemony in the Asia-Pacific. The United States increasingly sees China as its key peer challenger in Asia: China was singled out in the 2006 Quadrennial Defense Review as having, among the ‘major and emerging powers … the greatest potential to compete militarily with the United States’.1 Although the United States has been the hegemon in the Asia-Pacific since the end of the Second World War, it will probably not remain so over the next 25 years. A rising China will present a critical foreign-policy challenge, in some ways more difficult than that posed by the Soviet Union during the Cold War.2 While the Soviet Union was a political and strategic competitor, China will be a formidable political, strategic and economic competitor. This development will lead to profound changes in the strategic environment of the Asia-Pacific. Still, the rise of China does not automatically mean that conflict is more likely; the emergence of a more assertive China does not mean a more aggressive China. While Beijing is increasingly prone to push its own agenda, defend its interests, engage in more nationalistic – even chauvinistic – behaviour (witness the Olympic torch counter-protests), and seek to displace the United States as the regional hegemon, this does not necessarily translate into an expansionist or warlike China. If anything, Beijing appears content to press its claims peacefully (if forcefully) through existing avenues and institutions of international relations, particularly by co-opting these to meet its own purposes. This ‘soft power’ process can be described as an emerging ‘Beijing Consensus’ in regional international affairs. Moreover, when the Chinese military build-up is examined closely, it is clear that the country’s war machine, while certainly worth taking seriously, is not quite as threatening as some might argue.

#### No up-front appropriations

DOE 11,

“Funding Federal Energy and Water Projects”, July, http://www.nrel.gov/docs/fy11osti/52085.pdf

On-site renewable PPAs allow Federal agencies to fund on-site renewable energy projects with no upfront capital costs incurred. A developer installs a renewable energy system on agency property under an agreement that the agency will purchase the power generated by the system. The agency pays for the system through these power purchase payments over the life of the contract. After installation, the developer owns, operates, and maintains the system for the life of the contract. The PPA price is typically determined through a competitive procurement process.

#### Massive military renewables program now

Colman ‘12

Zack Colman, The Hill, 8/7/12, White House to seek $7B in green energy contracts for military, thehill.com/blogs/e2-wire/e2-wire/242593-army-announces-renewable-energy-contracts-as-white-house-continues-green-push

The White House announced Tuesday it is inviting contract proposals from green energy firms to boost the Army’s use of renewable energy. The administration is making $7 billion available for the U.S. Army Corps of Engineers to spend on locally-generated biomass, geothermal, solar or wind energy for up to 30 years. The move is part of a broader White House-led push to green the armed forces, over GOP opposition, which claims the efforts are a waste of taxpayer dollars. The Defense Department has set ambitious targets, aiming for renewable sources to account for 25 percent of its energy by 2025, with the Army working toward getting 1 gigawatt of power from green sources by that year. Heather Zichal, the White House deputy assistant for energy and climate change, praised the DOD’s “extraordinary work” to promote renewable energy usage, in a media call on Tuesday. She said alternative energy will reduce costs and enhance national security. Republicans, however, have pressed the White House and military to abandon some alternative energy programs. They say the efforts cost too much with budget sequestration threatening to slash the defense budget by $492 billion over 10 years. Zichal, though, said the president was fully behind the push and believed the military’s turn toward alternative energy was “operationally necessary, financially prudent and mission critical.” She also lauded the Navy’s July demonstration of its “Great Green Fleet” aircraft carrier strike group. That Pacific Rim exercise tested a fuel that combined a $26-per-gallon biofuel with conventional petroleum. On Monday, the Army, along with the Interior Department, announced it would integrate green energy electricity sources such as wind and solar at military installations. Interior and the Army said those power generators would keep the lights on should the commercial electric grid fail. The military-centric announcements are one part of a larger White House renewable energy blitz this week. Earlier Tuesday, the administration revealed it would fast-track seven solar and wind electricity projects on federal lands and also held a news conference celebrating the completion of the first wind farm on federal lands in Nevada.

#### Alt causes—

#### Cost inflation

Murdock 12

Clark Murdock, CSIS Defense and National Security Group Senior Adviser, 1/10/12, Weaker Defense Dollars, www.defensenews.com/article/20120610/DEFFEAT05/306100005/Weaker-Defense-Dollars

The White House and Capitol Hill have spent months publicly battling over the size of defense cuts, while the Defense Department faces a far greater threat from within: the prospect of not only fewer defense dollars but also weaker defense dollars. Most of the current commentary inside the Capital Beltway is focused on the $500 billion in sequestration cuts that could emerge in January, but it is the escalating cost of continuing to do business that has sapped the defense dollar’s purchasing power. The deepest level of cuts being envisioned, the dreaded sequester, only goes half as far as has been seen in every previous drawdown this century, including a drop of 43 percent after the Korean War, 33 percent after the Vietnam War and 36 percent following the Cold War. Nonetheless, senior Pentagon officials have stridently opposed these cuts, invoking epithets ranging from “mindless” and “devastating” to “catastrophic.” This reaction is likely due to the fact that the defense budget is being hollowed out by internal cost inflation. The defense budget is $300 billion larger than it was in 2001, and yet there are fewer dollars available today for buying weapons and fielding new capabilities. Indeed, increasing personnel, operations and acquisition costs have combined to form a three-headed monster that is eating away at the foundation of U.S. military superiority. Personnel and operating costs have always made up the largest portion of the budget, but they have recently ballooned to 70 percent of the total budget and are squeezing out the accounts that pay for new hardware and the development of the next generation of systems. If personnel costs are allowed to continue to grow at their current rate, they will, as Todd Harrison of the Center for Strategic and Budgetary Assessments has observed, “consume the entire defense budget by FY2039.”

#### Sequestration

Murdock 12

Clark Murdock, CSIS defense and national security group senior adviser, May 2012, Planning for a Deep Defense: Drawdown—Part I, http://csis.org/files/publication/120522_DD_Interim_Report.pdf

Although some are still in denial about the imposition of the bipartisan BCA cuts,28 the post- 9/11 drawdown will both be deeper and steeper than DoD (and its supporters) clearly hope. As discussed in Appendix B, the sequester cuts alone would reduce the defense budget by another 9 percent. Although gaming the post-November 2012 "Taxmageddon" scenario -- the end of CY2012 brings an end to the Bush tax cuts and the Obama payroll tax cut, in addition to triggering the budget deficit reduction sequester mechanism -- has become a cottage industry in Washington, the likelihood that DoD will escape further reductions seems quite small. Preventing the imposition of sequester or, more likely, lifting the sequester once it's triggered will require a "grand bargain" deal on deficit reduction that consists of entitlement cuts and tax increases (sometimes called revenue enhancements). The defense budget, which constitutes 54 percent of discretionary spending, will be part of the solution, given Democratic aversion to entitlement cuts and Republican antipathy to tax increases. Optimistic (from DoD's perspective) scenarios are for a total drawdown of $800-900B, which would be a 15-17 percent cut from the FY 2012 FYDP. Pessimistic (again from DoD's perspective) estimates run from a $1.5T decrease (28 percent) and above. This author's best guess -- $1.2-1.5T (23-28 percent) depending on how Republicans and Democrats fare in the presidential and congressional races. If President Obama wins re-election, the Democrats retain control of the Senate, and the GOP loses strength in the House, DoD is likely to take a bigger hit ($1.5T). If Republicans take the presidency and control both houses of Congress, they might prefer to exempt DoD altogether from the contraction in government spending (see footnote 28 and statements by candidate Mitt Romney), but Democratic strength in Senate (and their likely ability to prevent cloture by denying the GOP 60-vote margins) will, in the author’s view, keep DoD at the drawdown table.

## 2AC CP—AT ARPA-E

#### And implementation – licensing and dual use tech make DoD a natural fit

Hayward et al 10

Steven Hayward, AEI Resident Scholar, Mark Muro, Brookings Institute Metropolitan Policy Program, Ted Nordhaus and Michael Shellenberger, Breakthrough institute cofounders, October 2010, Post-Partisan Power, thebreakthrough.org/blog/Post-Partisan Power.pdf

In addition to reforming energy deployment subsidies and launching a new competitive deployment strategy, the nation should once again leverage the power of federal procurement to establish demanding requirements to drive innovation and improvement in new energy technologies. The DOD has a long track record of using the power of procurement to successfully drive the commercialization and improvement of new technologies, many of which later spun off into broader commercial adoption. In contrast, the DOE has no way to either procure or use energy technologies at commercial scale. The DOD should help fill this void, once again using procurement to advance a range of potential dual-use energy innovations. The Pentagon’s 2010 “Quadrennial Defense Review” prioritizes expanded DOD involvement in energy innovation—and with good reason.69 The U.S. military today uses more oil than Sweden and more electricity than Denmark. Every $10 increase in the price of oil costs the DOD more than $1 billion dollars, sapping money that should be used to equip our troops for critical missions at home and abroad.70 With fuel convoys costing both lives and money every day in Iraq and Afghanistan, questions of energy are understandably high on the list of Pentagon priorities, and a growing community of national security experts, including both active and retired generals and flag officers, has identified the development of new energy alternatives that can both reduce America’s exposure to volatile oil markets and enhance military operational capabilities as key to securing the nation’s defense.71 Congress should provide new funds necessary to secure America’s energy future and national defense, providing up to $5 billion annually (as needed) to support DOD efforts to procure, demonstrate, test, validate, and improve a suite of cutting-edge energy technologies with potential to enhance American energy security or improve the strategic and tactical capabilities of the American armed forces. Energy technologies with clear dual-use commercial and military potential well suited to DOD procurement could include: advanced biofuels, including aviation fuels; advanced solar thermal and photovoltaic power technologies; improved batteries; electric vehicles; and new, modular nuclear reactors (discussed in greater detail below). As discussed above, DOD should work closely with ARPA-E and other research initiatives in both DOD and DOE to ensure a steady flow of energy innovation geared towards military needs. Procurement contracts should require continued innovation and cost improvements from supplying firms and should be competitively awarded. New efforts should be pursued to ensure that innovative firms both large and small can participate in procurement contracts and the military can benefit from the best American innovations, no matter where they arise.72 Embrace the Potential of Nuclear — But Pursue a Portfolio A new generation of smaller, innovative nuclear reactors holds great promise in providing affordable, reliable, zero-carbon power and heat to utilities of all sizes, industrial facilities, and military bases. For decades, small reactors between one-tenth to one-twentieth the size of existing commercial nuclear plants have powered U.S. aircraft carriers and submarine fleets. New modular commercial reactor designs based on the same reliable technology are smaller, safer, and less expensive than older designs and have the potential to be affordably mass-manufactured. Such technologies also offer the possibility of greater applicability globally and could potentially represent a new high-value, export-oriented manufacturing industry for the U.S. economy. A new generation of more advanced designs may hold even greater promise for the future.73 Modular reactor designs should receive priority attention from the Departments of Energy and Defense, who can each work to research advanced reactor technologies, license and approve new commercial modular reactor designs, and procure and demonstrate small modular reactors at DOE nuclear facilities and DOD military bases.

#### DoD won’t procure

Bonvillian and Van Atta 12

William B. Bonvillian, Director of the Massachusetts Institute of Technology Washington DC Office, and Richard Van Atta, Senior Research Analyst at the Institute for Defense Analyses, former Department of Defense Special Assistant for Dual Use Technology Policy and Assistant Deputy Under Secretary for Dual Use and Commercial Programs, March 2012, Energy Innovation at the Department of Defense: Assessing the Opportunities, http://bipartisanpolicy.org/library/report/energy-innovation-department-defense-assessing-opportunities

The Remaining Technology Implementation Challenge for DARPA and ARPA-E Both DARPA and ARPA-E face a profound challenge in technology implementation. For DARPA, the Cold War era of major defense acquisition budgets is long gone, and defense “recapitalization”— replacement of the existing generation of aircraft, ships, and land vehicles with new defense platforms—is evolving at a glacial pace. Finding homes for its evolving technologies, therefore, has increasingly become a difficult task for DARPA. Because technology transition was once a relatively straightforward task for DARPA, it has not yet fully faced up to the implications of how complex it has now become. ARPA-E faces a technology transfer problem of the first magnitude: the U.S. has a very limited history of moving technology advances into and transforming CELS, including in energy. Although ARPA-E faces a long list of challenges, the problem of technology implementation is perhaps the most profound. This is because of the difficulty new energy technologies face, not only with the problem of the Valley of Death in moving from research to late-stage development, but the problem endemic to CELS of market launch—implementing technology at scale. ARPA-E has worked imaginatively to structure new elements into its model to address this problem. The models of the Strategic Environmental R&D Program (SERDP) and Environmental Security Technology Certification Program (ESTCP) from DoD, where the R&D entity directly hands off to the test bed, provides an interesting new model in the energy area for ARPA-E to consider as it focuses on technology implementation. Collaboration with these programs, which ARPA-E is actively working on, may provide a crucial new tool set. ARPA-E is not alone in facing this implementation problem; the applied agencies at DOE, led by EERE, face a similar problem, and the SERDP/ESTCP combined model of R&D-test bed-deployment offers an interesting new approach. DARPA, too, despite remarkable past successes, is not immune, as suggested above, from the implementation problem, which appears to be growing. It, too, might learn lessons and make further uses of the SERDP/ESTCP approach. In summary, implementation presents a major challenge for both agencies. DARPA needs to consider its existing portfolio of implementation support, and consider better connection to available tools (such as Mantech and the Defense Production Act, for example) for its manufacturing initiatives. ARPA-E has worked imaginatively on its implementation capabilities, but the com- plexity of its task requires it to consider additional mechanisms.

#### Can’t commercialize

Bonvillian and Van Atta 12

William B. Bonvillian, Director of the Massachusetts Institute of Technology Washington DC Office, and Richard Van Atta, Senior Research Analyst at the Institute for Defense Analyses, former Department of Defense Special Assistant for Dual Use Technology Policy and Assistant Deputy Under Secretary for Dual Use and Commercial Programs, March 2012, Energy Innovation at the Department of Defense: Assessing the Opportunities, http://bipartisanpolicy.org/library/report/energy-innovation-department-defense-assessing-opportunities

Role as first adopter/initial-market creator. DARPA has frequently undertaken a technology insertion role; in coordination with other parts of DoD it has been able to create initial markets for its new technologies, allowing the Department to serve as first technology adopter. DOE offers no comparable first market for ARPA-E technologies. Given DoD’s interest in energy technology advances, it could serve as an initial market. ARPA-E will need to develop further strategies to find first adopters and initial markets, because the lack of track records of costs and efficiencies constitutes a serious barrier to commercializing and scaling new energy technologies.

#### DoD already established its recommendations for SMR adoption

King 11

Marcus King, Ph.D., Center for Naval Analyses Project Director and Research Analyst for the Environment and Energy TeamLaVar Huntzinger, Thoi Nguyen, March 2011, Feasibility of Nuclear Power on U.S.Military Installations, www.cna.org/sites/default/files/research/Nuclear Power on Military Installations D0023932 A5.pdf

Recognizing nuclear power as a potential benefit to Department of Defense (DoD) facilities, Congress directed the DoD, in section 2845 of the National Defense Authorization Act (NDAA) of 2010, to “conduct a study to assess the feasibility of developing nuclear power plants on military installations” [12]. Specifically, the study is to consider the following topics: • Options for construction and operation • Cost estimates and the potential for life-cycle cost savings • Potential energy security advantages • Additional infrastructure costs • Effect on the quality of life of military personnel • Regulatory, state, and local concerns • Effect on operations on military installations • Potential environmental liabilities • Factors that may impact safe colocation of nuclear power plants on military installations • Other factors that bear on the feasibility of developing nuclear power plants on military installations. To meet this requirement, the office of the Deputy Under Secretary of Defense for Installations and Environment, DUSD(I&E), asked CNA to conduct this feasibility study. The CNA effort was directed by a steering group consisting of representatives from DUSD (I&E), each of the military departments, DOE, NRC, and DOE Labs. This report documents our analysis and findings.

#### AND—It recommended against being an early adopter—proves the CP can’t establish a bureaucratic consensus for the plan

King 11

Marcus King, Ph.D., Center for Naval Analyses Project Director and Research Analyst for the Environment and Energy TeamLaVar Huntzinger, Thoi Nguyen, March 2011, Feasibility of Nuclear Power on U.S.Military Installations, www.cna.org/sites/default/files/research/Nuclear Power on Military Installations D0023932 A5.pdf

The most significant risk for SMR power plants is associated with being an early adoptor of new technology. From a DoD perspective, economic feasibility depends on negotiating arrangements for the project that ensure DoD is not responsible for FOAK expenses. Having contractor owners and operators would reduce operating risks associated with being an early adoptor. If partners can’t be found who are willing to bear the FOAK and early adoptor risks then DoD should not undertake such a project. The recent MOU between DOE and DoD identifies a framework for cooperation and partnership for sharing risks associated with this type of project.

## Microgrid CP

#### Doesn’t solve regulatory confusion or cyberdefense

Daniel Sater 11, Research Fellow at Global Green USA’s Security and Sustainability Office, “Military Energy Security: Current Efforts and Future Solutions”, August, http://globalgreen.org/docs/publication-185-1.pdf

Cybersecurity remains one of the leading challenges impeding the development of a smart grid. In January 2011, the GAO published a report on the progress being made on cybersecurity as it related to smart grids71. Unfortunately, the report did not specifically address microgrids. The GAO found six challenges, however, to the development of a smart grid. The DOD is nonetheless well suited to handle the challenges listed by the GAO and the confinement of microgrids to military installations should mitigate many cybersecurity risks. The challenges listed by the GAO and the advantages of military microgrids for cybersecurity appear below. Challenge 1: Aspects of the regulatory environment may make it difficult to ensure smart grid systems’ cybersecurity. The federal government and state governments regulate electricity production and distribution. Having multiple entities produce regulations can lead to conflicting rules and thus confusion. Microgrids on military installations should avoid many of the regulatory issues the GAO found with the smart grid. The confinement of microgrids to military bases means that only the DOD will have regulatory control over them. There is precedent for states to exempt military installations from state regulations. According to a different GAO report, states often excluded military installations from their renewable energy-production goals.72 Furthermore, it is unlikely that any state government would want to get into the politically untenable battle with the Pentagon over issuing competing regulations governing military bases. Challenge 2: Utilities are focusing on regulatory compliance instead of comprehensive security. Microgrid cybersecurity will benefit from having the same entity, the DOD, issue the microgrid regulations and own the microgrids. Utilities have little incentive to invest in security measures past the bare minimum necessary for regulatory compliance. However, unlike a utility, the DOD will suffer in the event of a cybersecurity failure and thus has incentives to pursue comprehensive security. Challenge 3: The electric industry does not have an effective mechanism for sharing information on cybersecurity. Different utility companies across different states do not have a central authority analogous to that which military bases have in the Pentagon. Though there will certainly be bureaucracy, the DOD has more capacity to share information about cybersecurity and cyber-attacks than utilities. Challenge 4: Consumers are not adequately informed about the benefits, costs, and risks associated with smart grid systems. The DOD can take steps to inform all of its employees about microgrids in ways that may not be available to utilities to inform their customers. The DOD could require short classes on the benefits and risks of microgrids for all its employees and more rigorous education for its base commanders and others making decisions about grid implementation. A utility company cannot require its customers to take a class. A utility’s best option for educating its customers would be to send out information packets with monthly bills and hope that consumers read them. Challenge 5: There is a lack of security features being built into certain smart grid systems. Given the importance of the DOD’s mission and the potentially catastrophic repercussions of lax cybersecurity, the Pentagon will not take the security of its microgrids lightly, especially with the recent publication of the “Department of Defense Strategy for Operating in Cyberspace.”73 Challenge 6: The electricity industry does not have metrics for evaluating cybersecurity. The lack of evaluation metrics is a serious problem, but the DOD could instruct USCYBERCOM to create a specific set of metrics for microgrid development.

#### Plan spills over to space nuclear power.

David 12

(Leonard, has been reporting on the space industry for more than five decades. He is a winner of last year's National Space Club Press Award and a past editor-in-chief of the National Space Society's Ad Astra and Space World magazines. He has written for SPACE.com since 1999, “ Air Force Eyes Nuclear Reactors, Beamed Power for Spacecraft” 22 February 2012, http://www.space.com/14643-air-force-space-nuclear-reactors-power-beaming.html)

Work on small modular nuclear reactors on Earth is highlighted in the Air Force report: "While the implementation of such a technology should be weighed heavily against potential catastrophic outcomes, many investments into small modular reactors can be leveraged for space-based systems. As these nuclear power plants decrease in size, their utility on board space-based assets increases."

The report explains that the Air Force space systems portfolio should consider piloting small modular nuclear systems, a view previously recommended by the Air Force Scientific Advisory Board.

#### That’s key to permanent off-earth settlements.

ScienceDaily ‘9

(“'Trash Can' Nuclear Reactors Could Power Human Outpost On Moon Or Mars,” http://www.sciencedaily.com/releases/2009/10/091004020806.htm, AM)

Three recent tests at different NASA centers and a national lab have successfully demonstrated key technologies required for compact fission-based nuclear power plants for human settlements on other worlds. NASA's Marshall Space Flight Center in Huntsville, Ala., offers a one-of-a-kind test facility which, without using nuclear materials, enables engineers to simulate the nuclear power process of heat transfer from a reactor to a power converter. "The recent tests bear out that Fission surface power system could be an important source of energy for exploration on the moon and Mars," said Mike Houts, project manager for nuclear systems at Marshall. "This power system could provide an abundant source of reliable, cost-effective energy and may be used anywhere on the lunar surface." For this particular test series, the Marshall reactor simulator was linked to a Stirling engine, developed by NASA’s Glenn Research Center in Cleveland. The Stirling engine, named for 19th-century industrialist and inventor Robert Stirling, converts heat into electricity. The Marshall reactor simulator included a specialized pump, provided by the U.S. Department of Energy, and a coolant loop filled with a mixture of sodium and potassium. The coolant loop provided heat to the Stirling engine at conditions very similar to an actual fission-based surface power system. The joint testing helped resolve potential integration issues and provided information and experience needed to reduce technology risks associated with this system concept. The testing of the Stirling engine with the Marshall reactor simulator may well be a key factor in demonstrating the readiness of fission surface power technology, and could provide NASA with an efficient and robust system to produce power in the harsh environment on the moon and Mars. NASA's current plan for human space exploration is to return astronauts to the moon by 2020 on expeditions that could lead to a permanent outpost for exploring the lunar surface and testing technologies that could aid a manned mission to Mars. The space agency has been studying the feasibility of using nuclear fission power generators to support future moon bases. Engineers performed tests in recent weeks as part of a joint effort by NASA and the Department of Energy. Nuclear fission power plants work by splitting the nuclei of atoms in a sustainable, controllable reaction that releases heat, which can then be funneled through a power converter to transfer that energy into usable electricity. "A small fission-based nuclear reactor coupled with a Stirling engine could provide up to 40 kilowatts of usable energy, enough to support a moon base or Mars outpost," said Houts. That's about the same amount of power needed to supply eight houses on Earth, NASA officials have said. The test series was conducted as part of the fission-based surface power project, within NASA's Exploration Technology Development Program, which is tasked with developing advanced technologies that will enable NASA to conduct future human exploration missions, while reducing mission risk and cost.

#### Colonization solves inevitable extinction.

Matheny ‘7

(Jason, PhD Student in School of Public Health @ Johns Hopkins, Risk Analysis: An International Journal, “Reducing the Risk of Human Extinction”, 27:5, Wiley InterScience)

As for astronomical risks, to escape our sun's death, humanity will eventually need to relocate. If we survive the next century, we are likely to build self-sufficient colonies in space. We would be motivated by self-interest to do so, as asteroids, moons, and planets have valuable resources to mine, and the technological requirements for colonization are not beyond imagination (Kargel, 1994; Lewis, 1996).   Colonizing space sooner, rather than later, could reduce extinction risk (Gott, 1999; Hartmann, 1984; Leslie, 1999), as a species' survivability is closely related to the extent of its range (Hecht, 2006). Citing, in particular, the threat of new biological weapons, Stephen Hawking has said, "I don't think the human race will survive the next thousand years, unless we spread into space. There are too many accidents that can befall life on a single planet" (Highfield, 2001). Similarly, NASA Administrator, Michael Griffin (2006), recently remarked: "The history of life on Earth is the history of extinction events, and human expansion into the Solar System is, in the end, fundamentally about the survival of the species."

## 2AC Cliff—Wake

#### Decline doesn’t cause war

Morris Miller, Professor of Administration @ the University of Ottawa, ‘2K

(Interdisciplinary Science Review, v 25 n4 2000 p ingenta connect)

The question may be reformulated. Do wars spring from a popular reaction to a sudden economic crisis that exacerbates poverty and growing disparities in wealth and incomes? Perhaps one could argue, as some scholars do, that it is some dramatic event or sequence of such events leading to the exacerbation of poverty that, in turn, leads to this deplorable denouement. This exogenous factor might act as a catalyst for a violent reaction on the part of the people or on the part of the political leadership who would then possibly be tempted to seek a diversion by finding or, if need be, fabricating an enemy and setting in train the process leading to war. According to a study under- taken by Minxin Pei and Ariel Adesnik of the Carnegie Endowment for International Peace, there would not appear to be any merit in this hypothesis. After studying ninety-three episodes of economic crisis in twenty-two countries in Latin America and Asia in the years since the Second World War they concluded that:19 Much of the conventional wisdom about the political impact of economic crises may be wrong ... The severity of economic crisis – as measured in terms of inflation and negative growth – bore no relationship to the collapse of regimes ... (or, in democratic states, rarely) to an outbreak of violence ... In the cases of dictatorships and semi-democracies, the ruling elites responded to crises by increasing repression (thereby using one form of violence to abort another).

#### No impact uniqueness—stimulus package will end and government spending will decline—businesses are already reacting

Seeking Alpha 11/9/12

Investment News Site, “Even With A Fiscal Cliff Deal, Stocks And The U.S. Economy Will Unravel In 2013,” http://seekingalpha.com/article/995621-even-with-a-fiscal-cliff-deal-stocks-and-the-u-s-economy-will-unravel-in-2013, AM

Deal or no deal on the Fiscal Cliff, taxes are going higher, and the level of U.S. Government spending is going to dwindle because the nearly $1 trillion Obama stimulus package is done, and current levels of spending on defense, entitlements and other areas are also not sustainable and are poised for budget cuts. We will soon see the economic support that the Bush tax cuts, heavy government spending and the massive Obama stimulus plan provided as they evaporate and are replaced with higher tax rates and budget cuts. To get a sampling of what the combined impact of higher taxes and reduced government spending might feel like in 2013, all we have to do is take a look at Europe. Italy, Spain, Portugal and Greece have all raised taxes and cut government spending in the past couple of years, and the resulting effects have been quite devastating. It did not take long for unemployment to spike and economic weakness to set in as consumers and businesses also cut spending. We are already seeing signs of this in the United States in advance of a potential Fiscal Cliff deal as corporations become more cautious, horde cash and reduce hiring. It also looks like U.S. consumers are becoming more cautious as even companies like McDonald's (MCD) see same store sales drop for the first time in 9 years. Industrial companies like Caterpillar (CAT) have also been signaling a slowdown as it recently reduced earnings guidance for the next couple of years. Stock market The stock market is starting to reflect the realities facing the United States. The Standard & Poors 500 Index (SPY) which trades for about 14 times earnings, has begun to trade lower and currently is just slightly above the 200-day moving average. I expect it to break below that key support level in the coming weeks and months which is likely to spur additional selling pressure. This country and its economy have been driven largely by borrowed money for many years, and that party is coming to an end. While the Obama stimulus plan and postponement of budget cuts has masked and delayed the real weakness in the economy for the past couple of years, that bandage is coming off soon and investors should consider getting very defensive in advance of 2013, when the effects of rising taxes and budget cuts will bear down hard on the economy. It's time to raise cash and avoid industrial stocks like Caterpillar and General Electric (GE), which are highly sensitive to the economic cycles.

#### Ideological lock-in

Cook, writer for the National Journal, 11/8/2012

(Nancy, http://www.nationaljournal.com/magazine/to-avert-a-fiscal-cliff-catastrophe-someone-has-to-blink-20121108)

The far more likely scenario for both parties is a swan dive over the fiscal cliff. The election gave Obama some leverage, especially since the Democrats retained control of the Senate. But House Republicans also kept their majority. Both parties view the status quo as an affirmation of their power. “The president feels like his mandate from a slim margin of victory is to raise taxes,” says a Republican Senate aide privy to GOP discussions. “A razor-thin margin will not change the principles of the Republicans.” A plunge would follow weeks of behind-the-scenes negotiations, public political posturing, and pressure from outside groups—both political and business ones. And it would surely shake the nation’s confidence. But it might not be all bad. True, from an economic standpoint, it would turn deficit reduction into a de facto program of austerity, just as the unemployment rate is sinking and the economy is recovering. But from a purely political standpoint, the cliff dive would allow lawmakers to negotiate with a clean slate. Neither party likes a recession per se, but they may both dislike one less than they dislike surrendering their entrenched tax positions.

#### Tea party blocks

Michael Mathes, AFP, 11/9/12, Tea Party still a force, despite some losses, www.google.com/hostednews/afp/article/ALeqM5ghHKvO-nUR1ZzCDsfpdTFVr4I2FQ?docId=CNG.f123008f7575a156fb9c945fe5b10c48.6f1

Despite a handful of high-profile losses by Tea Party-backed candidates, the anti-tax, small-government movement solidified its imprint in the US Congress, with the bulk of its lawmakers re-elected. Some Democrats took Tuesday's election -- in which President Barack Obama defeated Republican Mitt Romney, increased his Senate majority and clawed back some seats in the House -- as a sign of diminished Tea Party stature two years after many candidates backed by the movement romped to victory in Congress. House Speaker John Boehner waved off potentially disruptive influences of the fiscally conservative movement in the House of Representatives as he braces for clutch negotiations with Democrats over looming challenges known as the "fiscal cliff." And he defended the group's goals as broadly consistent with those of Republicans of all stripes within the 435-member House. "All of us who were elected 2010 were supported by the Tea Party," he told ABC News on Thursday. "These are ordinary Americans who have taken a more active role in our government, they want solutions," Boehner declared, saying the Republican Party's leadership and members affiliated with the movement "all understand each other a lot better." But some experts and Tea Party leaders see a fresh clash brewing, even as the movement could be alienating voters in battlegrounds like Florida and red states like Missouri. "There will be something like a civil war within the Republican Party, with the extreme right of Tea Partyers and the Christian right on one side, and those who were formerly the GOP's mainstream on the other," Brigitte Nacos, a politics professor at Columbia University who tracks the movement, told AFP. "What is mostly at stake here is the future of the GOP" and its ability to win presidential elections and congressional majorities, she added. At least 51 of the 55 Tea Party members who ran for re-election on November 6 will return for the 113th Congress that begins in January, although there were some key defeats. Among them was Allen West, the outspoken former US Army officer and Tea Party hero for his fiery small-government stance, who recently caught criticism when he branded 80 Democrats as "members of the Communist Party." West is seeking a recount in his Florida district and has not conceded. Representative Joe Walsh also went down. And in two crucial US Senate races, Tea Party-backed candidates Todd Akin and Richard Mourdock both slumped to defeat, after each recently made comments about abortion that made them appear unsympathetic to rape victims. Some veteran conservative ideologues were re-elected to the House after tough races, notably Michele Bachmann, a founder of the Tea Party Caucus, who reportedly spent 12 times as much money as her Democratic rival but won her seat by just 3,000 votes. Jenny Beth Martin, founder of Tea Party Patriots, one of the first such groups in the nation, said that with the "catastrophic loss" of Republican establishment candidate Romney, the Tea Party is the "last best hope" for the country to adhere to its founding principles. "Our work begins again today," she said in a statement. "We will turn our attention back to Congress, to fight the battles that lie ahead including balancing the budget, repealing Obamacare, cutting the debt, holding the line on the debt ceiling, and the many other issues that will arise to threaten America." But Senator Charles Schumer, the number three Democrat in the Senate, described the Tea Party as on the "decline," with several of their candidates having to moderate their positions to win re-election after riding 2010's Tea Party wave. "Those Tea Party candidates who won, many of them ran away from the Tea Party platform," Schumer said at a Christian Science Monitor breakfast on Thursday. "They are a little bit chastened, the ones who've come back," he said, adding that their demands to repeal Obama's landmark health care law or not raise the debt ceiling will "play much less prominent" a role. Tea Party lawmakers are in no way backing off, said Jacqueline Bodnar of FreedomWorks, a grassroots group promoting fiscal conservatism. "If you look qualitatively, you're seeing much stronger fiscal conservatives who are fundamentally changing the composition of the House," Bodnar said, pointing to their focus on the very issues that make up the fiscal cliff challenges that lawmakers hope to settle in the coming months. "The debt ceiling increase was once standard protocol, and now it's a battle every single time."

#### Obama PC on grand bargain negotiations fail

The Hotline, 9/10/12, Slow and Steady Wins the Race, Lexis

Gaps in Obama's leadership contributed to the collapse of a "grand bargain" on spending and debt last year. with Obama "failing to cultivate congressional relationships that may have helped him break through GOP opposition, author Bob Woodward told ABC. Woodward: "President Clinton, President Reagan. And if you look at them, you can criticize them for lots of things. They by and large worked their will. On this, President Obama did not. Now, some people are going to say he was fighting a brick wall, the Republicans in the House and the Republicans in Congress. Others will say it's the president's job to figure out how to tear down that brick wall. In this case, he did not." Asked if Obama "simply wasn't ready for the job of being president," Woodward responded: "I am not ducking this. I am weighing evidence, and there's evidence that he got on top a lot of things, he did a lot of things. And there's evidence that there are gaps. He did not fix this." Woodward places "particular blame for the failure to reach a deal" with Obama, "writing that the seeds of discord were planted early in his administration." Woodward: "There's this divided-man quality to President Obama always. Initially he meets with the congressional leaders, he says you know, 'We're going to be accommodating, we're going to listen, we're going to talk, we're going to compromise.' But then they -- Republicans ask some questions and challenge him a little bit and he says 'Look I won. I'm in charge here.' And the Republicans feel totally isolated and ostracized. And this was the beginning of a war" (Klein, ABC, 9/10).

#### Obama not key to the cliff

Warren, Chicago editor for the Daily Beast, 11/9/2012

(James, http://www.thedailybeast.com/articles/2012/11/09/president-obama-s-hill-challenge-in-avoiding-fiscal-cliff.html)

Obama “has to change the way he operates,” argues Cook. “The White House motto seems to be ‘No New Friends,’” his allusion to the small and tight group of mostly Chicago chums with whom the president and Michelle Obama socialize.

But even longtime Washington hands are unclear how the system will resolve what a prominent Republican lobbyist calls a “three-ring policy circus” of huge automatic spending cuts due to kick in on Jan. 1; a decision on whether to extend Bush-era tax cuts; and a decision next year on raising the debt ceiling. A longer recession and higher unemployment could be in the offing if there’s no resolution.

And it may be equally unclear whether a more overtly engaged Obama would alter the bargaining landscape, given underlying political frictions in both parties—and changes in the capital’s own political and social culture.

#### No link

Appelbaum 12

Binyamin, Defense cuts would hurt scientific R&D, experts say, The New York Times, 1-8, http://hamptonroads.com/2012/01/defense-cuts-would-hurt-scientific-rd-experts-say

Sarewitz, who studies the government's role in promoting innovation, said the Defense Department had been more successful than other federal agencies because it is the main user of the innovations that it finances. The Pentagon, which spends billions each year on weapons, equipment and technology, has an unusually direct stake in the outcome of its research and development projects.¶ "The central thing that distinguishes them from other agencies is that they are the customer," Sarewitz said. "You can't pull the wool over their eyes."¶ Another factor is the Pentagon's relative insulation from politics, which has allowed it to sustain a long-term research agenda in controversial areas. No matter which party is in power, the Pentagon has continued to invest in clean-energy technology, for example, in an effort to find ways to reduce one of its largest budget items, energy costs.

#### Winners win

Marshall and Prins ‘11

(BRYAN W, Miami University and BRANDON C, University of Tennessee & Howard H. Baker, Jr. Center for Public Policy, “Power or Posturing? Policy Availability and Congressional Influence on U.S. Presidential Decisions to Use Force”, Sept, Presidential Studies Quarterly 41, no. 3)

Presidents rely heavily on Congress in converting their political capital into real policy success. Policy success not only shapes the reelection prospects of presidents, but it also builds the president’s reputation for political effectiveness and fuels the prospect for subsequent gains in political capital (Light 1982). Moreover, the president’s legislative success in foreign policy is correlated with success on the domestic front. On this point, some have largely disavowed the two-presidencies distinction while others have even argued that foreign policy has become a mere extension of domestic policy (Fleisher et al. 2000; Oldfield and Wildavsky 1989) Presidents implicitly understand that there exists a linkage between their actions in one policy area and their ability to affect another. The use of force is no exception; in promoting and protecting U.S. interests abroad, presidential decisions are made with an eye toward managing political capital at home (Fordham 2002).

#### No impact—they’ll delay timelines

Schiff, president and chief global strategist of Euro Pacific Capital, 11/10/2011

(Peter, “Going Over The Fiscal Cliff Isn't The Problem, It's The Solution,” http://www.businessinsider.com/extend-and-pretend-2012-11)

If you recall, the cliff was created by a deal last year when Congress couldn't find ways to trim the deficit in exchange for raising the debt ceiling. When they failed to reach an agreement, Congress knew they had to raise the debt ceiling anyway. The resulting Budget Control Act of 2011, signed in August of that year, offered the pretense that they were dealing with our long-term fiscal crisis and not simply raising the debt ceiling with no strings attached. This was done not only to appease some House Republicans, who had threatened to vote against a debt ceiling increase, but to satisfy the bond rating agencies that had threatened (I would choose a different word or provide a source to back this up)a down-grade if Congress failed to act.

Now the focus turns to how Congress will dismantle the structure it created just 16 months ago. There can be little doubt that they will as economists are assuring politicians that driving over the fiscal cliff will immediately bring on a recession. The expiration of the Bush era tax cuts for all taxpayers will cost Americans an estimated $423 billion in 2013 alone. Hundreds of billions of across the board spending cuts, including the military, have been delineated. No politician would allow that to happen.

It is amazing that members of Congress can keep a straight face as they claim to want to address our long-term deficit problem while simultaneously working to avoid any substantive action. No doubt an agreement will be reached that will replace the looming fiscal cliff with another one farther down the road (which they can easily dismantle before we actually reach the precipice). Will the rating agencies buy this bill of goods a second time? If we lack the political courage to go over this fiscal cliff, why should anyone think we will be able to stomach going over the next one? Especially since each time we delay going over the cliff, we simply increase its future size, making it that much harder to actually go over it.

#### Multiple issues before the cliff

Geewax, 11/7

(NPR Correspondent, After Election, Congress Turns To 'Fiscal Cliff,' Other Money Issues

http://www.northcountrypublicradio.org/news/npr/164474557/after-election-congress-turns-to-fiscal-cliff-other-money-issues

Still, they must try to get something done. The soon-to-expire Congress is set to convene Nov. 13. Very likely, comprehensive solutions to fiscal-cliff problems will have to wait for the new Congress in January. But because so many deadlines will be hit before then, the lawmakers will need to pass measures to cope with a number of other crises, and then stall for time on the edge of the cliff. For example, Superstorm Sandy may force lawmakers to take quick action to shore up the Federal Emergency Management Agency, also known as FEMA. The agency could get overwhelmed by the cost of helping people whose homes have been destroyed by flooding. And then there's the cost of rebuilding public transit systems. A large, bipartisan group of congressmen signed a letter this week, asking House leaders to prepare to spend more money for cleaning up after the storm. They wrote that "as the full brunt of Hurricane Sandy is quantified, Congress must stand ready to provide the aid and assistance to the people and communities most devastated by this storm." And then there's the debt ceiling. Last week, the Treasury Department warned that the country probably will hit its $16.4 trillion borrowing limit by the end of the year. If the U.S. were to hit the ceiling and risk default on its debts, it could trigger a second downgrade of the U.S. government's credit rating and another rattling of global financial markets. Aside from FEMA and the debt ceiling, Congress must find ways to delay the fiscal-cliff cluster of changes. Take just this one: the alternative minimum tax — the AMT, an obscure tax rule — is about to sharply increase taxes for about 27 million households, according to the Congressional Research Service. Any couple with children and an annual income of more than $75,000 could be facing a federal tax bill that is thousands of dollars higher this year. Yes. Their taxes would shoot up for the 2012 tax year. Once the filing season begins in January, retroactive fixes to the AMT become much more difficult to implement, so Congress must act before New Year's Eve. When first created in 1969, the AMT was intended to ensure that wealthy people could not use deductions to escape paying all taxes. But the tax was not adjusted for inflation, and Congress has had to regularly apply a "patch" to ensure that the AMT didn't apply to average families. But because of political gridlock, Congress didn't pass a patch this year — and now the deadline is looming. So, you've got FEMA, the debt ceiling and the AMT patch all demanding immediate action, even before turning to all of the other fiscal-cliff elements.

#### Bipart support

Christine Todd Whitman 12, CASEnergy Co-Chair, Former EPA Administrator and New Jersey Governor, “Nuclear Power Garners Bipartisan Support”, August 13, http://energy.nationaljournal.com/2012/08/finding-the-sweet-spot-biparti.php?rss=1&utm_source=feedburner&utm_medium=feed&utm_campaign=Feed%3A+njgroup-energy+%28Energy+%26+Environment+Experts--Q+with+Answer+Previews%29#2237728

The energy policy that I’ve seen garner consistent support from the left and the right over the years is also one with which I’m deeply familiar. This policy involves building a diverse portfolio of low-carbon energy sources, featuring a renewed investment in nuclear energy. And it’s not just policymakers from both sides of the aisle who support nuclear energy – it’s everyday energy consumers as well. According to a Gallup poll conducted in March of this year, nearly 60 percent of Americans support the use of nuclear energy to meet our nation’s electricity needs, and a majority support expanding America’s use of nuclear power. Next-generation nuclear energy projects are underway in Georgia, South Carolina and Tennessee, thanks in part to steady popular support, as well as support from President Obama, bipartisan congressional leaders and other policymakers at the federal and state levels. An additional 10 combined construction and operating licenses for 16 plants are under review by the Nuclear Regulatory Commission. This support is founded in the fact that nuclear energy, safely managed, provides an efficient, reliable source of energy. In fact, nuclear power is the only baseload source of carbon-free electricity. It provides nearly two-thirds of the nation’s low-carbon electricity, and will continue to be an important source of energy well into the future given the advent of innovative large and small reactor designs. The use of nuclear energy prevents more than 613 million metric tons of carbon dioxide every year – as much CO2 as is emitted by every passenger car in America. Bipartisan support for nuclear energy also stems from the boost that it provides to local job markets and to local and state economies. As nuclear energy expands and as more than half of the industry workforce approaches retirement, the industry offers growing opportunities for well-paying careers. The industry already supports more than 100,000 jobs, and the combination of retirements and the construction of new facilities could create as many as 25,000 new jobs in the near term. What’s more, the construction of a nuclear facility spurs the creation of other local jobs in industries ranging from manufacturing to hospitality. The industry generates between $40 and $50 billion in revenue and electricity sales, or some $470 million in total economic output and $40 million in labor wages at each U.S. facility every year. That’s a powerful economic engine and a positive impact that leaders are embracing. As America refocuses on cleaner energy policies that help boost our economy, nuclear power is becoming a clear and critical part of a secure, sustainable energy portfolio. We need electricity and we want clean air; with nuclear energy we can have both. It’s a source of power that leaders on both sides of the aisle can support.

# 1AR

## AT Backup Generators

Generators are too short-term

Andres 11

Richard B. Andres, Energy Security Chair, Institute for National Strategic Studies Professor of National Security Strategy, National War College, National Defense University, October 4, 2011, "SECURE GRID ‘11", http://www.ndu.edu/inss/docuploaded/Secure%20Grid%20'11%20After-Action%20Report.pdf

The Military – According to USNORTHCOM, its bases at the installation level are not normally provided real time advance warning of an impending GMD. Certain missions directly impacted by space weather do currently receive forecasts and warnings. However, notice to installations to ensure readiness of the support infrastructure may be necessary as well. It is essential that bases hosting critical missions have sufficient electrical power to sustain independent continuous operations even if the surrounding commercial power grid is lost. Though many installations possess diesel‐powered electrical generators, they have limited diesel fuel storage. In the event of a widespread grid outage, fuel supplies could dwindle rapidly, thereby impacting the ability of installations to conduct primary missions.

#### They don’t last – empirics

Annie Snider 12, E&E reporter, “Pentagon still can't define 'energy security,' much less achieve it”, January 16, http://www.eenews.net/public/Greenwire/2012/01/16/1

Hurricane Katrina humbled U.S. military bases in 2005, cutting power at air towers, training facilities and command centers just as it did everywhere else along the Gulf Coast. The Naval Construction Battalion Center in Gulfport, Miss., for example, a staging ground for regional relief operations after the storm, needed relief itself after running for two weeks on backup power systems. And Keesler Air Force Base near Biloxi, Miss., lost its airfield lights and had to scramble to keep its hospital running after a generator was swamped. While diesel generators kept critical missions going during Katrina, the storm provided a wakeup call for Pentagon leaders concerned about terror attacks on the electric grid, which provides 99 percent of the energy that bases consume. Could bases withstand a power outage that outlasts their three-to-seven-days' supply of diesel for backup systems? Is it wise for the military to rely on the same power plants and transmission lines that feed homes and businesses? A terrorist attack that caused a long-term grid disruption "could significantly affect our military forces globally -- potentially blinding them, neutering their command and control, degrading their mobility and isolating them from their principal sources of logistics support," Paul Stockton, the Pentagon's assistant secretary for homeland defense, wrote recently in the online journal Homeland Security Affairs. A board of outside experts tasked by the Department of Defense to study the issue found in a 2008 report that there are significant gaps in DOD's ability to prevent and respond to major electrical outages. "Critical national security and homeland defense missions are at an unacceptably high risk of extended outages from failure of the grid," the Defense Science Board concluded. "The grid is fragile, vulnerable, near its capacity limit, and outside of DOD control. In most cases, neither the grid nor on-base backup power provides sufficient reliability to ensure continuity of critical national priority functions and oversight of strategic missions in the face of long-term (several months) outage." And while the Pentagon has joined interagency efforts to beef up grid security, experts say solutions remain elusive. Four years after the Defense Science Board report, DOD has yet to define what "energy security" means at its bases, let alone how to assure it, according to dozens of interviews with military officials, lawmakers, defense energy experts, project developers and utilities. How DOD ultimately answers these questions will not only determine the limits of U.S. defenses; it is also likely to send waves through civilian energy and technology industries.

## Uniqueness overwhelms

#### Multiple other things Obama does should overwhelm the link

World Outline, postgraduate student in international affairs at King’s College, 1/24/2012

[“How valuable is multilateral diplomacy in a post-9/11 world?,” http://worldoutline.wordpress.com/2012/01/24/how-valuable-is-multilateral-diplomacy-in-a-post-911-world/]

At the turn of the last century, 189 world leaders convened at the Millennium Summit and approved the Millennium Declaration which outlined eight specific goals that the United Nations was to achieve by 2015.[4] Yet, just a year later the 9/11 terrorist attacks tilted the world upon its head. The Security Council was rallied into action after the attacks and unanimously backed the United States against the threat which had caused so much devastation.[5] However, a wounded United States became increasingly relentless and unilateral in their ‘War on Terror’; when the Security Council refused to authorise a US attack upon an allegedly nuclear-armed Iraq, the United States, led by George. W. Bush, launched the assault anyway without UN approval.[6] This has been referred to as the ‘crisis of multilateralism’, as the United States undermined the very institution of which it is the biggest financial contributor and the most influential player.[7] If the founding member of the UN was refusing to follow the guidelines of the institution then why should other states follow the rules? This act set a worrying precedent for the rest of the world and, as Kofi Annan asserted, ‘undermined confidence in the possibility of collective responses to our common problems’.[8] Other instances of American unilateralism are Bush’s abstention from the Human Rights Council, his refusal to sign the Kyoto Protocol and the US departure from the Comprehensive Test Ban Treaty. The United States was losing sight of the benefits that multilateral diplomacy has to offer. However, the arrival of Barack Obama at the Oval Office has revived multilateral values within US foreign policy. The Obama administration has realised that it must now engage with the UN and this has marked a ‘transitional moment in the history of multilateralism’.[9] In his 2010 National Security Strategy, Obama acknowledged the fact that the US had been successful after the Second World War by pursuing their interests within multilateral forums such as the United Nations and not outside of them.[10] The global financial crisis of 2008 and the European Union’s sovereign debt crisis have demonstrated just how interdependent the economies of the western world are and these crises have created an age of austerity in which multilateralism is needed more than ever before.[11] The US has overstretched its resources and is now currently winding down two wars in Afghanistan and Iraq; they have realised that they simply do not have the means to conduct their foreign affairs exclusively anymore. Clear indications of Washington’s improved multilateral engagement with the UN since Obama’s inauguration, and the changing attitude in US foreign policy, are the economic sanctions negotiated over Iran, Obama’s decision for the US to join the Human Rights Council and, more specifically, its participation in the recent Libya mission. In Libya, the US provided support for the mission, yet played a subdued role in the campaign, allowing its European counterparts to take the lead. In contrast to his predecessor, Obama is displaying pragmatism rather than sentimentalism in his search for partners, making alliances in order to adapt to the emerging multipolar world; this is typified by Obama’s recent visit to the Asia-Pacific and his tour of South America (Brazil, Chile and El Salvador) in 2010. For the time being, US unipolarity looks to be a thing of the past; its foreign policy is changing from Bush’s unilateralism at the start of the century to a more multilateral approach at the beginning of a new decade under Obama.[12] This is the correct precedent that the most powerful nation in the world should be setting for other states to follow. The fact that the US is now engaging with the UN to counter global problems has restored the credibility that the UN had lost after the Iraq debacle and, by setting this example, other nations will follow suit and the international community as a whole can only benefit. From this change in US foreign policy, it is clear that multilateral diplomacy is of more value today than it was a decade ago.

## AT: Cred

#### Credibility is determined by capability

Press 5

Daryl Press, Associate Professor of Government | Dartmouth College, Calculating credibility:

how leaders assess military threats. Google Books

In international politics credibility is a prized asset. A country whose prom-an build valuable alliances because potential allies will not abandonment. A country whose threats are credible can deter many enemies and prevent costly wars rather than fight them. Every country strives to make its threats and promises credible, but how is this done? What causes credibility? Statesmen, scholars, and pundits believe they know how credibility is won and lost. The conventional wisdom holds that credibility depends on a country's past behavior—its history of keeping or breaking commitments. Like people who keep their word, countries that keep their promises will be believed when they issue new assurances. And like people who casually break their promises, countries that renege on their commitments soon discover that their promises carry no weight. In international politics, it seems, countries must keep their promises and carry out their threats to preserve their credibility, even if doing so exacts serious costs in the short term. This book argues that the conventional wisdom about credibility is wrong. A country's credibility, at least during crises, is driven not by its past behavior but rather by power and interests, if a country makes threats that it has the power to carry out—and an interest in doing so—those threats will be believed even if the country has bluffed in the past. If it makes threats that it lacks the power to carry out—or has no interest in doing so—its credibility will be viewed with great skepticism. When assessing credibility during crises, leaders focus on the "here and now/' not on their adversary's past behavior. Tragically, those countries that have fought wars to build a reputation for resolve have wasted vast sums of money and, much worse, thousands of lives. Evidence shows that presidents, prime ministers, and dictators believe the conventional wisdom about the sources of credibility. As a result countries have paid dearly to "invest" in reputation. Nowhere has this reasoning played a more influential role than in the past fifty years of U.S. foreign policy. The Cold War had just begun when the Truman administration intervened in the Korean War to protect America's credibility. As Secretary of State John Foster Dulles explained: "To sit by while Korea is overrun by unprovoked armed attack... would start [a] disastrous chain of events leading most probably to world war." The president clarified this reasoning in a radio address to the American public: "If aggression were allowed to succeed in Korea, it would be an open invitation to new acts of aggression elsewhere."' Evidence shows that presidents, prime ministers, and dictators believe the conventional wisdom about the sources of credibility. As a result countries have paid dearly to "invest" in reputation. Nowhere has this reasoning played a more influential role than in the past fifty years of U.S. foreign policy. The Cold War had just begun when the Truman administration intervened in the Korean War to protect America's credibility. As Secretary of State John Foster Dulles explained: "To sit by while Korea is overrun by unprovoked armed attack... would start [a] disastrous chain of events leading most probably to world war." The president clarified this reasoning in a radio address to the American public: "If aggression were allowed to succeed in Korea, it would be an open invitation to new acts of aggression elsewhere." Fifteen years later American officials made the same arguments for intervention in Vietnam. Secretary of State Dean Rusk explained in 1965 why vital U.S. interests were at stake in Southeast Asia: "The integrity of the U.S. principal pillar of peace throughout the world. If that "CToarwrT dim-rrom n \ncs unreliable, the communist world would draw con-lead to our ruin and almost certainly to a catastrophic war. That same year President Lyndon Johnson echoed Rusk's reasoning: "To leave Viet-Nam to its fate would shake... confidence ... in the value of an American commitment and in the value of America's word." Years later, after the war had clearly become a quagmire, President Richard Nixon warned Americans that it would be dangerous to abandon South Vietnam because "the cause of peace might not survive the damage that would be done to other nations' confidence in our reliability."2 Even after suffering through the tragedy of Vietnam, America's leaders remained concerned that any signs of irresolution would weaken U.S. credibility. In 1983 President Ronald Reagan cautioned that the United States could not let Communists come to power in Latin America or else "our credibility will collapse and our alliances would crumble."3 Concern for protecting America's reputation for resolve remains strong in the post-Cold War era. When Iraq invaded Kuwait in August 1990, President George H. W. Bush cautioned that America's credibility was at stake: a failure to defend Kuwait, the president warned, "would be a signal to actual ' and potential despots around the world" that they could swallow their neighbors without fear of the United States.4 Former president Nixon agreed, arguing that both U.S. and UN credibility were on the line: "If we fail to roll back (Saddam Hussein's) aggression ... no potential aggressor in the future will be deterred by warnings from the U.S. or by UN resolutions."5 Americas leaders and pundits also claimed that civil wars in Bosnia and Somalia put American credibility at stake.6 And when, in 1999, Serbia escalated its brutalities against Kosovar Albanians in defiance of NATO's warn- Introduction Defense William Cohen announced thai the stakes fo nd the obvious humanitarian issues: he declared tha "NATO's credibility [is] on the line." Former secretary of state Lawrence Ea gleburger put it most clearly: NATO could not afford to fail in Kosovo be cause "our credibility must be preserved or all the would-be Milosevic around the world will believe that they, too, can kill and maim with im pun it y."7 Each of these claims—from the Korean War through the post-Cold Wa period—rests on an idea, which I call "Past Actions" theory, that tomor row's enemies will assess America's credibility on the basis of U.S. action today. This theory is widely believed. But is it true? This book tests the conventional wisdom against a competing argument about the sources of credibility. The "Current Calculus" theory posits that decisionmakers assess the credibility of their adversaries' threats by evaluating the balance of power and interests—and not the adversaries' history for keeping or breaking commitments. When decisionmakers face a threat, they ask themselves a few simple and intuitive questions. They wonder: Does the enemy have an interest in carrying out his threat? Does he have the power to do it? And—bringing together power and interests—are the enemy's interests sufficient to justify the costs that he will have to pay by carrying out his threat? If he can do what he threatens with relatively low costs, the adversary's threats will be credible. Otherwise his threats will seem empty.

In contrast with Past Actions theory—which envisions leaders assessing credibility by peering into the past—Current Calculus theory posits that decisionmakers treat crises as if they were sui generis. If Current Calculus theory is correct, then countries do not need to take costly actions (such as fighting wars) to protect their future credibility. Future commitments will be credible if—and only if—they are backed up by sufficient strength and connected to weighty interests

#### *******THIS IS NOT A STRAW PERSON – PRESS IS THE AUTHOR OF “Calculating credibility: how leaders assess military threats” ---- REFERENCES TO THIS BOOK ARE THUS REFERENCES TO HIS OWN ARGUMENT

## AT: Nuclear solves now

#### Even if plant numbers are increasing, the share of generation will decrease

Tirone 9/19/12

Jonathan, Associated Press, “Nuclear Power Production Set to Grow Even After Japan Phase-Out (Vienna),” http://www.northjersey.com/news/international/170334006_Nuclear_Power_Production_Set_to_Grow_Even_After_Japan_Phase-Out__Vienna_.html?page=all, AM*Agency=IAEA

The total share of nuclear power input to the electrical grid will fall to 10.4 percent in 2030 from 13.8 percent in 2010, according to the agency's most pessimistic scenario.

## AT uranium shortage

#### No shortage–most qualified ev

NEI ‘12

Nuclear Energy Institute, “Myths & Facts About Nuclear Energy”, June, http://www.nei.org/resourcesandstats/documentlibrary/reliableandaffordableenergy/factsheet/myths--facts-about-nuclear-energy-january-2012/

Fact: Readily available uranium resources (5.5 million metric tons) will last at least 100 years at today’s consumption rate, according to the World Nuclear Association and the Nuclear Energy Agency of the Organization for Economic Cooperation and Development. An estimated additional 10.5 million metric tons that remain untapped will expand the available supply to at least 200 years at today’s consumption rate. The agency also determined that further exploration and improvements in extraction technology are likely to at least double this estimate over time. These estimates do not take into account the effect that increased recycling of used nuclear fuel would have on global supplies. The Massachusetts Institute of Technology (MIT) recently confirmed that uranium supplies will not limit the expansion of nuclear energy in the U.S. in its 2010 study “The Future of the Nuclear Fuel Cycle.”

## 1AR Microgrid CP

#### More ev—DOD study

S.B. Van Broekhoven et al june ‘12 N. Judson S.V.T. Nguyen W.D. Ross, “Microgrid Study:

Energy Security for DoD Installations,” AM

Cyber security concerns are a significant detriment to microgrid development. The DoD should

develop/certify a set of DIACAP-approved devices that can be used across the services for energy

management systems.

#### That outweighs everything

Wilhusen and Trimble 12

(Statement of Gregory C. Wilshusen, Director Information Security Issues David C. Trimble, Director Natural Resources and Environment, “Challenges in Securing the Modernized Electricity Grid” February 28, 2012, GAO Testimony Before the Subcommittee on Oversight and Investigations, Committee on Energy and Commerce, House of Representatives, GAO-12-507T)

The threats to systems supporting critical infrastructures are evolving and growing. In a February 2011 testimony, the Director of National Intelligence noted that there had been a dramatic increase in cyber activity targeting U.S. computers and systems in the previous year, including a more than tripling of the volume of malicious software since 2009. Varying types of threats from numerous sources can adversely affect computers, software, networks, organizations, entire industries, and the Internet itself. These include both unintentional and intentional threats, and may come in the form of targeted or untargeted attacks from criminal groups, hackers, disgruntled employees, hostile nations, or terrorists. The interconnectivity between information systems, the Internet, and other infrastructures can amplify the impact of these threats, potentially affecting the operations of critical infrastructures, the security of sensitive information, and the flow of commerce. Moreover, the smart grid’s reliance on IT systems and networks exposes the electric grid to potential and known cybersecurity vulnerabilities, which could be exploited by attackers.

#### This is the key solvency deficit question

Bodenheimer 12

(David, partner in the law firm of Crowell & Moring LLP in the DC office where he heads the Homeland Security Practice and specializes in Government Contracts, False Claims Act, Privacy, and Cybersecurity, “Cyberwarfare in the Stuxnet Age Can Cannonball Law Keep Pace With the Digital Battlefield?” Winter 2012, The SciTech Lawyer, Volume 8, Number 3)

Now that cyberweapons have been field-tested, virtually no one expects Stuxnet to be the last attack. As Dr. Lewis testified, “[c]yber attack will be like the airplane—within a few years, no self respecting military will be without this capability.”25 Major US adversaries are developing the capacity for cyberattacks on critical infrastructure: One is the threat of cyber attack. Many nation states, like Russia, China, North Korea, and Iran, have offensive cyber attack capabilities, while terrorist groups like Hezbolla and al Qaeda continue to work to develop capabilities to attack and destroy critical infrastructure like the electric grid through cyber attacks.26 Indeed, some US offcials have predicted that major cyberattacks are “nearly a certainty,” given “the promised retaliation against the U.S. for the Stuxnet work that destroyed Iranian nuclear centrifuges.”27 The distributed denial of service (DDOS) attacks on Estonia and Georgia during disputes with Russia and the coordinated hacking attacks on Google to access accounts of Chinese dissidents provide realworld examples that the age of cyberwar has already arrived. Given this new reality, the private sector needs to gear up for the risks that come with a cyberwar world.

## No Aliens – General

#### Scientific consensus is on our side – no intelligent life beyond earth

Financial Times in ‘00

(Clive Cookson and Victoria Griffith, “Our Odyssey ends here: Man’s quest for self-discovery is at a dead-end with the acceptance that we are alone in space”, December 30, L/N)

Yet, since the film was first shown in 1968, scientific opinion has gradually shifted away from the belief in smart aliens. Where science moves, the public usually follows.

This may seem an odd statement, considering the number of recent media reports about extraterrestrial life. Signs of water on Mars and Europa, a moon of Jupiter, have encouraged speculation about alien creatures.

Yet the type of life astronomers talk about these days is "dumb", not intelligent. The great hope of Nasa's Mars missions is to find evidence of microbes, living or dead. Martian bacteria would certainly be an important find, but they are a big step down from the little green men of earthlings' imagination.

Even veterans of SETI, as the Search for Extraterrestrial Intelligence is known, are beginning to sound more sceptical. Frank Drake, chairman of the SETI Institute in California, has dreamt of discovering life on other planets for 40 years. Every day, he and his colleagues attempt to pick up radio signals from other planets. Every day, they go home empty-handed.

"There may be no complex organisms out there," says Drake. "The chances of tool-bearing organisms who could send out a signal are even more remote. There is intelligent life in the oceans, for example, but the whales and dolphins wouldn't be able to communicate with another planet."

Astronomers' growing scepticism about intelligent life on other planets is fuelled partly by changes in thinking about Darwin's theory of evolution. Kubrick dedicates the first quarter of 2001 to a segment called "The Dawn of Man". The movie explores the notion that alien intervention 4m years ago transformed apes from vegetarian victims into tool-bearing carnivores, kick-starting their evolution into human beings.

While the film's notion of evolutionary "progress" is vague, Kubrick's Dawn of Man sequence reflects the famous Darwinian idea that apes gradually became more upright and more intelligent until they turned into modern homo sapiens. This view allows humans to see themselves at the pinnacle of the evolutionary tree - so far. Who knows what kind of superior beings may lie on the evolutionary path ahead?

Just a few years after the movie's debut, however, a new twist on Darwinism radically altered this view. In 1972 palaeontologist Stephen Jay Gould and his colleague Niles Eldredge developed the theory of "punctuated equilibria", according to which the most important evolutionary changes are not a gradual progression but radical and swift.

Research in geology and palaeontology since then has emphasised the random nature of such biological shifts. Species are formed not by the movement to greatness but by a series of "accidents". If the evolutionary tape were to be rewound a thousand times, nothing like human beings would appear again.

Had the dinosaurs not been wiped out by a cataclysmic event, mammals would have been a mere footnote in the evolutionary bible. And if human beings are merely an "accident" - a small twig on the evolutionary tree, as Gould likes to say - then the likelihood that creatures like ourselves would exist on other planets seems very remote indeed.

At the same time, some astronomers say the conditions in which intelligent life evolved on Earth are extra-ordinary enough to make it likely that we are alone in our galaxy, if not in the universe.

In their influential book Rare Earth (Springer, Pounds 17), Peter Ward and Donald Brownlee of the University of Washington list the factors that make Earth so special: Its distance from the sun has ensured the existence of liquid water for 3.5bn years. It has the right mass to retain atmosphere and oceans. Plate tectonics built land masses. Jupiter, its giant neighbour, has protected Earth from too many life-extinguishing collisions with asteroids and comets, while allowing a few to punctuate the evolutionary equili-brium. Its orbit around the sun is stable. There is enough carbon to support life but not to allow runaway greenhouse heating. Radiation levels promote genetic change without causing lethal damage.

## AT: Space Disease

No contamination risks: differences in lifeforms guarantee that we can’t catch ET diseases

Robert Zubrin, President of the Mars Society, founder and CEO of Pioneer Astronautics, March April 2001 http://www.planetary.org/html/news/opinions/zubrinresponse.html

But couldn't such life, if somehow unearthed by astronauts, be harmful? Absolutely not. Why? Because disease organisms are keyed to their hosts. Like all other organisms, they are specially adapted to life in a particular environment. In the case of human disease organisms, this environment is the interior of the human body or of a closely related species, such as another mammal. For almost 4 billion years, the pathogens that afflict humans today have waged a continuous biological arms race with the defenses developed by our ancestors. An organism that has not evolved to breach our defenses and survive in the microcosmic free-fire zone that constitutes our interiors will have no chance of successfully attacking us. This is why humans do not catch Dutch elm disease and trees do not catch colds. Any indigenous Martian host organism would be far more distantly related to humans than are elm trees.

There is no evidence for the existence of (and every reason to believe the impossibility of) macroscopic Martian fauna and flora. Without indigenous hosts, the existence of Martian pathogens is impossible. And if there were hosts, the huge differences between them and terrestrial species would make the idea of common diseases an absurdity.

Equally absurd is the idea of independent Martian microbes coming to Earth and competing with terrestrial microorganisms in the open environment. Microorganisms are adapted to specific environments. The notion of Martian organisms out-competing terrestrial species on their home ground (or terrestrial species overwhelming Martian microbes on Mars) is as silly as the idea that sharks transported to the plains of Africa would replace lions as the local ecosystem's leading predator.

## 1AR AT Weaponization

#### Weaponization now

Sirota, 12

(1/23, Salon Columnist & Author of "Back to Our Future: How the 1980s Explain the World We Live In Now." Co-host of political commentary show ‘The Rundown; with Sirota & Brown, “Space: The next war zone?,” http://www.salon.com/2012/01/23/space_the_next_war_zone/singleton/

It started on January 12th, when the Obama administration negged an international agreement aimed at both reducing dangerous space debris and keeping space as demilitarized as possible. As Canada’s National Post noted, the White House rejected the covenant specifically “because it impinged on the (U.S.) military’s use of space.” A few days after the rejection, Secretary of State Hillary Clinton issued a formal statement declaring that the United States “will not enter into a code of conduct that in any way constrains our national security-related activities in space.” With neoconservatives promoting superheated claims that space demilitarization will harm America’s national security, the administration’s declaration looks politically timed, especially considering that, according to the New York Times in 2010, the White House previously promised to “renounce the unilateral stance of the Bush administration and instead emphasize international cooperation (in space), including the possibility of an arms control treaty that would limit the development of space weapons.” In one sense, this is nothing new. After all, the United States government has long been trying to militarize space. As far back as 1958, for example, Time magazine reported that Lt. General Donald L. Putt told the House Armed Services Committee of the Air Force’s “plans to become the U.S. Space Force and eventually occupy the moon.” A year later, NASA scientists were hard at work on a “Project Horizon” plan that the agency says was aiming to place “a military colony on the moon.” Then, of course, came Ronald Reagan’s Strategic Defense Initiative (“Star Wars”), which ultimately translated into an ever-growing Pentagon budget for space operations. But in another sense, the very public nature of the Obama administration’s space decrees this month represents something monumental: a proud reiteration that despite the budgetary, diplomatic and human consequences of U.S. military aggression in the last decade, America still has both no plans to change its imperial posture, and many plans to carry that posture into the few frontiers still left unconquered. In practice, that means a stealth effort to dominate the Arctic, a brazen attempt to control the Internet, and yes, the ongoing attempt to dominate space for military purposes. All of that may seem like fodder for the fantastical plots of bad sci-fi films, but unfortunately, it’s all too real and all too consequential. Indeed, as military powers like China already start to follow our saber-rattling example, the U.S. government’s posture is today setting the stage for major hegemonic fights for these frontiers, with space the biggest potential battleground of all. No doubt, if and how those conflicts develop will determine whether or not our tomorrow is as dark as sci-fi so often imagines.

#### US already publicly moving to weaponize space—budgets prove

Pincus, 12

(3/26, W-Post Columnist, “Hearings show our dependence on military space technology”

http://www.washingtonpost.com/world/national-security/hearings-show-our-dependence-on-military-space-technology/2012/03/24/gIQANVV8cS_story.html)

The United States may be falling behind in transportation, education and health care down here on Earth, but its military infrastructure is certainly way ahead when it comes to imagery and communications satellites armed with defensive and offensive capabilities out there in space. That the United States leads in the militarization of space is apparent from House and Senate Armed Services subcommittee hearings this month on the fiscal 2013 budget of $9.7 billion for military space programs.